Business Practices for Open Access Same-Time Information Systems (OASIS) Standards & Communication Protocols

Business Practices Requirements:

002-1	INTRODUCTION

002-1.1	DEFINITION OF TERMS

The following definitions are offered to clarify discussions of the OASIS in this document.

a. Transmission Services Information (TS Information) is transmission and ancillary services information that must be made available by public utilities on a non-discriminatory basis to meet the regulatory requirements of transmission open access.

b. Open Access Same-Time Information System (OASIS) comprises the computer systems and associated communications facilities that public utilities are required to provide for the purpose of making available to all transmission users comparable interactions with TS Information.

c. Open Access Same-Time Information System Node (OASIS Node) is a subsystem of the OASIS. It is one computer system in the (OASIS) that provides access to TS Information to a Transmission Customer.

d. Transmission Provider (TP or Primary Provider) is the public utility (or its designated agent)

that owns, operates or controls facilities used for the transmission of electric energy in interstate commerce. (This is the same term as is used in Part 35.3).

e. Transmission Customer (TC or Customer) is any eligible Customer (or its designated agent) that can or does execute a transmission service agreement or can or does receive transmission service. (This is the same term as is used in Part 35.3).

f. Secondary Transmission Provider (ST, Reseller, or Secondary Provider) is any Customer who offers to sell transmission capacity it has purchased. (This is the same as Reseller in Part 37).

g. Transmission Services Information Provider (TSIP) is a Transmission Provider or an agent to whom the Transmission Provider has delegated the responsibility of meeting any of the requirements of Part 37. (This is the same as Responsible Party in Part 37).

h. Value-Added Transmission Services Information Provider (VTSIP) is an entity who uses TS Information in the same manner as a Customer and provides value-added information services to its Customers.

002-2	NETWORK ARCHITECTURE REQUIREMENTS

002-2.1	ARCHITECTURE OF OASIS NODES

a. Permit Use of Any OASIS Node Computers: TSIPs shall be permitted to use any computer systems as an OASIS Node, so long as they meet the OASIS requirements.

b. Permit Use of Any Customer Computers: OASIS Nodes shall permit the use by Customers of any commonly available computer systems, as long as they support the required communication links to the Internet.

c. Permit the Offering of Value-Added Services: TSIPs are required, upon request, to provide their Customers the use of private network connections on a cost recovery basis. Additional services that are beyond the scope of the minimum OASIS requirements are also permitted. When provided, these private connections and additional services shall be offered on a fair and non-discriminatory basis to all Customers who might choose to use these services.

d. Permit Use of Existing Communications Facilities: In implementing the OASIS, the use of existing communications facilities shall be permitted. The use of OASIS communication facilities for the exchange of information beyond that required for open transmission access (e.g., transfer of system security or operations data between regional control centers) shall also be permitted, provided that such use does not negatively impact the exchange of open transmission access data and is consistent with the Standards of Conduct in Part 37.

e. Single or Multiple Providers per Node: An OASIS Node may support a single individual Primary Provider (plus any Secondary Providers) or may support many Primary Providers.

002-2.2	INTERNET-BASED OASIS NETWORK

a. Internet Compatibility: All OASIS Nodes shall support the use of internet tools, internet directory services, and internet communication protocols necessary to support the Information Access requirements stated in Section 4.

b. Connection through the Public Internet: Connection of OASIS Nodes to the public Internet is required so that Users may access them through Internet links. This connection shall be made through a firewall to improve security.

c. Connection to a Private Internet Network: OASIS Nodes shall support private connections to any OASIS User (User) who requests such a connection. The TSIP is permitted to charge the User, based on cost, for these connections. The same internet tools shall be required for these private networks as are required for the public Internet. Private connections must be provided to all users on a fair and nondiscriminatory basis.

d. Internet Communications Channel: The OASIS Nodes shall utilize a communication channel to the Internet which is adequate to support the performance requirements given the number of Users subscribed to the Providers on the Node (see Section 5.3).

002-2.3	COMMUNICATION STANDARDS REQUIRED

a. Point-to-Point Protocol (PPP) and Internet Protocol Control Protocol (IPCP) (reference RFCs 1331 and 1332) shall be supported for private internet network dial-up connections.

b. Serial Line Internet Protocol (SLIP) (reference RFC 1055) shall be supported for private internet network dial-up connections.

c. Transport Control Protocol and Internet Protocol (TCP/IP) shall be the only protocol set used between OASIS Nodes whenever they are directly interconnected, or between OASIS Nodes and Users using private leased line internet network connections.

d. Hyper Text Transport Protocol (HTTP), Version 1.0 (RFC 1945), shall be supported by TSIPs so that Users= web browsers can use it to select information for viewing displays and for downloading and uploading files electronically.

e. Internet Protocol Address: All OASIS Nodes are required to use an IP address registered with the Internet Network Information Center (InterNIC), even if private connections are used.

002-2.4	INTERNET TOOL REQUIREMENTS

Support for the following specific internet tools is required, both for use over the public Internet as well as for any private connections between Users and OASIS Nodes:

a. Browser Support: OASIS Nodes shall insure that Users running minimally either Netscape's Navigator version 4.0.x or Microsoft's Internet Explorer version 4.0.x browsers (or any other commercially or privately available browser supporting that set of capabilities common to both of these industry standard browsers) shall have a fully functional user interface based on the Interface Requirements defined in Section 4.

b. HTML Forms shall be provided by the TSIPs to allow Customers to enter information to the OASIS Node.

c. Domain Name Service (DNS) (ref. RFC 1034, 1035) shall be provided as a minimum by the TSIPs (or their Internet Service Provider) for the resolution of IP addresses to allow Users to navigate easily between OASIS Nodes.

d. Simple Network Management Protocol (SNMP) is recommended but not required to provide tools for operating and managing the network, if private interconnections between OASIS Nodes are established.

e. The Primary Provider shall support E-mail for exchanges with Customers, including the sending of attachments. The protocols supported shall include, as a minimum, the Simple Messaging Transfer Protocol (SMTP), Post Office Protocol (POP), and Multipurpose Internet Mail Extensions (MIME).

002-2.5	NAVIGATION AND INTERCONNECTIVITY BETWEEN OASIS NODES

a. World Wide Web Browsers: TSIPs shall permit Users to navigate using WWW browsers for accessing different sets of TS Information from one Provider, or for getting to TS Information from different Providers on the same OASIS Node. These navigation methods shall not favor User access to any Provider over another Provider, including Secondary Providers.

b. Internet Interconnection across OASIS Nodes: Navigation tools shall not only support navigation within the TSIP's Node, but also across interconnected OASIS Nodes. This navigation capability across interconnected Nodes shall, as a minimum, be possible through the public Internet.

002-3	INFORMATION ACCESS REQUIREMENTS

002-3.1	REGISTRATION AND LOGIN REQUIREMENTS

a. Location of Providers: To provide Users with the information necessary to access the desired Provider, all Primary Providers shall register their OASIS Node URL address with www.tsin.com. This URL address should include the unique four letter acronym the Primary Provider will use as the PRIMARY_PROVIDER_CODE.

b. Initial User Registration: TSIPs shall require Users to register with a Primary Provider before they are permitted to access the Provider's TS Information. There must be a reference pointing to registration procedures on each Primary Provider's home page. Registration procedures may vary with the administrative requirements of each Primary Provider.

c. Initial Access Privileges: Initial registration shall permit a User only the minimum Access Privileges. A User and a Primary Provider shall mutually determine what access privilege the User is permitted. The TSIP shall set a User's Access Privilege as authorized by the Primary Provider.

d. User Login: After registration, Users shall be required to login every time they establish a dial-up connection. If a direct, permanent connection has been established, Users shall be required to login initially or any time the connection is lost. Use of alternative forms of login and authentication using certificates and public key standards is acceptable.

e. User Logout: Users shall be automatically logged out any time they are disconnected. Users may logout voluntarily.

002-3.2	SERVICE LEVEL AGREEMENTS

Service Level Agreements: It is recognized that Users will have different requirements for frequency of access, performance, etc., based on their unique business needs. To accommodate these differing requirements, TSIPs shall be required to establish a "Service Level Agreement" with each User, which specifies the terms and conditions for access to the information posted by the Providers. The default Service Level Agreement shall be Internet access with the OASIS Node meeting all minimum performance requirements.

002-3.3	ACCESS TO INFORMATION

a. Display: TSIPs shall format all TS Information in HTML format such that it may be viewed and read directly by Users without requiring them to download it. This information shall be in clear English as much as possible, with the definitions of any mnemonics or abbreviations available on-line. The minimum information that is to be displayed is provided in the Templates in Section 4.3.

b. Read-Only Access to TS Information: For security reasons, Users shall have read-only access to the TS Information. They shall not be permitted to enter any information except where explicitly allowed, such as HTML transaction request forms or by the Templates in Section 4.3.

c. Downloading Capability: Users shall be able to download from an OASIS Node the TS Information in electronic format as a file. The rules for formatting of this data are described in Section 4.2.

d. On-Line Data Entry on Forms: Customers shall be permitted to fill out on-line the HTML forms supplied by the TSIPs, for requesting the purchase of services and for posting of products for sale (by Customers who are Resellers). Customers shall also be permitted to fill-out and post Want- Ads.

e. Uploading Capability: Customers shall be able to upload to OASIS Nodes the filled-out forms. TSIPs shall ensure that these uploaded forms are handled identically to forms filled out on-line. TSIPs shall provide forms that support the HTTP input of Comma Separated Variable (CSV) records. This capability shall permit a Customer to upload CSV records using standard Web browsers or additional client software (such as fetch_http) to specify the location of the CSV records stored on the Customer's hard disk.

f. Selection of TS Information: Users shall be able to dynamically select the TS Information they want to view and/or download. This selection shall be, as a minimum, through navigation to text displays, the use of pull-down menus to select information for display, data entry into forms for initiating queries, and the selection of files to download via menus.

002-3.4	PROVIDER UPDATING REQUIREMENTS

The following are the Provider update requirements:

a. Provider Posting of TS Information: Each Provider (including Secondary Providers and Value-Added Providers) shall be responsible for writing (posting) and updating TS Information on their OASIS Node. No User shall be permitted to modify a Provider's Information.

b. General Postings

(i)  INFO.HTM: Each Provider shall provide general information on how to use their node and describe all special aspects, such as line losses, congestion charges and assistance. The address for the directory of this information shall be INFO.HTM (case sensitive), an HTML web page, linked to the Provider's registered URL address. See section 4.5 for information required to be on the web page INFO.HTM.

(ii)  Standards of Conduct:  The Transmission Provider shall establish a link entitled “Standards of Conduct,” located on the OASIS home page at the Transmission Provider’s registered URL address.

c. OASIS Node Space for Secondary Provider: To permit Users to readily find TS Information for the transmission systems that they are interested in, TSIPs shall provide database space on their OASIS Node for all Secondary Providers who have purchased, and who request to resell, transmission access rights for the power systems of the Primary Providers supported by that Node.

d. Secondary Provider Posting to Primary Provider Node: The Secondary Providers shall post the relevant TS Information on the OASIS Node associated with each Primary Provider from whom the transmission access rights were originally purchased.

e. Secondary Provider Posting Capabilities: The TSIPs shall ensure that the Secondary Providers shall be able to post their TS Information to the appropriate OASIS Nodes using the same tools and capabilities as the Customers, meet the same performance criteria as the Primary Providers, and allow users to view these postings on the same display page, using the same tables, as similar capacity being sold by the Primary Providers.

f. Free-Form Posting of non-TS Information: The TSIP shall ensure that Providers and Customers may post non-TS Information, such as Want-Ads and that this information is easily accessible by all Users. The TSIP shall be allowed to limit the volume and/or to charge for the posting of non-TS Information.

g. Time Stamps: All TS Information shall be associated with a time stamp to show when it was posted to the OASIS Node.

h. Transaction Tracking by an Assignment Reference Number: All requests for purchase of transmission or ancillary services will be marked by a unique accounting number, called an assignment reference.

i. Time-Stamped OASIS Audit Log: All posting of TS Information, all updating of TS Information, all User logins and disconnects, all User download requests, all Service Requests, and all other transactions shall be time stamped and stored in an OASIS Audit Log. This OASIS Audit Log shall be the official record of interactions, and shall be maintained on-line for download for at least 90 days. Changes in the values of posted Capacity (Available Transfer Capability) must be stored in the on-line Audit Log for 20 days. Audit records must be maintained for 3 years off-line and available in electronic form within seven days of a Customer request.

j. Studies: A summary description with dates, and programs used of all transmission studies used to prepare data for the Primary Provider's ATC and TTC calculation will be provided along with information as to how to obtain the study data and results.

002-3.5	ACCESS TO CHANGED INFORMATION

a. General Message & Log: TSIPs shall post a general message and log that may be read by Users. The message shall state that the Provider has updated some information, and shall contain (or point to) a reverse chronological log of those changes. This log may be the same as the Audit Log. The User may use the manual capability to see the message.

b. TSIP Notification Design Responsibilities: The TSIP shall avoid a design that could cause serious performance problems by necessitating frequent requests for information from many Users.

002-3.6	USER INTERACTION WITH AN OASIS NODE

There are three basic types of User interactions which must be supported by the OASIS Node. These interactions are defined in Section 4.3.

a. Query/Response: The simplest level of interactions is the query of posted information and the corresponding response. The User may determine the scope of the information queried by specifying values, through an HTML form, a URL string, or an uploaded file, using Query Variables and their associated input values as defined with each Template in Section 4.3. The response will be either an HTML display or a record oriented file, depending on the output format that the User requests. The TSIP may establish procedures to restrict the size of the response, if an overly broad query could result in a response that degrades the overall performance of the OASIS Node for their Users.

b. Purchase Request: The second type of Customer interaction is the submittal of a request to purchase a service. The Customer completes an input form, a URL string or uploads a file and submits it to the OASIS Node. The uploaded file can either be a series of Query Variables or a record oriented file.  The Seller of the service, possibly off-line from the OASIS Node, processes the request and the status is updated accordingly. If the Seller approves the purchase request, then the Cusomer must again confirmed it. Once the Customer confirms an approved purchase, a reservation for those services is considered to exist, unless later the reservation is reassigned, displaced, or annulled.

c. Upload and Modify Postings: Customers who wish to resell their rights may upload a form, create the appropriate URL or upload a file to post services for sale. A similar process applies to eligible Third Party Sellers of ancillary services. The products are posted by the TSIP. The seller may monitor the status of the services by requesting status information. Similarly the Seller may modify its posted transmission services by submitting a service modification request through a form, a URL query, or by uploading a file.

002-4	INTERFACE REQUIREMENTS

002-4.1	INFORMATION MODEL CONCEPTS

a. ASCII-Based OASIS Templates: For providing information to Users, TSIPs shall use the specified OASIS Templates. These Templates define the information that must be presented to Users, both in the form of graphical displays and as downloaded files. Users shall be able to request Template information using query-response data flows. The OASIS Templates are described in section 4.3. The Data Element Dictionary, which defines the Data Elements in the OASIS Templates, is provided in Appendix A. Data elements must be used in the exact sequence and number as shown in the Templates when file uploads and downloads are used. Although the contents of the graphical displays are precisely defined as the same information as in the Templates, the actual graphical display formats of the TS information are beyond the scope of the OASIS requirements. Due to the nature of graphical displays, there may be more than one graphical display used to convey the information in a single Template.

b. ASCII-Based OASIS File Structures: For uploading requests from and downloading information to Users, TSIPs shall use specific file structures that are defined for OASIS Template information (see section 4.2). These file structures are based on the use of headers that contain the Query Variable information, including the name of the OASIS Template. These headers thus determine the contents and the format of the data that follows. Although headers may not be essential if file transfers contain the exact sequence and number of Data Elements as the Templates, this feature is being preserved for possible future use when additional flexibility may be allowed.

002-4.2	OASIS NODE CONVENTIONS AND STRUCTURES

002-4.2.1	OASIS Node Naming Requirements

The following naming conventions shall be used to locate information posted on an OASIS Node. OASIS naming conventions shall conform to standard URL structures.

002-4.2.1.1	OASIS Node Names

In order to provide a consistent method for locating an OASIS Node, the standard Internet naming convention shall be used. All OASIS Node names shall be unique. Each Primary Provider OASIS Node name and home directory shall be registered with the master OASIS directory site at http://www.tsin.com. OASIS Node names shall be stored in an Internet DNS name directory.

002-4.2.1.2	OASIS Node and Primary Provider Home Directory

The home directory name on an OASIS Node shall be "OASIS" (all upper case) to identify that the directory is related to the OASIS. The directory of each Primary Provider shall be listed under the "OASIS" directory:

http://(OASIS Node name)/OASIS/(PRIMARY_PROVIDER_CODE)

Where:

(OASIS Node name) is the World Wide Web URL address of the OASIS Information Provider.

(PRIMARY_PROVIDER_CODE) (Case sensitive) is the 4-character acronym of the primary provider.

PRIMARY_PROVIDER_CODEs shall be registered with the master OASIS directory site at http://www.tsin.com. A pointer to user registration information shall be located on the Primary Provider's home page.

002-4.2.1.3	Script Names

Common Gateway Interface (CGI) scripts shall be located in the directory "data" as follows (case sensitive): http://(OASIS Node name)/OASIS/ (PRIMARY_PROVIDER_CODE) /data/(cgi script name)?(Query Variables)

Where:

(cgi script name) is the OASIS Template name in lower case (see Section 4.3). Other cgi scripts may be defined as required to implement the HTML interface to the documented Templates.

(Query Variables) is a list of query variables with their settings formatted as defined by the HTTP protocol (i.e., URL encoded separated by ampersands).

Example:

To request the hourly schedule Template at Primary Provider WXYZ Co.

http://www.wxyz.com/OASIS/WXYZ/data/schedule ?templ=schedule& ver=1.2& fmt=data &stime=19960412040000PD &sptime=19960412100000PD& pprov=wxyz

002-4.2.2	Data Element Dictionary

The following are the requirements for the Data Element Dictionary:

a. Definition of OASIS Information Elements: All OASIS Information Data Elements shall be defined in the Data Element Dictionary which will be stored in the OASIS Node directory:

- http://(OASISNode Name)/OASIS/(PRIMARY_PROVIDER_CODE)/ (datadic.htm | datadic.txt)

- Where:

- datadic.htm is the HTML version of the Data Element dictionary (case sensitive)

- datadic.txt is the ASCII text version of the Data Element dictionary (case sensitive)

- The Data Element Dictionary is defined in Appendix A.

b. Provider-specific Data Element Values: The valid values that certain OASIS Information Data Elements may take on, such as PATH_NAME, etc., are unique to a Primary Provider. Names that must be uniquely identified by Primary Provider shall be listed on-line on the OASIS Node via the LIST Template (see Section 4.3.5). In posting OASIS information associated with Data Elements which are not free-form text, TSIPs shall use only the accepted Data Element values listed in the Data Element Dictionary and/or those values posted in the LIST of provider specific names provided on the OASIS Node.

002-4.2.3	OASIS Template Constructs

002-4.2.3.1	Template Construction

Section 4.3 lists the set of OASIS Templates that shall be supported by all OASIS Nodes. These OASIS Templates are intended to be used precisely as shown for the transfer of data to/from OASIS Nodes, and identify, by Data Elements names, the information to be transferred. The construction of the OASIS Templates shall follow the rules described below:

a. Unique OASIS Template Name: Each type of OASIS Template shall be identified with a unique name which shall be displayed to the User whenever the OASIS Template is accessed.

b. Transfer Protocol: OASIS Templates are transferred using the HTTP protocol. Templates shall support both the "GET" and "POST" methods for transferring "query string" name/value pairs, as well as the OASIS specific "comma separated value" (CSV) format for posting and retrieval of information from OASIS Nodes. HTML screens and forms shall be implemented for each OASIS Template.

c. Source Information: Each OASIS Template shall identify the source of its information by including or linking to the name of the Primary Provider, the Secondary Provider, or the Customer who provided the information.

d. Time Of Last Update: Each OASIS Template shall include a time indicating when it was created or whenever the value of any Data Element was changed.

e. Data Elements: OASIS Templates shall define the elementary Data Element Dictionary names for the data values to be transferred or displayed for that Template.

f. Documentation: OASIS Information shall be in non-cryptic English, with all mnemonics defined in the Data Element Dictionary or a glossary of terms. TSIPs shall provide on-line descriptions and help screens to assist Users understanding the displayed information. Documentation of all formats, contents, and mnemonics shall be available both as displays and as files that can be downloaded electronically. In order to meet the "User-Friendly" goal and permit the flexibility of the OASIS Nodes to expand to meet new requirements, the OASIS Templates shall be as self-descriptive as possible.

002-4.2.3.2	Template Categories

OASIS Templates are grouped into the following two major categories:

a. Query/Response: These Templates are used to query and display information posted on an OASIS Node. Each query/response Template accepts a set of user specified Query Variables and returns the appropriate information from data posted on the OASIS Node based on those Query Variables. The valid Query Variables and information to be returned in response are identified by Data Element in Section 4.3.

b. Input/Response: These Templates are used to upload/input information on an OASIS Node. The required input information and information to be returned in response are identified by Data Element in Section 4.3, Template Descriptions.

002-4.2.3.3	Template HTML Screens

Though the exact form and content of the HTML screens and forms associated with the OASIS Templates are not dictated by this document, the following guidelines shall be adhered to for all HTML screens and forms implemented on an OASIS Node:

a. Data Element Headings: Data displayed in an HTML screen/form shall be labeled such that the associated data value(s) is(are) easily and readily identifiable as being associated with a particular OASIS Template Data Element. HTML "Hot-Links" or other pointer mechanisms may be provided for Data Element headings in OASIS Templates which permit the User to access documentation describing the meaning, type, and format of the associated data.

b. Display Limitations: HTML screens and forms shall be implemented in such a way to allow the display of all data specified for each OASIS Template. This may take the form of "wrapping" of lines of information on the screen, the use of horizontal and/or vertical scrolling, or the use of "Hot-Links" or other pointer mechanisms. There is not necessarily a one-to-one relationship between HTML screens implemented on OASIS Nodes, and their associated Template. However, all Template Data Elements shall be viewable through one or more HTML screens.

c. Template Navigation: HTML "Hot-Links" or other pointer mechanisms may be provided to assist the navigation between screens/forms associated with related OASIS Templates.

002-4.2.4	Query/Response Template Requirements

Retrieval of information posted on an OASIS Node is supported by the Query/Response Templates. The "query" identifies the OASIS Template and optionally supplies additional Data Elements that may be used to select specific information to be returned in the "response".

002-4.2.4.1	Query Requirements

Query information is transferred to an OASIS Node using the HTTP protocol as a string of Query Variables in the form of name/value pairs. Query Variable name/value pairs are specified as a collection of encoded strings (e.g., blank characters replaced by plus (+) character, etc.) in the form of name=value, with each name/value pair separated by ampersands (&) (see section 4.2.6). OASIS Nodes shall support the following methods for Users to input Query information:

a. HTML: HTML FORM input and/or hypertext links shall be provided to allow Users to specify OASIS Template Query Variables. This will be the easiest way to obtain information and should be the choice of most casual Users and for simple requests. The exact nature and form of these HTML screens are not specified, and may differ between OASIS Nodes.

b. GET Method: The HTTP GET method for specifying query information appended to a standard OASIS URL shall be supported. Using this method, the name=value formatted Query Variables preceded by a question mark (?) are appended to the URL. Each "name" in a name/value pair corresponds to a Data Element name associated with that Template. OASIS Nodes shall support the specification of all Data Elements associated with a Template by both their full name and alias as defined in the Data Dictionary. The "value" in a name/value pair represents the value to be associated with the Data Element being specified in the appropriate format as defined in the Data Dictionary and encoded according to the HTTP protocol.

c. POST Method: The HTTP POST method for specifying query information in the message body shall be supported. Using this method, the name=value formatted Query Variables shall be transferred to an OASIS Node using the "Content-length:" HTTP header to define the length in bytes of the encoded query string and the "Content-type: application/x-www-form-urlencoded" HTTP header to identify the data type included in the message body. Each "name" in a name/value pair corresponds to a Data Element name associated with that Template. An OASIS Node shall support the specification of all Data Elements associated with a Template by both their full name and alias as defined in the Data Dictionary. The "value" in a name/value pair represents the value to be associated with the Data Element being specified in the appropriate format as defined in the Data Dictionary and encoded according to the HTTP protocol.

User queries using any of the above methods are supported directly by the User's web browser software. More sophisticated data transfer mechanisms, such as the automated querying of information based on Query Variable strings contained in a User data file (i.e., "uploading a file containing a URL string), require appropriate software (e.g., "fetch_http") running on the User's computer system to effect the data transfer.

002-4.2.4.2	Response Requirements

In response to a validly formatted Query for each Query/Response OASIS Template, the OASIS Node shall return the requested information in one of two forms based on the User specified OUTPUT_FORMAT Query Variable:

a. HTML: If the User requests the response to have the format of "HTML" (OUTPUT_FORMAT=HTML) then the response from the OASIS Node shall be a web page using the HTML format. This shall be the default for all Query/Response Templates.

b. CSV Format: Comma Separated Value (CSV) format (OUTPUT_FORMAT=DATA) returns the requested information in the body of the HTTP response message. The "Content-length:" HTTP header shall define the length in bytes of the response, and the "Content-type: text/x-oasis-csv" HTTP header shall be used to identify the data type included in the message body (see CSV File Format).

002-4.2.5	Input/Response Template Requirements

Input/Response Templates support the posting of information on an OASIS Node, including reservations for transmission/ancillary service and services for sale on the secondary market, etc. The "input" identifies the required data associated with an OASIS Template to be posted on the OASIS Node, and the "response" specifies the information returned to the User.

002-4.2.5.1	Input Requirements

Input information is transferred to an OASIS Node using the HTTP protocol as either a string of Query Variables in the form of name/value pairs, or as a Comma Separated Value (CSV) message. Query Variable name/value pairs are specified as a collection of encoded strings (e.g., blank characters replaced by plus (+) character, etc.) in the form of name=value, with each name/value pair separated by ampersands (&). CSV formatted messages are specified in the body of an HTTP message as a series of Data Records preceded by a fixed set of header records (see section 4.2.7). OASIS Nodes shall support the following methods for Users to transfer Input data:

a. HTML: HTML FORM input shall be provided to allow Users to specify the necessary Input data associated with each Input/Response OASIS Template. This may be in the form of fill in blanks, buttons, pull-down selections, etc., and may use either the GET or POST methods. The exact nature and form of these HTML screens are not specified, and may differ between OASIS Nodes.

b. GET Method: The HTTP GET method for specifying Input information in the form of a query string appended to a standard OASIS URL shall be supported. Using this method, the name=value formatted Query Variables preceded by a question mark (?) are appended to the URL. Each "name" in a name/value pair corresponds to a Data Element name associated with that Template. OASIS Nodes shall support the specification of all Data Elements associated with a Template by both their full name and alias as defined in the Data Dictionary. The "value" in a name/value pair represents the value to be associated with the Data Element being specified in the appropriate format as defined in the Data Dictionary and encoded according to the HTTP protocol.

c. POST Method: The HTTP POST method for specifying Input information in the form of a query string in the message body shall be supported. Using this method, the name=value formatted Query Variables shall be transferred to an OASIS Node using the "Content-length:" HTTP header to define the length in bytes of the encoded query string and the "Content-type: application/x-www-form-urlencoded" HTTP header to identify the data type included in the message body. Each "name" in a name/value pair corresponds to a Data Element name associated with that Template. OASIS Nodes shall support the specification of all Data Elements associated with a Template by both their full name and alias as defined in the Data Dictionary. The "value" in a name/value pair represents the value to be associated with the Data Element being specified in the appropriate format as defined in the Data Dictionary and encoded according to the HTTP protocol.

d. CSV Format: Comma Separated Value (CSV) formatted Input information transferred in the body of a User's HTTP message shall be supported. The "Content-length:" HTTP header shall define the length in bytes of the Input, and the "Content-type: text/x-oasis-csv" HTTP header shall be used to identify the data type included in the message body.

002-4.2.5.2	Response to Input

In response to a validly formatted Input for each Input/Response OASIS Template, the OASIS Node shall return an indication as to the success/failure of the requested action. The OASIS Node shall respond to the Input in one of two forms, based on the OUTPUT_FORMAT, which was input by a User either as a Query Variable or in a CSV format Header Record:

a. HTML: If the User requests the response to have the format of "HTML" (OUTPUT_FORMAT =HTML) then the response from the OASIS Node shall be a web page using the HTML format. This shall be the default for all Input/Response Templates invoked using either the FORM, GET or POST methods of input.

b. CSV Format: Comma Separated Value (CSV) format (OUTPUT_FORMAT=DATA) returns the response information in the body of the HTTP response message. The "Content-length:" HTTP header shall define the length in bytes of the response, and the "Content-type: text/xoasis- csv" HTTP header shall be used to identify the data type included in the message body. This shall be the default for all Input/Response Templates invoked using the CSV Format methods of input.

002-4.2.6	Query Variables

002-4.2.6.1	General

Both Query/Response and Input/Response OASIS Templates shall support the specification of a query string consisting of Query Variables formatted as name/value pairs. OASIS Nodes shall support the specification of Data Element names ("name" portion of name=value pair) in both the full name and alias forms defined in the Data Dictionary. OASIS Nodes shall support the specification of Query Variables from the User using either the HTTP GET or POST methods. On input, Data Element names and associated values shall be accepted and processed without regard to case. On output, Data Element names and associated values may not necessarily retain the input case, and could be returned in either upper or lower case.

002-4.2.6.2	Standard Header Query Variables

The following standard Query Variable Data Elements shall be supported for all OASIS Templates and must be entered for each Query by a User:

VERSION

TEMPLATE

OUTPUT_FORMAT

PRIMARY_PROVIDER_CODE

PRIMARY_PROVIDER_DUNS

RETURN_TZ

Since these header Query Variables must be supported for all Templates, they are not listed explicitly in the Template descriptions in Section 4.3 The User must enter all standard Header Query Variables with appropriate values.

002-4.2.6.3	Responses to Queries

Responses to Queries will include the following information as a minimum:

TIME_STAMP

VERSION

TEMPLATE

OUTPUT_FORMAT

PRIMARY_PROVIDER_CODE

PRIMARY_PROVIDER_DUNS

RETURN_TZ

The additional information shall include:

a. The requested information as defined by the Template indicated in the Query

b. For CSV downloads, the additional header Data Elements required (see section 4.2.7.3)

002-4.2.6.4	Multiple Instances

Certain Query Variables may be repeated in a given Query/Response OASIS Template query string. Such multiple instances are documented in the Template definitions using an asterisk (*) after the Query Variable. When more than one instance of the Query Variable is specified in the query string, OASIS Nodes shall recognize such multiple instances by either the Data Element's full name or alias suffixed with sequential numeric qualifiers starting with the number 1, (e.g., PATH_NAME1=abc&PATH_NAME2=xyz, or PATH1=abc&PATH2=xyz). At least 4 multiple instances will be permitted for each Query Variable marked with an asterisk (*).

002-4.2.6.5	Logical Operations

OASIS Nodes shall use the following logical operations when processing Query Variables for Query/Response OASIS Templates.

a. All Query Variables, with the exception of multiple instances of the same Query Variable Data Element, shall be operated on to return information based on the logical- AND of those Query Variables. For example, the query string "SELLER_CODE=abc &PATH=xyz" should return information associated with only those records that are on transmission path "xyz" AND associated with transmission provider "abc."

b. Multiple instances of the same Query Variable shall be operated on as logical-OR. For example, "SELLER_CODE=abc &PATH1=xyz&PATH2=opq" should return information associated with transmission provider "abc" AND either transmission path "xyz" OR transmission path "opq". Some logical operations may exclude all possibilities, such that the responses may not contain any data.

002-4.2.6.6	Handling of Time Data Elements

a. In cases where a single Query Variable is provided to select information associated with a single Template Data Element that represents a point in time (e.g., TIME_OF_LAST_UPDATE), OASIS Nodes shall return to the User all requested information whose associat Data Element time value (e.g. TIME_OF_LAST_UPDATE) is equal to or later than the value specified by the Query Variable. In this case the stop time is implicitly "now".

b. A pair of Query Variables (e.g. START_TIME_QUEUED and STOP_TIME_QUEUED) that represents the start and stop of a time interval but is associated with one single Template Data Element (e.g. TIME_QUEUED) shall be handled by OASIS Nodes to return to the User all requested information whose associated Data Element time value falls within the specified time interval.

c. A pair of Query Variables (e.g. START_TIME and STOP_TIME Query Variables) that represents the start and stop of one time interval but is associated with another pair of Template Data Elements (e.g. START_TIME and STOP_TIME of a service offering) that represents a second time interval, shall be handled by OASIS Nodes to return to the User all requested information whose associated Data Element time interval overlaps any portion of the specified time interval. Specifically, the START_TIME Query Variable selects all information whose STOP_TIME Data Element value is later than the START_TIME Query Variable, and the STOP_TIME Query Variable selects all information whose START_TIME Data Element value is earlier than the STOP_TIME Query Variable.   For example:

The transoffering Template query string "START_TIME 970101000000ES&STOP_TIME 970201000000ES" shall select from the OASIS database all associated offerings whose start/stop times overlap any portion of the time from 00:00 January 1, 1997, to 00:00 February 1, 1997. This would include offerings that (1) started prior to Jan. 1 and stopped any time on or after Jan. 1, and (2) started on or after Jan 1 but before Feb 1

d. For changes to and from daylight savings time, either Universal Time or the correct time and zone must be used, based on whether daylight savings time is in effect.

e. All time values shall be checked upon input to ensure their validity with respect to date, time, time zone, and daylight savings time.

002-4.2.6.7	Default Values

Query Variables that are not specified by the User may take on default values as appropriate for that Query Variable at the discretion of the OASIS TSIP.

002-4.2.6.8	Limitations on Queries

OASIS TSIP may establish validation procedures and/or default values for Query Variables to restrict the size and/or performance impact of overly broad queries.

002-4.2.7	CSV Format

002-4.2.7.1	General Record Format

OASIS Users shall be able to upload information associated with Input/Response OASIS Templates and download information associated with all OASIS Templates using a standardized Comma Separated Value (CSV) format. CSV formatted data is transferred to/from OASIS Nodes as part of the body of an HTTP message using the "Content-length:" HTTP header to define the length in bytes of the message body, and the "Content-type: text/x-oasis-csv" HTTP header to identify the data type associated with the message body. CSV formatted data consists of a fixed set of header records followed by a variable number of Data Records. Each record shall be separated by a carriage return plus line feed (denoted by the symbol ( in all examples). The fields within a record shall be delimited by commas (,). All data within a CSV formatted message shall use printable ASCII characters with no other special embedded codes, with the exception of the special encoding requirements associated with text fields.

002-4.2.7.2	Input Header Records

The following standard header records are required for the uploading of Input data for all Input/Response OASIS Templates:

VERSION=nn.n(

TEMPLATE=aaaaaaaaaa(

OUTPUT_FORMAT=[DATA] (

PRIMARY_PROVIDER_CODE=aaaa(

PRIMARY_PROVIDER_DUNS=nnnnnnnnn(

RETURN_TZ=aa(

DATA_ROWS=nnn(

COLUMN_HEADERS=[Template Data Element names separated by commas] (

The format of the value associated with each of the Input header record Data Elements are dictated by the Data Dictionary. The value associated with the DATA_ROWS Data Element shall define the total number of Data Records that follow in the message after the COLUMN_HEADERS record. The COLUMN_HEADERS record defines, by Data Element name, the data associated with each comma separated column contained in each subsequent Data Record (row). On Input, either the Data Element's full name or alias listed in the Data Dictionary may be specified.

002-4.2.7.3	Response Header Records

When explicitly specified using the OUTPUT_FORMAT=DATA Query Variable or implied by the Input of a CSV format message, the OASIS Nodes shall respond with the following standard response header records for all OASIS Templates:

REQUEST_STATUS=nnn(

ERROR_MESSAGE=aaa(

TIME_STAMP=yyyymmddhhmmsstz(

VERSION=nn.n(

TEMPLATE=aaaaaaaaaa(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=aaaa(

PRIMARY_PROVIDER_DUNS=nnnnnnnnn(

RETURN_TZ=tz(

DATA_ROWS=nnn(

COLUMN_HEADERS=[Template Data Element names separated by commas] (

The format of the value associated with each of the Response header record Data Elements are dictated by the Data Dictionary. The value associated with the DATA_ROWS Data Element shall define the total number of Data Records returned in the message following the COLUMN_HEADERS header record. The COLUMN_HEADERS record defines, by Data Element name, the data associated with each comma-separated column contained in each subsequent Data Record (row). In all OASIS Node responses, the Data Element's full name shall be listed in the COLUMN_HEADERS record. The order of the column headings shall be the same as shown in the Templates for URL uploads and downloads. For graphical displays, the Provider may define the order that the Data Element names are shown.

002-4.2.7.4	Data Records

Data Records immediately follow the standard Input or Response header records. With the exception of Data Records grouped together as a single "logical record" through the use of Continuation Records, each Data Record in a CSV formatted Input message represents a single, complete execution of the associated OASIS Template. That is, sending five CSV formatted Input messages for a given Template to the same PRIMARY_PROVIDER_CODE with a single Data Record per message shall be handled in exactly the same fashion as sending a single CSV formatted Input message for the same Template and PRIMARY_PROVIDER_CODE which contains five Data Records. Each field (column) within each Data Record defines the value to be associated with the corresponding Data Element defined in the COLUMN_HEADERS record. The number of Data Records in the message is defined by the DATA_ROWS header record. The data values associated with each column Data Element are interpreted based on the Data Element type as defined in the Data Dictionary:

a. Numeric Data Elements: All numeric Data Elements shall be represented by an ASCII string of numeric digits in base ten, plus the decimal point.

b. Text Data Elements: Alphabetic and alphanumeric Data Elements shall be represented as ASCII strings and encoded using the following rules:

- Text strings that do not contain commas (,) or double quotes (") shall be accepted both with and without being enclosed by double quotes.

- Text fields with commas (,) or double quotes (") must be enclosed with double quotes. In addition double quotes within a text field shall be indicated by two double quotes ("").

- The Data Element field length specified in Data Dictionary does not include the additional double quotes necessary to encode text data.

c. Null Data Elements: Null Data Elements shall be represented by two consecutive commas (,,) corresponding to the leading and trailing (if appropriate) Data Element comma separators. Null text strings may optionally be represented by two consecutive double quote characters within the leading and trailing comma separators (i.e., Y,"",Y).

002-4.2.7.5	Continuation Records

Continuation records shall be used to indicate that the information in multiple rows (records) is part of one logical record. Continuation records will be indicated through the use of a column header called CONTINUATION_FLAG. This column header is either the first column (if in a response to a query) or second column (if in a response to an input) in all Templates permitting continuation records. The first record shall contain an "N" in the CONTINUATION_FLAG column and each following record which is part of a continuation record shall contain a "Y" in this column, thus associating the information in that record with the information in the previous record. An "N" shall indicate that the record is not a continuation record. In addition to the CONTINUATION_FLAG Data Element identifying that a record is associated with a previous record, any unique record identifier associated with the first (CONTINUATION_FLAG = N) record shall be repeated in all subsequent continuation records returned in an OASIS response. Each Template that supports the use of continuation records and those particular Data Elements (COLUMN_HEADERS) that may be referenced in one or more continuation records are identified in Section 4.3. On upload or input of Template data, any values supplied via continuation records that correspond to COLUMN_HEADERs other than those explicitly allowed to appear in continuation records for a particular Template shall be ignored. However commas must be included to properly align the fields (columns). Note that the submission of continuation records is only supported by the CSV Format method of uploading data to an Input/Response Template

002-4.2.7.6	Error Handling in CSV-Formatted Responses

a. Validity of each record in the CSV-formatted Response to a Template Input shall be indicated through the use of RECORD_STATUS and ERROR_MESSAGE Data Elements which are included in each Data Record (row) of the Response.

- If no error was encountered in an Input Data Record, the RECORD_STATUS Data Element in the corresponding Response record shall be returned with a value of 200 (success), and the ERROR_MESSAGE shall be blank.

- If any error is detected in processing an Input Data Record, it shall be indicated by a RECORD_STATUS Data Element value other than 200. The ERROR_MESSAGE shall be set to an appropriate text message to indicate the source of the error in that Data Record.

b. The overall validity of each Template Query or Input shall be indicated in the CSV-formatted Response via the two REQUEST_STATUS and ERROR_MESSAGE header records (see section 4.2.7.3):

- If no errors were encountered in processing the User's Input Data Records, the REQUEST_STATUS shall be returned with the value of 200 (success), and the ERROR_MESSAGE shall be blank.

- If any errors were detected in the Template Input Data Records, the REQUEST_STATUS value shall be any value other than 200, and the ERROR_MESSAGE shall be set to an appropriate text message to indicate the source of the error.

c. The OASIS Node shall validate all Input records before returning a Response to the User. The Node shall process all valid records, while invalid records shall be identified as erroneous through the use of RECORD_STATUS and ERROR_MESSAGE. The User must correct the invalid fields and resubmit only those records that were invalid. If an error is encountered in a record which is part of a set of Continuation records, then all records belonging to that set must be resubmitted.

002-4.2.8	Registration Information

002-4.2.8.1	General

As specified in the Information Access Requirements, OASIS Nodes shall provide a mechanism to register Users of the OASIS Node with a Provider. For all levels of access to OASIS information beyond simple read-only access, OASIS Nodes shall provide a mechanism to identify Users of the OASIS at least to the level of their respective Companies. The OASIS Node shall maintain both Company and User registration information.

002-4.2.8.2	Company Information

OASIS Templates require that certain Company registration information be maintained. As an extension of the Company registration information of the host, domain and port identifiers for dynamic notification of changes in the Customer's purchase requests, a field should be added to the Company's registration information that would define/identify how notification would be delivered to that Company should a transmission or ancillary purchase request be directed to that Company as a Seller of a transmission or ancillary service. The pertinent information would be either a full HTTP protocol URL defining the protocol, host name, port, path, resource, etc. information or a "mailto:" URL with the appropriate mailbox address string. On receipt of any purchase request directed to that Company as SELLER via either the "transrequest" or "ancrequest" Templates, or on submission of any change in request information submitted to that Company as SELLER via either the "transcust" or "anccust" Templates, a notification message formatted as documented for the delivery of notification to the Customer, shall be formatted and directed to the Seller. At a minimum, OASIS Nodes shall maintain the following information for each Company:

a. Company Code: 4 character code for primary transmission providers; 6 character code for eligible customers in accordance with NERC Tagging Information System (TIS) requirements shall be maintained for each Company.

b. Default Contact: Unless specified for each individual user affiliated with the Company, default contact information consisting of a phone number, fax number, and e-mail address shall be maintained for each Company.

c. Provider Affiliation: Each eligible Customer shall be obligated to identify to the OASIS TSIP any affiliation with a Transmission Provider whose "home page" is on that OASIS Node.

d. Notification URL: For Companies using the URL notification mechanism for delivery of messages on each change of ancillary/transmission reservation STATUS, each Company shall provide the IP host name and port number to be used in delivering notification messages. OASIS Nodes shall have the right to refuse support for notification to any IP ports other than port 80.

002-4.2.8.3	User Information

With the exception of "read-only" (visitor) access, OASIS Nodes shall, at a minimum, provide a mechanism to identify Users of the Node with at least their Company. However, OASIS Nodes and Providers shall have the right to require full User identification even for visitor accounts. To support the required OASIS Template Data Elements, OASIS Nodes shall maintain the following information for each registered User:

- Company

- Name

- Phone

- Fax

- E-mail

In the event no additional User identification/registration information is maintained by the OASIS Nodes, all Template Data Elements referring to "company, name, phone, fax, e-mail" for either Customers or Sellers shall default to the Contact Information maintained for that User's Company.

002-4.2.9	Representation of Time

002-4.2.9.1	General

It is critical that all Users of OASIS Nodes have a clear and unambiguous representation of time associated with all information transferred to/from OASIS Nodes. For this reason, all Data Elements associated with time in OASIS Nodes shall represent "wall clock" times, which are NOT to be confused with other common industry conventions such as "hour ending." For the convenience of the User community, OASIS Nodes shall be allowed to accept the input and display of "time" in any acceptable form provided such non-standard representations are CLEARLY labeled on the associated HTML screens. Alternate representations of time in CSV formatted messages shall not be allowed. The following rules shall be implemented in OASIS Nodes for the representation of time on User entries (Query and Input) and output (Response) Templates.

002-4.2.9.2	Input Time

All time related Data Elements associated with either the Input or Query of Input/Response or Query/Response OASIS Templates shall be validated according the following rules. If the time zone associated with a time Data Element is associated with either Universal Time (UT) or a "standard" time zone (e.g., ES, CS, etc.), OASIS Nodes shall accept and apply a fixed hour offset from Universal Time year-round. If the time zone associated with a time Data Element is specified with a "daylight savings" time zone (e.g. ED, CD, etc.), OASIS Nodes shall verify that daylight savings time is in effect for the date/time specified. If daylight savings time (as specified by the time from 2:00am on the first Sunday of April through 2:00 am on the last Sunday of October) is not in effect, the Users input shall be rejected with an error response. If daylight savings time is in effect, the Users input shall be accepted and the appropriate hours offset from Universal Time shall be applied by OASIS Nodes for conversion to all other time zones. The input of start/stop times for transactions spanning the crossover day between standard and daylight (and vices versa) times must be made either entirely in standard time (valid year-round), or in two different time zones (xS/xD or xD/xS) for the start and stop times, depending on the time of year.

002-4.2.9.3	Output (Response) Time

The OASIS Node shall return all time Data Elements in the response to Input/Response or Query/Response OASIS Templates based on either the User specified RETURN_TZ header Query Variable or an appropriate OASIS specific default. OASIS Nodes shall interpret RETURN_TZ to specify:

a. The base time zone for conversion of all time Data Elements (e.g. Eastern, Pacific, etc.)

b. Whether daylight savings time is recognized. For example, a RETURN_TZ=ES would return all time Data Elements in Eastern Standard Time year-round. However, a RETURN_TZ=ED would direct OASIS Nodes to return all time Data Elements in Eastern Standard Time (ES) when daylight savings time is not in effect, and then return all time Data Elements in Eastern Daylight Time (ED) when daylight time is in effect.

002-4.2.10	Transaction Process

OASIS shall implement Templates that allow Customers and Sellers to enter, modify and consummate arrangements for transmission and ancillary services. The following subsections outline the basic steps for arranging for these services. Section 4.2.13 provides further detail on the use of OASIS Templates to modify the terms of a transaction in support of specific provisions of the Open Access ProForma Tariff.

002-4.2.10.1	Purchase Transactions

Customers shall purchase services from the Seller using the following basic steps (see Exhibit 4-1):

a. The Templates (transrequest and ancrequest) shall be used by a Customer to enter a request for specific transmission or ancillary services from a specific Seller. Basic requests for transmission services from the Primary Transmission Provider shall be assigned a REQUEST_TYPE of "ORIGINAL"; requests for transmission services on the secondary market (where SELLER is not the Primary Transmission Provider) shall be assigned a REQUEST_TYPE of "RESALE" (Section 4.2.13 documents other values that may be assigned to REQUEST_TYPE). The Customer may enter a BID_PRICE which is different from the OFFER_PRICE in order to try to negotiate a lower price. The OASIS Node sets the initial STATUS of the request to QUEUED. The Customer may set the STATUS_NOTIFICATION to indicate that the OASIS Node must notify the Customer on any change in the request's STATUS or related Data Elements (see Dynamic Notification). The Customer may designate the request as PRECONFIRMED. Preconfirmed requests will be automatically set to the STATUS of CONFIRMED when ACCEPTED by the Seller without requiring an explicit confirmation from the Customer. Prior to or commensurate with a Seller's setting of a preconfirmed reservation request's STATUS to ACCEPTED (and by implication CONFIRMED), the Seller must set OFFER_PRICE equal to the value of BID_PRICE as established by the Customer on submission of the request.

b. The Templates (transstatus and ancstatus) shall be used by Customers and Sellers to monitor the status of their transactions in progress. These Templates shall also be used by any Users to review the status of any transactions. The NEGOTIATED_PRICE_FLAG Data Element is set when the Seller agrees to a BID_PRICE (by setting OFFER_PRICE equal to BID_PRICE) that is different from the previously posted price. It will show "higher" when OFFER_PRICE is higher than the posted price, and "lower" when the OFFER_PRICE is lower than the posted price.

c. The Templates (transsell and ancsell) shall be used by a Seller to set a new value into STATUS, to enter a MW value in CAPACITY_GRANTED, if offering partial service, and to negotiate a price by entering a new OFFER_PRICE which is different from the BID_PRICE entered by the Customer in the transrequest Template. During these negotiations, a Reseller shall formally indicate the approval or disapproval of a transaction and indicate which rights from prior confirmed reservations are to be reassigned. A Primary Provider may, but is not required, to enter transaction approval or disapproval using this Template. In the event the Seller is only able to grant a portion of the transmission capacity requested by the Customer and the Seller is obligated or elects to extend an offer for partial service, the Seller shall indicate to the Customer the amount of capacity available using CAPACITY_GRANTED and set the reservation request's status to COUNTEROFFER. Preconfirmed requests that are set to COUNTEROFFER due to an offer of service at a level lower than requested by the Customer shall require explicit confirmation by the Customer. The valid STATUS values which may be set by a Seller are: RECEIVED, INVALID, STUDY, COUNTEROFFER, ACCEPTED, REFUSED, SUPERSEDED, DECLINED, DISPLACED, ANNULLED, or RETRACTED.

d. The Customer shall use the transstatus and ancstatus Templates to view the Seller's new offer price, partial service offer and/or approval/disapproval decision.

e. After receiving notification of the transaction's STATUS being set to COUNTEROFFER by the Seller, the Templates (transcust and anccust) shall be used by the Customer to modify the BID_PRICE and set the STATUS to REBID or CONFIRMED. Transcust shall also be used to confirm an offer for partial service (where CAPACITY_GRANTED is less than CAPACITY_REQUESTED) by setting the STATUS to CONFIRMED. After negotiations are complete (STATUS set to ACCEPTED by the Seller), the Customer shall formally enter the confirmation or withdrawal of the offer to purchase services for the OFFER_PRICE shown in the transstatus Template. The valid STATUS values which a Customer may set are: REBID, CONFIRMED, or WITHDRAWN.

f. The Seller shall use the transstatus (ancstatus) Template to view the Customer's new bid price and/or confirmation/withdrawal decision, again responding through transsell or ancsell if necessary. If the Seller offers to sell a service at an OFFER_PRICE less than that posted in the transoffering (ancoffering) Template, the transoffering (ancoffering) Template must be updated to reflect the new OFFER_PRICE.

g. For deals consummated off the OASIS Nodes by a Seller, after the Customer has accepted the offering, the Templates (transassign and ancassign) may be used by the Seller to notify the Primary Provider of the transfer of rights to the Customer. Continuation records may be used to indicate the reassigning of rights for a "profile" of different assignments and different capacities over different time periods.

h. The source of all User and Seller contact information shall be the User registration process. Therefore, it shall not be input as part of uploads, but shall be provided as part of all transaction downloads.

i. OASIS Nodes shall accept a Seller initiated change in STATUS to ACCEPTED only when OFFER_PRICE matches BID_PRICE (i.e., Seller must set OFFER_PRICE equal to BID_PRICE prior to or coincident with setting STATUS to ACCEPTED).

j. OASIS Nodes shall accept a Customer initiated change in STATUS to CONFIRMED only when BID_PRICE matches OFFER_PRICE (i.e., Customer must set BID_PRICE equal to OFFER_PRICE prior to or coincident with setting STATUS to CONFIRMED).

k. If CAPACITY_GRANTED is null when STATUS is being changed to ACCEPTED or CONFIRMED, the OASIS Node shall set it equal to CAPACITY_REQUESTED.

002-4.2.10.2	Status Values

The possible STATUS values are:

QUEUED = initial status assigned by TSIP on receipt of "customer services purchase request."

INVALID = assigned by TSIP or Provider indicating an invalid field in the request, such as improper POR, POD, source, sink, etc. (Final state).

RECEIVED = assigned by Provider or Seller to acknowledge QUEUED requests and indicate the service request is being evaluated, including for completing the required ancillary services.

STUDY= assigned by Provider or Seller to indicate some level of study is required or being performed to evaluate service request.

REFUSED = assigned by Provider or Seller to indicate service request has been denied due to lack of availability of transmission capability. (Final state).

COUNTEROFFER = assigned by Provider or Seller to indicate that a new OFFER_PRICE is being proposed or that CAPACITY_GRANTED is less than CAPACITY_REQUESTED.

REBID = assigned by Customer to indicate that a new BID_PRICE is being proposed.

SUPERSEDED = assigned by Provider or Seller when a request which has not yet been confirmed is preempted by another reservation request. (Final state).

ACCEPTED = assigned by Provider or Seller to indicate the service request at the designated OFFER_PRICE and CAPACITY_GRANTED has been approved/accepted. If the reservation request was submitted PRECONFIRMED and CAPACITY_GRANTED is equal to CAPACITY_REQUESTED, the OASIS Node shall immediately set the reservation status to CONFIRMED. Depending upon the type of ancillary services required, the Seller may or may not require all ancillary service reservations to be completed before accepting a request.

DECLINED = assigned by Provider or Seller to indicate that the terms and conditions, such as the BID_PRICE, are unacceptable and that negotiations are terminated or that contractual terms and conditions have not been met. (Final state).

CONFIRMED = assigned by Customer in response to Provider or Seller posting "ACCEPTED" status, to confirm service. Once a request has been "CONFIRMED," a transmission service reservation exists. (Final state, unless overridden by DISPLACED or ANNULLED state).

WITHDRAWN = assigned by Customer at any point in request evaluation to withdraw the request from any further action. (Final state).

DISPLACED = assigned by Provider or Seller when a "CONFIRMED" reservation from a Customer is displaced by a higher priority reservation and the Customer is not offered or has not exercised right of first refusal (i.e. refused to match terms of new request). (Final state).

ANNULLED = assigned by Provider or Seller when, by mutual agreement with the Customer, a confirmed reservation is to be voided. (Final state).

RETRACTED = assigned by Provider or Seller when the Customer fails to confirm or withdraw the request within the required time period. (Final state).

The following diagram can be used as a business process guideline; however, individual tariffs will dictate specific allowed actions between states.

Exhibit 4-1 - State Diagram of Purchase Transactions

002-4.2.10.3	Dynamic Notification

Customers may specify the delivery of dynamic notification messages on each change in STATUS or any other Data Element(s) associated with an ancillary or transmission service reservation. OASIS Nodes shall support the delivery of dynamic notification messages through either the HTTP protocol or by electronic mail. The selection of which mechanism is used and the contents of the messages delivered to the client program or e-mail address is defined by the content of the STATUS_NOTIFICATION Data Element as described in the next subsections. Regardless of whether this dynamic notification method is used or not, it shall still remain the User's responsibility to get the desired information, possibly through the use of a periodic "integrity request". OASIS Nodes shall not be obligated or liable to guarantee delivery/receipt of messages via the STATUS_NOTIFICATION mechanism other than on a "best effort" basis. As an extension of the Company registration information of the host, domain and port identifiers for dynamic notification of changes in the Customer's purchase requests, a field should be added to the Company's registration information that would define/identify how notification would be delivered to that Company should a transmission or ancillary purchase request be directed to that Company as a Seller of a transmission or ancillary service. The pertinent information would be either a full HTTP protocol URL defining the protocol, host name, port, path, resource, etc. information or a "mailto:" URL with the appropriate mailbox address string. On receipt of any purchase request directed to that Company as SELLER via either the "transrequest" or "ancrequest" Templates, or on submission of any change in request STATUS (or any other Data Elements associated with the request) to that Company as SELLER via either the "transcust" or "anccust" Templates, a notification message formatted as documented for the delivery of notification to the Customer, shall be formatted and directed to the Seller. This extension of dynamic notification is required only where the Transmission Provider has programmed its computer system for its own notification.

002-4.2.10.3.1 	HTTP Notification

OASIS Nodes shall deliver dynamic notification to a client system based on HTTP URL information supplied in part by the STATUS_NOTIFICATION Data Element and by information supplied as part of the Customer's Company registration information. HTTP URL's are formed by the concatenation of a protocol field (i.e., http: ), a domain name (e.g., //www.tsin.com), a port designation (e.g., :80), and resource location information.

The STATUS_NOTIFICATION Data Element shall contain the protocol field "http:", which designates the notification method/protocol to be used, followed by all resource location information required; the target domain name and port designations shall be inserted into the notification URL based on the Customer's Company registration information. The resource location information may include directory information, cgi script identifiers and URL encoded query string name/value pairs as required by the Customer's application. An OASIS Node performs no processing on the resource location information other than to include it verbatim along with the protocol, domain name and port information when forming the URL that will be used to deliver the HTTP protocol notification message.  For example,

Company XYZ has established the domain name and port designations of "//oasistc.xyz.com:80" as part of their registration information.When a transmission reservation is submitted by one of Company XYZ's users (the Customer), and includes a STATUS_NOTIFICATION Data Element with the value of

"http:/cgi-bin/status?DEAL_REF=8&REQUEST_REF=173", an OASIS Node shall deliver an HTTP notification message using the URL:

http://oasistc.xyz.com:80/cgi-bin/status?DEAL_REF=8&REQUEST_REF=173

If the STATUS_NOTIFICATION field contained only the "http:" protocol designation, the notification message would be delivered using the URL:

http://oasistc.xyz.com:80

The contents of the HTTP protocol notification message delivered by an OASIS Node shall consist of the complete URL created by combining fields from the STATUS_NOTIFICATION Data Element and Company registration information as part of an HTTP POST method request. In addition to the POST method HTTP header record, OASIS Nodes shall also append the CSV formatted output of the transstatus Template information for that particular reservation using the standard Content-type: text/x-oasis-csv and appropriate Content-length: HTTP header records. OASIS Nodes shall use a Primary Provider specific default value for RETURN_TZ in formulating the transstatus response information. Continuing with the previous example, the important records in the HTTP notification message that would be delivered to Company XYZ for the transmission reservation request submitted to Primary Provider ABC and given an ASSIGNMENT_REF of 245 would be,

POST http://oasistc.xyz.com:80/cgi-bin/status?DEAL_REF=8&REQUEST_REF=173

HTTP/1.0

.

.

Content-type: text/x-oasis-csv

Content-length: <byte count of remainder of message>

REQUEST_STATUS=200

TIME_STAMP=<appropriate value>

VERSION=1.4

TEMPLATE=transstatus

OUTPUT_FORMAT=DATA

PRIMARY_PROVIDER_CODE=ABC

PRIMARY_PROVIDER_DUNS=123456789

RETURN_TZ=<appropriate value for ABC>

DATA_ROWS=1

COLUMN_HEADERS=CONTINUATION_FLAG, ASSIGNMENT_REF, . . .

N, 245, . . .

In the event an error is encountered delivering the HTTP notification message to the target URL as indicated by a failure of the target system to respond, or return of HTTP response status of 408, 500, 503, or 504, OASIS Nodes shall retry up to two more times, once every 5 minutes.

002-4.2.10.3.2 	E-mail Notification

OASIS Nodes shall deliver dynamic notification to an e-mail address based on Mailto: URL information specified in the STATUS_NOTIFICATION Data Element. Mailto: URL's consist of the "mailto:" protocol identifier and an Internet mail address to which the notification message should be sent.  The STATUS_NOTIFICATION Data Element shall contain the protocol field "mailto:", which designates the notification method/protocol to be used, followed by an Internet mail address in conformance with RFC 822. OASIS Nodes shall send an e-mail message to the Internet mail address containing the following information: "To:" set to the mail address from the STATUS_NOTIFICATION Data Element, "From:" set to an appropriate mail address of the OASIS Node, "Subject:" shall be the transstatus Template name followed by the value of the ASSIGNMENT_REF Data Element and the current value for the STATUS Data Element associated with the reservation (e.g., "Subject: transstatus 245 ACCEPTED"), and the body of the message shall contain the CSV formatted output of the transstatus Template information for that particular reservation. OASIS Nodes shall use a Primary Provider specific default value for RETURN_TZ in formulating the transstatus response information.

002-4.2.10.4	Use of Comments

Transmission and ancillary service reservation templates support the following text data elements to be used to communicate information between parties (i.e., transmission provider, seller, and customer) to a transaction:

- PRIMARY_PROVIDER_COMMENTS - for information to be communicated by the primary transmission provider to all other parties

- SELLER_COMMENTS - for information to be communicated by the seller (either primary provider or reseller) to the customer

- CUSTOMER_COMMENTS - for information to be communicated by the customer to the seller

- STATUS_COMMENTS - for information to be communicated by any party to all other parties

Use of these comments fields is at the discretion of the parties to the transaction with the exception that sellers of services must indicate via SELLER_COMMENTS the reason for denial of any request for service (STATUS values of INVALID, REFUSED, or DENIED). Transactions which are subject to displacement, either before or after confirmation (STATUS values of SUPERSEDED or DISPLACED), shall also include a reference to the competing reservation request that initiated the displacement in the SELLER_COMMENTS.

002-4.2.11	Reference Identifiers

a. The TSIP shall assign a unique reference identifier, ASSIGNMENT_REF, for each Customer request to purchase capacity or services. The value of ASSIGNMENT_REF may be used to imply the order in which the request was received by the TSIP. This identifier will be used to track the request through various stages, and will be kept with the service through out its life. Whenever a transaction is modified by a subsequent transaction, a new ASSIGNMENT_REF number is assigned to that subsequent transaction along with a reference to the previous transaction such that a chain of all transactions related to the service can be maintained. These changes create a parent/child relationship between related requests. The TSIP shall use REASSIGNED_REF or RELATED_REF as specified in section 4.2.13 to identify the parent request’s ASSIGNMENT_REF and shall increment the IMPACTED counter of the parent request by 1. Reductions to a request posted by the Transmission Provider shall also reference the requests ASSIGNMENT_REF and the TSIP shall increment the IMPACTED counter of the request by 1.

b. The TSIP shall assign a unique reference identifier, POSTING_REF, to each Seller's offerings of service for sale or other information (messages) posted on an OASIS Node. The Seller in any/all subsequent Template submissions, that would result in a modification to or deletion of that specific offering or message, shall reference this identifier. Optionally, Customers may also refer to this POSTING_REF in their subsequent purchase requests to aid in identifying the specific offering associated with the purchase request.

c. Sellers may aggregate portions of several previous transmission service reservations to create a new offering to be posted on an OASIS Node. When all or a portion of such offerings are sold, the Seller (original Customer) is obligated to notify the Primary Provider of the sale/assignment by inserting appropriate reassignment information on the OASIS Node (via the transsell or transassign Templates) or by some other approved method. This reassignment information consists of the ASSIGNMENT_REF value assigned to the original reservation(s) and the time interval and capacity amount(s) being reassigned to the new reservation. These values are retained in the REASSIGNED_REF, REASSIGNED_START_TIME, REASSIGNED_STOP_TIME, and REASSIGNED_CAPACITY Data Elements.

d. Sellers may identify their service offerings received from Customers through the Seller supplied value specified for the SALE_REF Data Element.

e. Customers may track their purchase requests through the Customer supplied values specified for the DEAL_REF and REQUEST_REF Data Elements. Customers may also use POSTING_REF and SALE_REF in their purchase requests to refer back to posted offerings.

002-4.2.12	Linking of Ancillary Services to Transmission Services

The requirements related to ancillary services are shown in transoffering (and updated using transupdate) using the ANC_SVC_REQ Data Element containing the following permitted values:

SC:x; RV:x; RF:x; EI:x; SP:x; SU:x;

where SC, RV, RF, EI, SP and SU are the ancillary services 1 through 6 described in the Proforma Tariff,

- SC - Scheduling, system Control and dispatch

- RV - Reactive supply and Voltage control

- RF - Regulation and Frequency response

- EI - Energy Imbalance

- SP - SPinning reserve

- SU - SUpplemental reserve

and where x={M,R,O,U} means one of the following:

- Mandatory, which implies that the Primary Provider must provide the ancillary service

- Required, which implies that the ancillary service is required, but not necessarily from the Primary Provider

- Optional, which implies that the ancillary service is not necessarily required, but could be provided

- Unknown, which implies that the requirements for the ancillary service are not known at this time

Ancillary services may be requested by a User from the Provider at the same time as transmission services are requested via the transrequest Template, by entering the special codes into ANC_SVC_LINK to represent the Proforma ancillary services 1 through 6 (or more) as follows:

SC:(AA[:xxx[:yyy[:nnn]]]); RV: (AA[:xxx[:yyy[:nnn]]]); RF:

(AA[:xxx[:yyy[:nnn]]]);

EI: (AA[:xxx[:yyy[:nnn]]]); SP: (AA[:xxx[:yyy[:nnn]]]); SU:

(AA[:xxx[:yyy[:nnn]]]); {Registered}:(AA[:xxx[:yyy[:nnn]]])

where AA is the appropriate PRIMARY_PROVIDER_CODE, SELLER_CODE, or CUSTOMER_CODE, and represents the company providing the ancillary services. "AA" may be unspecified for "xxx" type identical to "FT", in which case the ":" character must be present and precede the "FT" type. If multiple "AA" terms are necessary, then each "AA" grouping will be enclosed within parenthesis, with the overall group subordinate to the AS_TYPE specified within parenthesis and where xxx represents either:

- "FT" to indicate that the Customer will determine ancillary services at a future time, or

- "SP" to indicate that the Customer will self-provide the ancillary services, or

- "RQ" to indicate that the Customer is asking the OASIS Node to initiate the process for making an ancillary services reservation with the indicated Provider or Seller on behalf of the Customer. The Customer must then continue the reservation process with the Provider or Seller. If the transmission services request is for preconfirmed service, then the ancillary services shall also be preconfirmed, or

- "AR" to indicate an assignment reference number sequence follows.

The terms "yyy" and "nnn" are subordinate to the xxx type of "AR". yyy represents the ancillary services reservation number (ASSIGMNENT_REF) and nnn represents the capacity of the reserved ancillary services. Square brackets are used to indicated optional elements and are not used in the actual linkage itself. Specifically, the :yyy is applicable to only the "AR" term and the :nnn may optionally be left off if the capacity of ancillary services is the same as for the transmission services, and optionally multiple ancillary reservations may be indicated by additional (xxx[:yyy[:nnn]]) enclosed within parenthesis. If no capacity amount is indicated, the required capacity is assumed to come from the ancillary reservations in the order indicated in the codes, on an "as-needed" basis.

Examples:

Example 1:

Assume ancillary services SC and RV are mandatory from the TP, whose code is "TPEL", and ancillary services RF, EI, SP and SU are required, but will be defined at a future time.

"SC: (TPEL:RQ); RV: (TPEL:RQ); RF:(:FT); EI:(:FT); SP:(:FT); SU:(:FT)";

Example 2:

Assume ancillary services SC and RV are mandatory from the TP, whose code is "TPEL", and RF, EI, SP and SU are self-supplied. The customer code is "CPSE"

"SC: (TPEL:RQ); RV: (TPEL:RQ); RF:(CPSE:SP); EI:(CPSE:SP);

SP:(CPSE:SP); SU:(CPSE:SP)"

Example 3:

Assume ancillary services SC and RV are mandatory from the TP, whose code is "TPEL", and ancillary services RF, EI, SP and SU were purchased via a prior OASIS reservation from seller "SANC" whose reservation number was "39843". There is sufficient capacity within the Ancillary reservation to handle this Transmission reservation.

"SC:(TPEL:RQ); RV:(TPEL:RQ); RF:(SANC:AR:39843);

EI:(SANC:AR:39843) SP:(SANC:AR:39843); SU:(SANC:AR:39843)"

Example 4:

Assume ancillary services SC and RV are mandatory from the TP, whose code is "TPEL", and ancillary services RF, EI, SP and SU were purchased via prior OASIS reservations from sellers "SANC" and "TANC", whose reservation numbers where "8763" and "9824" respectively. There is not sufficient capacity within the Ancillary reservation from seller "SANC" to handle this Transmission reservation. In this case the OASIS reservation number 8763 will be depleted for the time frame specified within the transmission reservation and the remaining required amount will come from reservation number "9824".

"SC:(TPEL:RQ); RV:(TPEL:RQ); RF:((SANC:AR:8763)(TANC:AR:9824));

EI:((SANC:AR:8763)(TANC:AR:9824));

SP:((SANC:AR:8763)(TANC:AR:9824));

SU:((SANC:AR:8763)(TANC:AR:9824))"

Example 5:

Assume a transmission reservation in the amount of 100 mw/hour for a period of one day is made. Ancillary services SC and RV are mandatory from the TP, whose code is "TPEL", and ancillary services RF, EI, SP and SU were purchased via prior OASIS reservations from sellers "SANC" and "TANC", whose reservation numbers where "8763" and "9824" respectively. There is sufficient capacity within the Ancillary reservation from seller "SANC" to handle this Transmission reservation, however the purchaser wishes to use only "40 mw's" from this seller. In this case the OASIS reservation number 8763 will be depleted in the amount of "40 mw's" for the time frame specified within the transmission reservation and the remaining required amount will come from reservation number "9824".

"SC:(TPEL:RQ); RV:(TPEL:RQ); RF:((SANC:AR:8763:40)(TANC:AR:9824));

EI:((SANC:AR:8763:40)(TANC:AR:9824));

SP:((SANC:AR:8763:40)(TANC:AR:9824));

SU:((SANC:AR:8763:40)(TANC:AR:9824))"

002-4.2.13	Modifications to Transactions

Transactions processed by OASIS as outlined in Section 4.2.10 may be subject to modification by subsequent transactions or events as permitted under the Transmission Provider's Tariff. The following subsections describe the actions to be taken on OASIS to implement specific provisions of the Open Access Pro Forma Tariff related to transmission service. Depending on the exact form of the Provider's Tariff, some of these provisions may not be applicable, and implementation of other provisions may be Provider specific. In general, modification to any OASIS transaction initiated by the Customer shall involve the submission of a new transaction. The new transaction shall identify the specific type of modification being requested using the REQUEST_TYPE Data Element, and reference the transaction to be modified using the RELATED_REF Data Element. In the specific case of secondary market transactions, related transactions are identified with the use of the REASSIGNED_REF Data Element. The following are the specific restricted values for the REQUEST_TYPE Data Element and a brief description of their use:

- ORIGINAL – typical reservation requests submitted to the Primary Provider

- RESALE – secondary market requests submitted to a Transmission Customer as Secondary Transmission Provider

- RENEWAL – request to renew an expiring transmission reservation

- MATCHING – request to meet or exceed a competing request to retain transmission service (right of first refusal)

- DEFERRAL – request to defer or apply for extension on start of transmission service

- REDIRECT – request to redirect all or portion of a transmission reservation to an alternate POR/POD and/or make other changes to the terms of service as permitted

- {registered} – Primary Transmission Provider's may register values for REQUEST_TYPE to implement specific provisions of their Tariffs.

The Primary Transmission Provider may also modify a Customer's transmission reservation to the extent that the original reservation's MW capacity available for scheduling may be reduced over all or a portion of the term of the original reservation subject to the terms of the Provider's Tariff. Any time a subsequent transaction initiated by the Customer modifies all or a portion of a prior transaction, or a reduction in reserved MWs is initiated by the Primary Provider, the IMPACTED counter will be incremented in the prior transaction shall be set.  OASIS User's may view the list of all subsequent transactions or events impacting a given transaction using the reduction Template.  The following subsections describe the application of REQUEST_TYPE to actions taken on OASIS, and how various modifications to existing reservations  are to be affected.

002-4.2.13.1	Original Transactions

Transactions submitted to the Primary Transmission Provider using the transrequest Template for the typical reservation of transmission service shall be identified by the REQUEST_TYPE of  "ORIGINAL", and be processed as described in Section 4.2.10. The RELATED_REF Data Element must be null, the Primary Provider specified as SELLER, and, if the REQUEST_TYPE is null, the  OASIS node shall default its value to "ORIGINAL". The value returned in the ASSIGNMENT_REF  Data Element shall be used to refer to this specific, original transmission reservation request in any  subsequent actions taken.

002-4.2.13.2	Partial Service

If in the evaluation of a transmission request, the Primary Provider determines that only a portion of the  Customer's requested capacity reservation (CAPACITY_REQUESTED Data Element) can be  accommodated and that the Provider is obligated or elects to offer the Customer only a portion of the  requested capacity, the Primary Provider shall set the CAPACITY_GRANTED Data Element(s)  associated with that transmission reservation to the amount available, and set the STATUS to  COUNTEROFFER. If the CAPACITY_REQUESTED and/or CAPACITY_GRANTED are not  constant over time, continuation records shall be used to convey the time varying profile of MW  capacity associated with the transmission request (CAPACITY_REQUESTED,  CAPACITY_GRANTED, START_TIME and STOP_TIME).  The Customer shall recognize the offer of partial service by CAPACITY_REQUESTED not being  equal to CAPACITY_REQUESTED and the request STATUS of COUNTEROFFER. The Customer  may elect to CONFIRM, WITHDRAW, or REBID the reservation using the transcust Template.  If the transmission reservation request was marked PRECONFIRMED by the Customer and an offer of  partial service is extended, the reservation request must be explicitly CONFIRMed by the Customer.  The OASIS node shall not automatically CONFIRM a request where CAPACITY_REQUESTED does  not equal CAPACITY_GRANTED when/if the request STATUS is set to ACCEPTED.

002-4.2.13.3	Secondary Sales – On OASIS

The sale or assignment of rights from one Transmission Customer to another may be conducted on OASIS using the same transaction process as described for purchases made from the Primary Transmission Provider. The request for purchase of transmission service from another Transmission Customer (Secondary Transmission Provider) is submitted by the Customer purchasing the capacity using the transrequest Template. Secondary transmission sales shall be identified by the REQUEST_TYPE of "RESALE", and be processed as described in Section 4.2.10. Th  RELATED_REF Data Element must be null, the Transmission Customer owning capacity offered for resale (the Secondary Transmission Provider) specified as SELLER, and, if the REQUEST_TYPE is  null, the OASIS node shall default its value to "RESALE".  The Secondary Transmission Provider (original Customer) selling their transmission rights over OASIS shall use the transsell Template to approve/deny the request. If the request is to be approved  (STATUS=ACCEPTED), the transmission reservation(s) currently held by the Customer selling their  capacity and the amount of capacity over time from each such reservation to be transferred to the  secondary market Customer must be identified. This information is supplied via the  REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME and  REASSIGNED_STOP_TIME Data Elements. The aggregation of all REASSIGNED_xxx Data  Elements must match the capacity and time frame of the secondary transmission request as specified in  the CAPACITY_GRANTED (and/or CAPACITY_REQUESTED), START_TIME and STOP_TIME  Data Elements of the "RESALE" transaction.  The Customer purchasing transmission service on the secondary market over OASIS shall use the  transcust to monitor the transaction and CONFIRM the sale if necessary. Upon confirmation of the secondary sale the IMPACTED attribute will be incremented for each reservations referenced by the  REASSIGNED_REF Data Elements.

002-4.2.13.4	Secondary Sales – Off OASIS

The sale or assignment of rights from one Transmission Customer to another does not have to be conducted on OASIS. However, the Transmission Customer acting as a Secondary Transmission Provider is obligated to notify the Primary Transmission Provider of all sales or assignments of transmission rights to a third party. The transassign Template shall be used by the Secondary Transmission Provider to convey this sale/assignment information to the Primary Provider.  The transassign Template allows the Secondary Transmission Provider to submit all information related to the secondary market sale. The REQUEST_TYPE of "RESALE" is directly implied by use of the transassign Template. The REASSIGNED_REF, REASSIGNED_CAPACITY,  REASSIGNED_START_TIME and REASSIGNED_STOP_TIME Data Elements identify the  transmission reservation(s) currently held by the Secondary Transmission Provider, and the amount of  capacity over time from each such reservation to be transferred to the secondary market Customer. The  aggregation of all REASSIGNED_xxx Data Elements must match the capacity and time frame of the  secondary transmission request as specified in the CAPACITY_GRANTED, START_TIME and  STOP_TIME Data Elements of the "RESALE" transaction.  The IMPACTED attributed will be incremented for each reservations referenced by the  REASSIGNED_REF Data Elements.

002-4.2.13.5	Renewal

Requests by the Transmission Customer to renew their transmission reservation, subject to the terms of the Provider's Tariff, should be submitted using the REQUEST_TYPE of  "RENEWAL" and specify the ASSIGNMENT_REF of the request to be renewed in the new  request's RELATED_REF Data Element. This unique REQUEST_TYPE and association  with the original request more clearly communicates, over OASIS, the intent of the  Transmission Customer, and distinguishes requests for renewal of service from new requests  by the same TC for additional service.

002-4.2.13.6	Displacement – No Right of First Refusal

Confirmed transmission reservations may be subject to displacement in the event competing, higher  priority requests are received by the Primary Transmission Provider. If the original Customer does not  have the right of first refusal and all capacity from the original, confirmed reservation is required to  accommodate the higher priority request, the Primary Transmission Provider shall set the original  reservation's STATUS to DISPLACED. The STATUS of DISPLACED indicates that the original  reservation has been displaced in its entirety. A reference to the competing request that forced the  displacement should be entered in the SELLER_COMMENTS field of the original reservation.  If only a portion of the original, confirmed reservation's capacity is required to accommodate the higher  priority request, the Primary Transmission Provider shall document the "recall" of reserved capacity  from the lower priority, confirmed reservation by incrementing the IMPACTED counter on that  reservation and posting on OASIS the amount and time frames over which the original reservation's  capacity was reduced. The Transmission Customer may view all impacts to existing transmission  reservations (e.g., partial displacements, secondary sales, etc.) using the reduction Template. A  reference to the competing request that forced the displacement should be entered in the  SELLER_COMMENTS field of the original reservation.

002-4.2.13.7	Displacement – With Right of First Refusal

Confirmed transmission reservations may be subject to displacement in the event competing, higher  priority requests are received by the Primary Transmission Provider. If the Primary Provider's Tariff  obligates, or the Primary Provider elects to grant the original Customer the right of first refusal, the  original Customer shall be notified of the competing request. The Primary Provider shall set the original request's COMPETING_REQUEST_FLAG to Y and update the SELLER_COMMENTS with a reference to the competing requests ASSIGNMENT_REF. These changes will initiate electronic notification, provided the Customer has elected to receive such notification.  If the original Customer elects to meet or exceed the terms and conditions of the competing request,  that Customer shall submit a new reservation request using the transrequest Template specifying 1) the  terms of the new request, 2) "MATCHING" for REQUEST_TYPE, and 3) the ASSIGNMENT_REF of  their original reservation in RELATED_REF. If the Primary Provider accepts the MATCHING request, the Primary Provider shall set the STATUS of the competing request to "REFUSED" and set the STATUS of the original, confirmed reservation to "DISPLACED". The STATUS of DISPLACED indicates that the original reservation has been displaced in its entirety.  If the original Customer does not elect to meet the terms of the competing request, the Primary  Transmission Provider shall displace the original reservation, in whole or in part, in the same manner  described for reservations that are not extended a right of first refusal.  Once the disposition of the original reservation and the competing request is finalized, the  COMPETING_REQUEST_FLAG shall be reset to "N" in the original reservation.

002-4.2.13.8	Deferral of Start of Service

The commencement of service for certain transmission reservations may be deferred by the Customer  as provided by the Primary Provider's Tariff. Such deferrals of the start of service are to be treated as  new requests. The Customer shall submit a new transmission reservation specifying 1) the new term of  service being requested, 2) "DEFERRAL" for REQUEST_TYPE and 3) the ASSIGNMENT_REF of  their original reservation in RELATED_REF. On approval of the request to defer the start of service,  the original reserved capacity may be subject to "recall" by the Primary Provider. If the Primary  Provider recalls all or a portion of the reserved MWs associated with the original request, the Primary  Provider shall increment the IMPACTED counter in the original reservation and document the  reduction in service via an appropriate OASIS posting viewable to the Customer with the reduction  Template.

002-4.2.13.9	Alternate POR/POD

Transmission Customers may have the right to move to alternate points of receipt and/or delivery under  the terms of the Primary Provider’s tariff. Customers holding confirmed transmission reservations may  request the use of alternate points of receipt and/or delivery by a new transmission reservation using  the transrequest Template. The new request shall specify 1) the terms of the new service requested, 2)  "REDIRECT" for the REQUEST_TYPE and 3) the ASSIGNMENT_REF of their original reservation  in RELATED_REF. On approval and confirmation of this new reservation, the Customer's rights to  schedule transmission service under their original reservation may be reduced. If transmission rights  under the original reservation are reduced, the Primary Provider shall increment the IMPACTED  counter in the original reservation and document the reduction in service via an appropriate OASIS  posting viewable to the Customer with the reduction Template.

002-4.2.13.10		Provider Recall

There are cases in implementing provisions of the Primary Provider's Tariff that the capacity reserved  by a Transmission Customer may be reduced in whole or in part. The particular reasons for these  reductions are Tariff specific. The Primary Provider shall provide a mechanism to post on OASIS any  such reductions or "recalls" in reserved capacity. The Customer shall be notified of any and all such  reductions in reserved capacity by the incrementing of the IMPACTED counter in association with  those reservations that are reduced; the IMPACTED flag is viewable with the transstatus Template.  Specific information regarding the exact nature of each reduction in the reserved capacity under a given  transmission reservation shall be posted and viewable with the reduction Template.   A specific example of a Primary Provider initiated recall of reserved capacity is the implementation of  a partial displacement of a transmission reservation. In this instance, the Customer has not elected (or  was not required to be offered) to match the terms of a higher priority, competing request. The Primary  Provider "recalls" that capacity necessary to accommodate the higher priority request from the original,  lower priority request. The IMPACTED counter of the original request is incremented, and a query  using the reduction Template for that original reservation would show the Customer the amount and  time-frame that the Customer's reserved capacity was recalled by the Primary Provider. (See sections  4.2.13.6 and 4.2.13.7.) Interruption of transmission service, where that interruption directly impacts the rights of the Customer  to schedule any service under that reservation, is another example of an impact to reserved capacity  that would be posted as a Primary Provider initiated recall of reserved capacity.   Secondary market sales of transmission rights are not examples of a Provider initiated recall of  reserved capacity, but the impact of any such sales shall also be returned in response to execution of the  reduction Template.

002-4.3	TEMPLATE DESCRIPTIONS

The following OASIS Templates define the Data Elements in fixed number and sequence which must  be provided for all data transfers to and from the OASIS Nodes. The definitions of the Data Elements  are listed in the Data Element Dictionary in Appendix A. TSIPs must provide a more detailed supplemental definition of the list of Sellers, Paths, Point of  Receipt (POR), Point of Delivery (POD), Capacity Types, Ancillary Service Types and Templates online,  clarifying how the terms are being used (see LIST Template). If POR and POD are not used, then Path Name must include directionality. Many of the Templates represent query-response interactions between the User and the OASIS Node.  These interactions are indicated by the "Query" and "Response" section respectively of each Template.  Some, as noted in their descriptions, are Input information, sent from the User to the OASIS Node. The  Response is generally a mirror of the Input, although in some Templates, the TSIP must add some  information.

002-4.3.1	Template Summary

The following table provides a summary of the process areas, and Templates to be used by Users to query information that will be downloaded or to upload information to the Primary Providers. These  processes define the functions that must be supported by an OASIS Node.

| Process Area | Process Name | Template(s) |
| --- | --- | --- |
| 4.3.2 Query/Response of Posted Services Being Offered | Query/Response Transmission Capacity Offerings | transoffering |
|  | Query/Response Ancillary Service Offerings | ancoffering |
| 4.3.3 Query/Response of Services Information | Query/Response Transmission Services | transserv |
|  | Query/Response Ancillary Services | ancserv |
| 4.3.4 Query/Response of Schedule details and Curtailments, Security Events, Reductions, and System Data | Query/Response Transmission Schedules and Curtailments | scheduledetail |
|  | Query/Response Security Events | security |
|  | Query/Response Reductions to Reserved Capacity | reduction |
|  | Query/Response Transmission System Data | systemdata |
| 4.3.5 Query/Response of Lists of Information | Query/Response List of Sellers, Paths, PORs, PODs, Capacity Types, Ancillary Service Types, Templates | list |
| 4.3.6 Purchase Transmission Services | Request Purchase of Transmission Services (Input) | transrequest |
|  | Query/Response Status of Transmission Service Request | transstatus |
|  | Seller Approves Purchase (Input) | transsell |
|  | Customer Confirm/Withdraw Purchase of Transmission Service (Input) | transcust |
|  | Seller Reassign Rights (Input) | transassign |
| 4.3.7 Seller Posting of Transmission Service | Seller Post Transmission Service for Sale (Input) | transpost |
|  | Seller Modify (Remove) Transmission Service for Sale (Input) | transupdate |
| 4.3.8 Purchase of Ancillary Service | Request Purchase of Ancillary Service (Input) | ancrequest |
|  | Query/Response Status of Ancillary Service Request | ancstatus |
|  | Seller Approves Purchase of Ancillary Service (Input) | ancsell |
|  | Customer Accept/Withdraw Purchase of Ancillary Service (Input) | anccust |
|  | Seller Reassign Rights (Input) | ancassign |
| 4.3.9 Seller Post Ancillary Service | Seller Post Ancillary Service (Input) | ancpost |
|  | Seller Modify (Remove) Ancillary Service for Sale (Input) | ancupdate |
| 4.3.10 Informal Messages | Post Want Ads (Input) |  | messagepost |
|  | Query/Response Want Ads | message |
|  | Delete Want Ad (Input) | messagedelete |
|  | Personnel Transfers | personnel |
|  | Discretion | discretion |
|  | Standards of Conduct | stdconduct |
| 4.3.11 Audit Log | Query/Response Audit Log | (various) |

002-4.3.2	Query/Response of Posted Services Being Offered

The following Templates define the information to be posted on services offered for sale. All discounts  for service negotiated by a Customer and Primary Provider (as Seller) at a price less than the currently  posted offering price shall be posted on OASIS Nodes in such a manner as to be viewed using these  Templates. All secondary market and/or third-party posting and Primary Provider offerings for like  services shall also be viewed using these Templates.  The Query must start with the standard header Query Variable Data Elements, listed in Section 4.2.6.2,  and may include any valid combination of the remaining Query Variables, shown below in the  Templates. START_TIME and STOP_TIME is the requested time interval for the Response to show  all offerings which intersect that interval (see Section 4.2.6.6). TIME_OF_LAST_UPDATE can be  used to specify all services updated since a specific point in time.  Query variable listed with an asterisk (*) can have at least 4 multiple instances defined by the user in  making the query.  In the Response, OFFER_START_TIME and OFFER_STOP_TIME indicate the "request time  window" within which a customer must request a service in order to get the posted OFFER_PRICE.  START_TIME and STOP_TIME indicate the time frame that the service is being offered for.  The SERVICE_DESCRIPTION Data Element shall define any attributes and/or special terms and  conditions applicable to the offering that are not listed under the standard SERVICE_DESCRIPTION  associated with the product definition supplied in the transserv or ancserv Templates.  SERVICE_DESCRIPTION shall be null if there are no unique attributes or terms associated with the  offering.

002-4.3.2.1	Transmission Capacity Offerings Available for Purchase (transoffering)

Transmission Services Offerings Available for Purchase (transoffering) is used to view transmission  services posted for sale by the Primary Provider or Resellers. At a minimum this Template must be  used to view each increment and type of service required to be offered under applicable regulations  and the Primary Provider's tariffs.  The POSTING_REF is set by the TSIP when an offering is posted and can be used in transrequest to  refer to a particular offering.  A User may query information about services available from all sellers for the time frame specified by  the SERVICE_INCREMENT Data Element, namely, hourly, daily, weekly, monthly, or yearly.

Template: transoffering

- Query

PATH_NAME*

SELLER_CODE*

SELLER_DUNS*

POINT_OF_RECEIPT*

POINT_OF_DELIVERY*

SERVICE_INCREMENT*

TS_CLASS*

TS_TYPE*

TS_PERIOD*

TS_WINDOW*

TS_SUBCLASS*

START_TIME (of transmission services)

STOP_TIME (of transmission services)

POSTING_REF

TIME_OF_LAST_UPDATE

- Response

The response is one or more records showing the requested service information. Note  that the Customer will receive as a series of records spanning all the SELLER_CODEs,  PATH_NAMEs, PORs, PODs, TS_xxx, and the START_TIME/STOP_TIME specified  in the query. The SALE_REF is a value provided by the SELLER to identify the  transmission service product being sold. The ANC_SVC_REQ indicates all ancillary  services required for the specified transmission services. All Template elements are  defined in the Data Element Dictionary.

TIME_OF_LAST_UPDATE

SELLER_CODE

SELLER_DUNS

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

INTERFACE_TYPE

OFFER_START_TIME

OFFER_STOP_TIME

START_TIME

STOP_TIME

CAPACITY (If null, then look in seller comments for information .)

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

ANC_SVC_REQ

SALE_REF

POSTING_REF

CEILING_PRICE

OFFER_PRICE

PRICE_UNITS

SERVICE_DESCRIPTION (if null, then look at transserv)

NERC_CURTAILMENT_PRIORITY

OTHER_CURTAILMENT_PRIORITY

SELLER_NAME

SELLER_PHONE

SELLER_FAX

SELLER_EMAIL

SELLER_COMMENTS

002-4.3.2.2	Ancillary Services Available for Purchase (ancoffering)

Ancillary Services Available for Purchase (ancoffering) is used to provide information regarding the  ancillary services that are available for sale by all sellers (both Primary Provider and Third Party  Sellers).

Template: ancoffering

- Query

SELLER_CODE*

SELLER_DUNS*

CONTROL_AREA*

SERVICE_INCREMENT*

AS_TYPE*

START_TIME

STOP_TIME

POSTING_REF

TIME_OF_LAST_UPDATE

- Response

TIME_OF_LAST_UPDATE

SELLER_CODE

SELLER_DUNS

CONTROL_AREA

OFFER_START_TIME

OFFER_STOP_TIME

START_TIME

STOP_TIME

CAPACITY

SERVICE_INCREMENT

AS_TYPE

SALE_REF

POSTING_REF

CEILING_PRICE

OFFER_PRICE

PRICE_UNITS

SERVICE_DESCRIPTION (if blank, then look at ancserv)

SELLER_NAME

SELLER_PHONE

SELLER_FAX

SELLER_EMAIL

SELLER_COMMENTS

002-4.3.3	Query/Response of Services Information

002-4.3.3.1	Transmission Services (transserv)

Transmission Services (transserv) is used to provide additional information regarding the transmission services SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_SUBCLASS, TS_WINDOW, NERC_CURTAILMENT_PRIORITY, and OTHER_CURTAILMENT_PRIORITY that are available for sale by a Provider in the Templates in Section 4.3.2. This Template is used to  summarize Provider tariff information for the convenience of the User. The Provider also sets  PRICE_UNITS with this Template.

Template: transserv

- Query

TIME_OF_LAST_UPDATE

- Response

TIME_OF_LAST_UPDATE

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

CEILING_PRICE

PRICE_UNITS

SERVICE_DESCRIPTION

NERC_CURTAILMENT_PRIORITY

OTHER_CURTAILMENT_PRIORITY

TARIFF_REFERENCE

002-4.3.3.2	Ancillary Services (ancserv)

Ancillary Services (ancserv) is used to provide additional information regarding the ancillary services that are available for sale by a Provider in the Templates in Section 4.3.2. This Template is used to summarize Provider tariff information for the convenience of the User. The Provider also sets PRICE_UNITS with this Template.

Template: ancserv

- Query

TIME_OF_LAST_UPDATE

- Response

TIME_OF_LAST_UPDATE

SERVICE_INCREMENT

AS_TYPE

CEILING_PRICE

PRICE_UNITS

SERVICE_DESCRIPTION

TARIFF_REFERENCE

002-4.3.4	Query/Response of Schedules and Curtailments, Security Events, Reductions,  and System Data

002-4.3.4.1	Transaction Schedule (scheduledetail)

Transaction Schedule (scheduledetail) provides information on the scheduled uses of the Provider’s transmission system and any curtailments or interruption thereof. Posting of transmission service  schedule information shall be in accordance with regulatory requirements, and reflect scheduled uses of  reserved capacity to a level of detail that such schedules are subject to a Provider’s application of  transmission security procedures and policies regarding curtailment and interruptions. There is no  restriction on the number of transaction schedule records that may refer to a given transmission  reservation at a given point in time.

The Query Variables ASSIGNMENT_REF, SELLER_CODE, SELLER_DUNS, CUSTOMER_CODE, CUSTOMER_DUNS, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, and  TS_PERIOD act to select those transmission reservations for which all applicable transaction schedule  information is to be returned. The PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY  Query Variables select all applicable interchange transaction schedule records that use the specified  path, point of receipt, and/or point of delivery. The TIME_OF_LAST_UPDATE, START_TIME, and STOP_TIME Query Variables select those particular interchange transaction schedule records updated  and/or effective: 1) on or after a particular point in time (START_TIME alone), 2) before a particular  point in time (STOP_TIME alone), or 3) between particular points in time (START_TIME and  STOP_TIME). The TRANSACTION_ID Query Variable selects all applicable schedule information records associated with that particular schedule. Note that the format of TRANSACTION_ID may be  Transmission Provider specific.

Each scheduledetail Template record returned in response to a query shall include information  associated with:

- information specifically related to the scheduled transaction,

- information from all applicable OASIS transmission reservations used to support the scheduled interchange transaction, and

- information related to any curtailment or interruption of service (if applicable), including a Transmission Provider’s refusal to accept or begin a Customer’s proposed interchange transaction for reliability or economic reasons (as allowed by the Provider’s Tariff).

Information to be supplied in each scheduledetail Template’s response records related to the scheduled  interchange are, SCHEDULE_REF, TRANSACTION_ID, PATH_NAME, POINT_OF_RECEIPT,  POINT_OF_DELIVERY, GCA_CODE, LCA_CODE, SOURCE, SINK, SCHEDULE_PRIORITY,  START_TIME, STOP_TIME, SCHEDULE_REQUESTED, and SCHEDULE_GRANTED.

The posting and availability of schedule and curtailment information on OASIS shall be in accordance with FERC Policy.

SCHEDULE_REF uniquely identifies a particular posting of schedule information. SCHEDULE_REF would vary with each record of data returned in response to a schedule query. TRANSACTION_ID, if applicable/available, contains a unique identifier associated with an interchange transaction that may  span multiple SCHEDULE_REF records. When available or applicable, the TRANSACTION_ID Data Element should reflect any industry-recognized transaction identifier rather than a Provider  specific internal identifier (e.g., the NERC electronic tagging “tag-id”). PATH_NAME,  POINT_OF_RECEIPT, and POINT_OF_DELIVERY identify the Transmission Provider’s specific  transmission resources used by the scheduled transaction, and would typically be identical to the  corresponding Data Elements associated with the OASIS transmission reservation used to support the  schedule. When known, the GCA_CODE and LCA_CODE identify the NERC registered Control Area  acronyms associated with the ultimate generation and load control areas respectively. When known or  required to more specifically identify the ultimate points of generation and load, the SOURCE and  SINK elements identify service points within the generation and load Control Areas respectively.  SCHEDULE_PRIORITY identifies the relative priority of this particular interchange transaction as  compared to all other scheduled transactions with respect to the application of curtailments or  interruptions. SCHEDULE_PRIORITY would typically reflect the curtailment priority Data Elements  associated with the OASIS transmission reservation used to support the schedule (i.e.,  NERC_CURTAILMENT_PRIORITY or OTHER_CURTAILMENT_PRIORITY). START_TIME  and STOP_TIME designate the particular time interval represented by this record associated with the  scheduled transaction. Note that multiple response records may be returned for a given scheduled  transaction when information associated with the schedule vary over time (e.g.,  SCHEDULE_REQUESTED, SCHEDULE_GRANTED, SCHEDULE_LIMIT, etc.), but that  scheduledetail Template response records for a given scheduled transaction should never overlap in  time. SCHEDULE_REQUESTED reflects the MW value requested to be scheduled by the Customer  during the hour, and SCHEDULE_GRANTED reflects the MW value actually scheduled by the  Transmission Provider at either the point of receipt or delivery, whichever is larger, over the  START_TIME/STOP_TIME time interval. When SCHEDULE_REQUESTED exceeds  SCHEDULE_GRANTED, a curtailment or interruption is in effect and additional information shall be  returned in the record.

Information in each scheduledetail Template’s response record related to the OASIS transmission  reservation(s) supporting the scheduled transaction includes ASSIGNMENT_REF, SELLER_CODE,  SELLER_DUNS, CUSTOMER_CODE, CUSTOMER_DUNS, AFFILIATE_FLAG,  SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_WINDOW, TS_SUBCLASS,  NERC_CURTAILMENT_PRIORITY, OTHER_CURTAILMENT_PRIORITY, and  CAPACITY_USED. Transaction schedules that are supported by the use of multiple OASIS  transmission reservations return the information attributable to each individual transmission reservation  using continuation records (i.e., records beginning with CONTINUATION_FLAG = ‘Y’). Each  continuation record shall also include the SCHEDULE_REF identifier from the first  (CONTINUATION_FLAG = ‘N’) record. CAPACITY_USED reflects the peak MW amount of the  reservation used to support the scheduled transaction; the sum of CAPACITY_USED over all  continuation records (if applicable) should equal the SCHEDULE_GRANTED.

Transaction schedules that were either “denied or interrupted” (ref. 18 CFR 37.6(a)(4)) shall include  information in the scheduledetail Template’s response related to the reason the transaction could not  be started or continued at the requested MW amount. The information returned shall include:  PROVIDER_ACTION, SCHEDULE_LIMIT, CURTAILMENT_OPTIONS, SECURITY_REF,  INITIATING_PARTY, RESPONSIBLE_PARTY, PROCEDURE_NAME, PROCEDURE_LEVEL,  FACILITY_LOCATION, FACILITY_NAME, FACILITY_CLASS, and FACILITY_LIMIT_TYPE. If  there are no restrictions to the scheduled transaction, these Data Elements shall all be returned as null.

PROVIDER_ACTION indicates the particular action taken by the Transmission Provider with respect  to the scheduled transaction; specific values to be returned are, DENIED if the schedule was not started  as requested, CURTAILED if the scheduled MW was limited for reliability reasons, or  INTERRUPTED if the scheduled MW was limited for economic reasons. SCHEDULE_LIMIT  reflects the maximum MW value over the START_TIME/STOP_TIME interval that the Provider has  determined can be scheduled. CURTAILMENT_OPTIONS defines any options the Customer may  exercise to reinstate all or part of the proposed schedule. SECURITY_REF, INITIATING_PARTY,  RESPONSIBLE_PARTY, PROCEDURE_NAME, PROCEDURE_LEVEL, FACILITY_NAME,  FACILITY_CLASS, and FACILITY_LIMIT_TYPE provide information related to the specific  transmission security event that prompted the Transmission Provider’s denial, curtailment or  interruption of the proposed scheduled transaction (see security Template).

Template: scheduledetail

- Query

PATH_NAME*

SELLER_CODE*

SELLER_DUNS*

CUSTOMER_CODE*

CUSTOMER_DUNS*

POINT_OF_RECEIPT*

POINT_OF_DELIVERY*

SERVICE_INCREMENT*

TS_CLASS*

TS_TYPE*

TS_PERIOD*

TS_WINDOW*

TS_SUBCLASS*

START_TIME

STOP_TIME

TIME_OF_LAST_UPDATE

ASSIGNMENT_REF

TRANSACTION_ID

- Response

CONTINUATION_FLAG

TIME_OF_LAST_UPDATE

SCHEDULE_REF

TRANSACTION_ID

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

GCA_CODE

LCA_CODE

SOURCE

SINK

SCHEDULE_PRIORITY

START_TIME

STOP_TIME

SCHEDULE_REQUESTED

SCHEDULE_GRANTED

ASSIGNMENT_REF

SELLER_CODE

SELLER_DUNS

CUSTOMER_CODE

CUSTOMER_DUNS

AFFILIATE_FLAG

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

NERC_CURTAILMENT_PRIORITY

OTHER_CURTAILMENT_PRIORITY

CAPACITY_USED

(if the transaction is subject to curtailment:)

PROVIDER_ACTION

SCHEDULE_LIMIT

CURTAILMENT_OPTIONS

SECURITY_REF

INITIATING_PARTY (e.g, CA/TP code)

RESPONSIBLE_PARTY (e.g., SC code)

PROCEDURE_NAME (e.g., "NERC TLR", or registered)

PROCEDURE_LEVEL (e.g., "2a", "3")

FACILITY_LOCATION (e.g, "INTERNAL" or

"EXTERNAL")

FACILITY_NAME

FACILITY_CLASS (e.g., transformer, etc.)

FACILITY_LIMIT_TYPE (e.g, thermal, stability, etc.)

002-4.3.4.2	Security Event (security)

Security Event (security) provides information on transmission security/reliability events that  may impact the Provider’s ability to schedule transactions. The TIME_OF_LAST_UPDATE,  START_TIME, and STOP_TIME Query Variables select those particular security event  postings updated and/or effective: 1) on or after a particular point in time (START_TIME  alone), 2) before a particular point in time (STOP_TIME alone), or 3) between particular  points in time (START_TIME and STOP_TIME).

The SECURITY_REF Data Element is a unique identifier assigned to each posting of  security related information; SECURITY_REF would vary with each record of data returned in  response to a security query. The EVENT_ID Data Element, when available, should reflect  any regional or interconnection-wide recognized security event identifier for events that are of  greater scope than those administered locally by the Provider (e.g., a NERC Security  Coordinator assigned identifier corresponding to a particular implementation of the NERC  TLR procedure). SECURITY_TYPE identifies the type of information posted for the event;  restricted values are OUTAGE for postings reflecting the state of critical transmission  facilities, and LIMIT for postings reflecting the implementation of security procedures to limit  or reduce scheduled transactions. The INITIATING_PARTY identifies by Control Area,  Security Coordinator or Transmission Provider code the entity calling for the “outage” or  “limit”, and RESPONSIBLE_PARTY identifies the entity (Control Area, Transmission  Provider, or Security Coordinator) responsible for administering any resulting security  procedure that may be instituted.

PROCEDURE_NAME and PROCEDURE_LEVEL reflect the specific security procedure and,  if applicable, the step, stage, or level within that procedure being implemented by  RESPONSIBLE_PARTY (e.g., NERC TLR is a recognized security procedure, and level “2a”  is a step within that procedure). FACILITY_NAME, FACILITY_CLASS, and  FACILITY_LIMIT_TYPE provide specific information related to the impacted transmission  facility. FACILITY_LOCATION identifies if the impacted facility is "INTERNAL" or  "EXTERNAL" relative to the Transmission Provider’s scope of authority over the named  facility.

START_TIME and STOP_TIME reflect the period of time encompassed by the particular  security event posted. In cases where a security procedure is invoked and then progresses  through various levels or stages, there shall be separate postings for each of those stages  declared by RESPONSIBLE_PARTY with START_TIME and STOP_TIME reflecting the  period of time each specific level of the procedure was in effect.

The use of the security Template to convey information related to major transmission facility  outages (SECURITY_TYPE = OUTAGE) is at the discretion of the Provider. Its definition in  this Template is intended to formalize the posting of facility outage information in an OASIS  Template structure where such information prior to implementation of this Template had  been posted in a free-form manner.

Template: security

- Query

START_TIME

STOP_TIME

TIME_OF_LAST_UPDATE

SECURITY_REF

EVENT_ID

SECURITY_TYPE

INITIATING_PARTY

RESPONSIBLE_PARTY

PROCEDURE_NAME

FACILITY_CLASS

FACILITY_LIMIT_TYPE

FACILITY_LOCATION

- Response

TIME_OF_LAST_UPDATE

SECURITY_REF

EVENT_ID

SECURITY_TYPE ("LIMIT" or "OUTAGE")

INITIATING_PARTY (e.g., CA/TP code)

RESPONSIBLE_PARTY (e.g., SC code)

PROCEDURE_NAME (e.g., "NERC TLR", or registered)

PROCEDURE_LEVEL (dependent on PROCEDURE_NAME)

FACILITY_CLASS (e.g., "FLOWGATE", "LINE", etc.)

FACILITY_LIMIT_TYPE (e.g., "THERMAL", "STABILITY", etc.)

FACILITY_LOCATION ("INTERNAL" or "EXTERNAL")

FACILITY_NAME (e.g., path or flowgate name)

START_TIME

STOP_TIME

002-4.3.4.3	Transmission Reservation Reduction (reduction)

The Transmission Reservation Reduction (reduction) Template provides information related  to the reduction in the Transmission Customer’s rights to schedule use of all or a portion of  capacity reserved for a given transmission reservation. Specific cases where such a  reduction in reserved capacity would be returned in response to this query Template include:  secondary market sales (as posted using the transassign or transsell Templates via the  REASSIGNED_REF, etc., Data Elements), a Transmission Provider’s interruption of the  reservation to accommodate higher priority reservations over the interruption interval (partial  displacement), etc.

The ASSIGNMENT_REF Query Variable is required and specifies the transmission  reservation whose reductions in reserved capacity (if any) are to be returned. The  START_TIME and STOP_TIME Query Variables allow the user to select the specific time  interval over which the reductions in reserved capacity are to be returned (e.g., return all  reductions in June for a year long reservation); by default all reductions over the life of the  reservation are returned.

In response to a reduction Template query, each primary record returned (CONTINUATION_FLAG = N) shall include the ASSIGNMENT_REF, CAPACITY_GRANTED  and CAPACITY_AVAILABLE in MWs over the interval from START_TIME to STOP_TIME.  CAPACITY_AVAILABLE is derived from the transmission reservation's CAPACITY_GRANTED less all reductions (if any) in reserved capacity over the interval from START_TIME to STOP_TIME as specified in the CAPACITY_REDUCED (as negative valued MWs) Data Element. The REDUCTION_TYPE, and REDUCTION_REASON Data Elements describe the circumstances and IMPACTING_REF references the associated transmission reservation (if applicable) that caused the reduction in capacity.

If no reductions in reserved capacity have been posted against the reservation,  CAPACITY_AVAILABLE will equal CAPACITY_GRANTED and the REDUCTION_TYPE,  REDUCTION_REASON, IMPACTING_REF and CAPACITY_REDUCED Data Elements will  be null. This response information is equivalent to the CAPACITY_GRANTED,  START_TIME, and STOP_TIME information that would be returned on execution of the  transstatus Template.

If the CAPACITY_AVAILABLE over the interval from START_TIME to STOP_TIME is the  result of more than one action reducing reserved capacity (e.g., multiple secondary market  sales for the same time period), each action reducing capacity will be returned in continuation  records (CONTINUATION_FLAG = Y) containing the ASSIGNMENT_REF,  REDUCTION_TYPE, REDUCTION_REASON, IMPACTING_REF and  CAPACITY_REDUCED Data Elements. If the action is another reservation (e.g. secondary  market sale) the REASSIGNED_CAPACITY from that reservation will be shown as a  negative value in CAPACITY_REDUCED.

Template: reduction

- Query

START_TIME

STOP_TIME

ASSIGNMENT_REF* (must be specified)

- Response

CONTINUATION_FLAG

ASSIGNMENT_REF

CAPACITY_GRANTED

CAPACITY_AVAILABLE

START_TIME

STOP_TIME

REDUCTION_TYPE (e.g., REDIRECT, INTERRUPTION, RESALE, DISPLACEMENT, etc.)

REDUCTION_REASON

IMPACTING_REF (if applicable)

CAPACITY_REDUCED

002-4.3.4.4	System Data (systemdata)

The System Data (systemdata) Template is used to query specific, time varying data that is  posted on a PATH, POINT_OF_RECEIPT, and/or POINT_OF_DELIVERY basis. The  SYSTEM_ATTRIBUTE Data Element defines the type of information returned in the  Template response. The restricted values for SYSTEM_ATTRIBUTE are,

- CBM – Capacity Benefit Margin

- TRM – Transmission Reliability Margin

- TTC – Total Transmission Capability

- NATC – Non-recallable (Firm) Available Transmission Capability

- RATC – Recallable (Non-firm) Available Transmission Capability

- A {registered} – Provider specific registered name for the data posted

Transmission Providers obligated to post values for one or more of the defined  SYSTEM_ATTRIBUTEs on specific transmission paths over time (e.g., hourly, then daily, etc.) as  called forth in FERC regulations shall return these posted values via the systemdata Template. If  SYSTEM_ATTRIBUTE is omitted in the query, then all attributes defined by the transmission  provider are returned, subject to the other query attributes constraints.. A given  SYSTEM_ATTRIBUTE may take on only one value at any given point in time. Note that TTC and  ATC information may also be viewed using the transoffering Template at the Transmission Provider's  discretion. Offers of service posted by Primary Providers as viewed with the transoffering Template  should reflect the applicable ATC(s) posted via systemdata in the CAPACITY Data Element.

Template: systemdata

- Query

PATH_NAME*

POINT_OF_RECEIPT*

POINT_OF_DELIVERY*

SYSTEM_ATTRIBUTE*

START_TIME

STOP_TIME

TIME_OF_LAST_UPDATE

- Response (acknowledgment)

POSTING_REF

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SYSTEM_ATTRIBUTE

START_TIME

STOP_TIME

ATTRIBUTE_VALUE

ATTRIBUTE_UNITS

TIME_OF_LAST_UPDATE

002-4.3.5	Query/Response of Lists of Information

002-4.3.5.1	List (list)

List (list) is used to provide lists of valid names. The minimum set of lists is LIST, SELLER_CODE,  PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SERVICE_INCREMENT,  TS_CLASS, TS_TYPE, TS_PERIOD, TS_SUBCLASS, TS_WINDOW,  NERC_CURTAILMENT_PRIORITY, REQUEST_TYPE, ANC_SERVICE_POINT,  FACILITY_CLASS, FACILITY_LIMIT_TYPE, PROCEDURE_NAME, SYSTEM_ATTRIBUTE,  SECURITY_TYPE, FACILITY_LOCATION, OTHER_CURTAILMENT_PRIORITY, AS_TYPE,  CATEGORY, and TEMPLATE. The information returned by the list Template may be used as values  for the associated OASIS Data Elements to query information, post or request services.

Template: list

- Query

LIST_NAME

TIME_OF_LAST_UPDATE

- Response

TIME_OF_LAST_UPDATE

LIST_NAME

LIST_ITEM

LIST_ITEM_DESCRIPTION

002-4.3.6	Purchase Transmission Services

The following Templates shall be used by Customers and Sellers to transact purchases of services.

002-4.3.6.1	Customer Capacity Purchase Request (transrequest)

The Customer Capacity Purchase Request (Input) (transrequest) is used by the Customer to request  the purchase of transmission services or request changes to previously submitted reservations for  transmission services. The response simply acknowledges that the Customer's request was received by  the OASIS Node. It does not imply that the Seller has received the request. Inputting values into the  reference Data Elements is optional.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection  used to input the request.

Supporting "profiles" of service, which request different capacities (and  optionally price) for different time periods within a single request, is at the  discretion of the Primary Provider. Continuation records may be used to indicate  requests for these service profiles; use of continuation records is only supported  when using the CSV Format upload of Template data. Each segment of a profile  is represented by the Data Elements CAPACITY_REQUESTED,  START_TIME, and STOP_TIME, which define the intervals in time overwhich  a non-zero MW demand is being requested. The initial segment of a profile is  defined by the CAPACITY_REQUESTED, START_TIME and STOP_TIME Data Elements specified in the first/only record submitted; subsequent segments  are specified in continuation records each containing the appropriate CAPACITY_REQUESTED, START_TIME and STOP_TIME values defining  the segment. Provider's may optionally support price negotiation on segments of  a profiled reservation request. In this case, the BID_PRICE Data Element is also  included in each continuation record. If the BID_PRICE Data Element is not  specified in the continuation records, the BID_PRICE specified in the first/only  record submitted will be applied to the entire reservation request.

For requesting transmission services which include multiple paths, the following fields may be  specified using continuation records: PATH_NAME, POINT_OF_RECEIPT, and  POINT_OF_DELIVERY. Supporting multiple paths or multiple POINT_OF_RECEIPT and  POINT_OF DELIVERY is at the discretion of the Provider.

The START_TIME and STOP_TIME indicate the requested period of service.

When the request is received at the OASIS Node, the TSIP assigns a unique ASSIGNMENT_REF  value and queues the request with a time stamp. The STATUS for the request is QUEUED. The  IMPACTED counter is initially set to 0. If the new request is not modifying an existing reservation (as  indicated by a null value for the RELATED_REF Data Element) and the SELLER is the Primary  Provider, REQUEST_TYPE must either be specified as "ORIGINAL" or be left null and OASIS will  substitute the default value of "ORIGINAL". If the new request is not modifying an existing reservation  and the SELLER is not the Primary Provider, REQUEST_TYPE must either be specified as  "RESALE" or be left null and OASIS will substitute the default value of "RESALE".

If the new request is modifying an existing transmission reservation, the Data Elements  REQUEST_TYPE and RELATED_REF must be entered. RELATED_REF contains the  ASSIGNMENT_REF for the transmission reservation being modified, and REQUEST_TYPE must be  one of MATCHING, REDIRECT, DEFERRAL, RENEWAL, or a Primary Provider registered value.

Specification of a value YES in the PRECONFIRMED field authorizes the TSIP to automatically  change the STATUS field in the transstatus Template to CONFIRMED when that request is  ACCEPTED by the Seller.

Template: transrequest

- Input

CONTINUATION_FLAG

SELLER_CODE (Primary or Reseller)

SELLER_DUNS

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SOURCE

SINK

CAPACITY_REQUESTED

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

STATUS_NOTIFICATION

START_TIME

STOP_TIME

BID_PRICE

PRECONFIRMED

ANC_SVC_LINK

POSTING_REF (Optionally set by Customer)

SALE_REF (Optionally set by Customer)

REQUEST_REF (Optionally set by Customer)

DEAL_REF (Optionally set by Customer)

CUSTOMER_COMMENTS

REQUEST_TYPE (Required for request changes)

RELATED_REF (Required for request changes)

- Response (acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF (assigned by TSIP)

SELLER_CODE

SELLER_DUNS

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SOURCE

SINK

CAPACITY_REQUESTED

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

STATUS_NOTIFICATION

START_TIME

STOP_TIME

BID_PRICE

PRECONFIRMED

ANC_SVC_LINK

POSTING_REF

SALE_REF

REQUEST_REF

DEAL_REF

CUSTOMER_COMMENTS

REQUEST_TYPE

RELATED_REF

ERROR_MESSAGE

002-4.3.6.2	Status of Customer Purchase Request (transstatus)

The Status of Customer Purchase Request (transstatus) is provided upon the request of any Customer or Provider to indicate the current status of one or more reservation records. Users may also view any transaction's status. However, the SOURCE and SINK may be masked for User requests until Transmission Providers must make source and sink information available at the time the request status posting is updated to show that a transmission request is confirmed.

Continuation records may be returned in association with a transmission reservation to convey information regarding: 1) sale or assignment of transmission rights on the secondary market (reassignments), 2) profiled requests, or 3) service over multiple paths Each continuation record associated with a transmission reservation shall be identified by the CONTINUATION_FLAG Data Element set to 'Y' and include the ASSIGNMENT_REF Data Element.

When a transmission reservation request acquires its rights to transmission service as the result of a sale or assignment of transmission rights on the secondary market, the identity of the original reservation, capacity, and time interval over which rights are assigned to the new reservation are defined by the Data Elements REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. These Data Elements will be returned in continuation records when more than one set of reassignment information is associated with a reservation.

If the transmission reservation has an associated profile, either as a result of the submission of CAPACITY_REQUESTED varying over time (support for Customer reservation profiles is at the discretion of the Provider) or due to the Provider offering partial service specifying a CAPACITY_GRANTED varying over time, then CAPACITY_GRANTED, CAPACITY_REQUESTED, START_TIME and STOP_TIME for the segments of the profile will be returned in continuation records. If the Provider supports negotiation of price on each segment of a Customer profiled request, BID_PRICE and OFFER_PRICE will also be returned with CAPACITY_REQUESTED, CAPACITY_GRANTED, START_TIME and STOP_TIME.

If the Provider supports reservations submitted on multiple paths, continuation records specifying PATH_NAME, POINT_OF_RECEIPT, and POINT_OF_DELIVERY associated with the reservation would be returned in continuation records.

The AFFILIATE_FLAG will be set by the TSIP to indicate whether or not the Customer is an affiliate of the Primary Provider. The NEGOTIATED_PRICE_FLAG will be set by the TSIP to indicate whether the OFFER_PRICE is higher, lower, or the same as the BID_PRICE. Any time that a confirmed transmission reservation's rights to schedule up to the amount of CAPACITY_GRANTED is reduced, either due to secondary market sales, partial displacements, Provider initiated "recalls" of capacity, etc., the IMPACTED Data Element shall be incremented. Specific information regarding the MW level and reason for reduction in reserved capacity is viewable using the reduction Template.

Template: transstatus

- Query

SELLER_CODE*

SELLER_DUNS*

CUSTOMER_CODE*

CUSTOMER_DUNS*

PATH_NAME*

POINT_OF_RECEIPT*

POINT_OF_DELIVERY*

SERVICE_INCREMENT*

TS_CLASS*

TS_TYPE*

TS_PERIOD*

TS_WINDOW*

TS_SUBCLASS*

STATUS*

START_TIME (Beginning time of service)

STOP_TIME

START_TIME_QUEUED (Beginning time queue)

STOP_TIME_QUEUED

NEGOTIATED_PRICE_FLAG

ASSIGNMENT_REF

REASSIGNED_REF

RELATED_REF

SALE_REF

REQUEST_REF

DEAL_REF

COMPETING_REQUEST_FLAG

TIME_OF_LAST_UPDATE

- Response

CONTINUATION_FLAG

ASSIGNMENT_REF

SELLER_CODE

SELLER_DUNS

CUSTOMER_CODE

CUSTOMER_DUNS

AFFILIATE_FLAG (Set by TSIP)

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SOURCE

SINK

CAPACITY_REQUESTED

CAPACITY_GRANTED

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

NERC_CURTAILMENT_PRIORITY

OTHER_CURTAILMENT_PRIORITY

START_TIME

STOP_TIME

CEILING_PRICE

OFFER_PRICE

BID_PRICE

PRICE_UNITS

PRECONFIRMED

ANC_SVC_LINK

ANC_SVC_REQ

POSTING_REF

SALE_REF

REQUEST_REF

DEAL_REF

IMPACTED (Greater than 0, if another reservation impacts this reservation)

COMPETING_REQUEST_FLAG

REQUEST_TYPE

ORIGINAL, RESALE, REDIRECT, MATCHING,DEFERRAL, RENEWAL, {registered}

RELATED_REF

NEGOTIATED_PRICE_FLAG ("L" if Seller accepted Price is lower than OFFER_PRICE in transoffering Template; "H" if higher; otherwise blank)

STATUS =

RECEIVED, QUEUED, INVALID, STUDY, REBID, COUNTEROFFER, ACCEPTED, DECLINED, SUPERSEDED, REFUSED, CONFIRMED, WITHDRAWN, DISPLACED, ANNULLED, RETRACTED

STATUS_NOTIFICATION

STATUS_COMMENTS

TIME_QUEUED

RESPONSE_TIME_LIMIT

TIME_OF_LAST_UPDATE

PRIMARY_PROVIDER_COMMENTS

SELLER_REF

SELLER_COMMENTS

CUSTOMER_COMMENTS

SELLER_NAME

SELLER_PHONE

SELLER_FAX

SELLER_EMAIL

CUSTOMER_NAME

CUSTOMER_PHONE

CUSTOMER_FAX

CUSTOMER_EMAIL

REASSIGNED_REF

REASSIGNED_CAPACITY (Capacity from each previous transaction)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

002-4.3.6.3	Seller Approval of Purchase (transsell)

Seller Approval of Purchase (Input) (transsell) is input by a Seller to modify the status and queue of a request by a Customer.

The following fields may be submitted in continuation records for the transsell Template to convey transmission rights from multiple original transmission reservations to this new reservation: REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. Use of continuation records is only supported when using the CSV format upload of Template data.

If the Provider/Seller cannot accommodate the Customer's CAPACITY_REQUESTED and is obligated or elects to offer the Customer partial service that varies over the total period of the reservation, CAPACITY_GRANTED, START_TIME and STOP_TIME Data Elements may be repeated in continuation records.

If the Provider/Seller supports the negotiation of price on individual segments of a profiled reservation request (support for reservation profiles is at the discretion of the Provider), OFFER_PRICE, START_TIME and STOP_TIME Data Elements may be submitted in continuation records to modify the Seller's offer price associated with the profile segment(s) corresponding to START_TIME and STOP_TIME. OFFER_PRICE associated with each segment of a profiled request must match the corresponding BID_PRICE for the reservation request's STATUS to be set to ACCEPTED.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request. The SELLER_REF Data Element may be set by the SELLER to a seller specific internal tracking number.

If the reservation is subject to the right of first refusal pending a status change to Displaced, the COMPETING_REQUEST_FLAG shall be set to Y, and SELLER_COMMENTS shall be updated with a reference to the competing request’s ASSIGNMENT_REF. If the reservation is subject to the right of first refusal pending a status change to Superseded, the COMPETING_REQUEST_FLAG shall be set to Y, the OFFER_PRICE shall be updated, the SELLER_COMMENTS shall be updated with a reference to the competing requests ASSIGNMENT_REF, and the STATUS shall be set to COUNTEROFFER. Once the disposition of the request is finalized, the COMPETING_REQUEST_FLAG shall be reset to N and any appropriate status change shall be made.

The Seller may accept a reservation only when the BID_PRICE and the OFFER_PRICE are the same.

Template: transsell

- Input

CONTINUATION_FLAG

ASSIGNMENT_REF (Required)

START_TIME

STOP_TIME

OFFER_PRICE

CAPACITY_GRANTED

STATUS =

RECEIVED, INVALID, STUDY, COUNTEROFFER, ACCEPTED, REFUSED, SUPERSEDED, DECLINED, ANNULLED, RETRACTED, DISPLACED

STATUS_COMMENTS

ANC_SVC_LINK

ANC_SVC_REQ

COMPETING_REQUEST_FLAG

NEGOTIATED_PRICE_FLAG

SELLER_REF

SELLER_COMMENTS

RESPONSE_TIME_LIMIT

REASSIGNED_REF

REASSIGNED_CAPACITY (Previous capacity to be reassigned)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

- Response

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF

START_TIME

STOP_TIME

OFFER_PRICE

CAPACITY_GRANTED

STATUS =

RECEIVED, INVALID, STUDY, COUNTEROFFER, ACCEPTED, REFUSED, SUPERSEDED, DECLINED, ANNULLED, RETRACTED, DISPLACED

STATUS_COMMENTS

ANC_SVC_LINK

ANC_SVC_REQ

COMPETING_REQUEST_FLAG

NEGOTIATED_PRICE_FLAG

SELLER_REF

SELLER_COMMENTS

RESPONSE_TIME_LIMIT

REASSIGNED_REF

REASSIGNED_CAPACITY (Previous capacity to be reassigned)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

ERROR_MESSAGE

002-4.3.6.4	Customer Confirmation of Purchase (Input) (transcust)

Customer Confirmation of Purchase (Input) (transcust) is input by the Customer to state his agreement or withdrawal of a purchase after the Seller has indicated that the purchase request is approved.  Only the BID_PRICE, STATUS, STATUS_COMMENTS, ANC_SVC_LINK, and CUSTOMER_COMMENTS Data Elements can be modified in this Template.

The PRECONFIRMED Data Element may only be set to a value of 'Y' using this Template. Once the Customer has set PRECONFIRMED to 'Y', either on the original submission of the transrequest Template or via this Template, its value cannot be reset to 'N'.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection used to input the request.

The Customer must change the BID_PRICE to be equal to the OFFER_PRICE before the reservation request's STATUS can be set to CONFIRMED.

If the Provider/Seller supports the negotiation of price on individual segments of a profiled reservation request (support for reservation profiles is at the discretion of the Provider), BID_PRICE, START_TIME and STOP_TIME Data Elements may be submitted in continuation records to modify the Customer's bid price associated with the profile segment(s) corresponding to START_TIME and STOP_TIME.  BID_PRICE associated with each segment of a profiled request must match the corresponding OFFER_PRICE for the reservation request's STATUS to be set to CONFIRMED.

Template: transcust

- Input

CONTINUATION_FLAG

ASSIGNMENT_REF (Required)

START_TIME

STOP_TIME

REQUEST_REF

DEAL_REF

BID_PRICE

PRECONFIRMED

STATUS=

REBID, CONFIRMED, WITHDRAWN

STATUS_COMMENTS

ANC_SVC_LINK

STATUS_NOTIFICATION If left blank, then original URL from the transrequest will be used

CUSTOMER_COMMENTS

- Response

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF

START_TIME

STOP_TIME

REQUEST_REF

DEAL_REF

BID_PRICE

PRECONFIRMED

STATUS=

REBID, CONFIRMED, WITHDRAWN

STATUS_COMMENTS

ANC_SVC_LINK

STATUS_NOTIFICATION

CUSTOMER_COMMENTS

ERROR_MESSAGE

002-4.3.6.5	Seller to Reassign Service Rights to Another Customer (transassign)

Seller to Reassign Service Rights to Another Customer (Input) (transassign) is used by the seller to ask the Transmission Services Information Provider to reassign some or all of the seller's rights to Services to another Customer, for seller confirmed transactions that have occurred off the OASIS Node. The TSIP shall assign a unique ASSIGNMENT_REF in the response (acknowledgment) and enter the status CONFIRMED as viewed in the transstatus Template. SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Only the following fields may be redefined in a continuation record for the transassign input Template: CAPACITY_REQUESTED, CAPACITY_GRANTED, START_TIME, STOP_TIME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. The REQUEST_TYPE of "RESALE" is implied through execution of this Template.

Template: transassign

- Input

CONTINUATION_FLAG

CUSTOMER_CODE

CUSTOMER_DUNS

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SOURCE

SINK

CAPACITY_REQUESTED

CAPACITY_GRANTED

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

START_TIME

STOP_TIME

OFFER_PRICE

ANC_SVC_LINK (optional: filled in if assignment is different than original transmission reservation)

POSTING_NAME

REASSIGNED_REF

REASSIGNED_CAPACITY (Capacity being sold from each previous assignment)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

SELLER_COMMENTS

SELLER_REF

- Response (acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF (assigned by TSIP)

CUSTOMER_CODE

CUSTOMER_DUNS

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

SOURCE

SINK

CAPACITY_REQUESTED

CAPACITY_GRANTED (Total capacity being reassigned)

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

START_TIME

STOP_TIME

OFFER_PRICE

ANC_SVC_LINK

POSTING_NAME

REASSIGNED_REF

REASSIGNED_CAPACITY (Capacity being sold from each previous assignment)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

SELLER_COMMENTS

SELLER_REF

ERROR_MESSAGE

002-4.3.7	Seller Posting of Transmission Services

Sellers shall use the following Templates for providing sell information. They may aggregate portions of several previous purchases to create a new service, if this capability is provided by the Transmission Services Information Provider:

002-4.3.7.1	Seller Capacity Posting (transpost)

Seller Capacity Posting (Input) (transpost) shall be used by the Seller to post the transmission capacity for resale on to the OASIS Node.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: transpost

- Input

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

INTERFACE_TYPE

CAPACITY

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

ANC_SVC_REQ

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

SALE_REF

OFFER_PRICE

SERVICE_DESCRIPTION

SELLER_COMMENTS

- Response (Acknowledgment)

RECORD_STATUS

POSTING_REF (Assigned by TSIP)

PATH_NAME

POINT_OF_RECEIPT

POINT_OF_DELIVERY

INTERFACE_TYPE

CAPACITY

SERVICE_INCREMENT

TS_CLASS

TS_TYPE

TS_PERIOD

TS_WINDOW

TS_SUBCLASS

ANC_SVC_REQ

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

SALE_REF

OFFER_PRICE

SERVICE_DESCRIPTION

SELLER_COMMENTS

ERROR_MESSAGE

002-4.3.7.2	Seller Capacity Modify (transupdate)

Seller Capacity Modify (Input) (transupdate) shall be used by a Seller to modify a posting of transmission capacity.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: transupdate

- Input

POSTING_REF (Must be provided)

CAPACITY (only if modified)

START_TIME (only if modified)

STOP_TIME (only if modified)

OFFER_START_TIME (only if modified)

OFFER_STOP_TIME(only if modified)

ANC_SVC_REQ (only if modified)

SALE_REF (only if modified)

OFFER_PRICE (only if modified)

SERVICE_DESCRIPTION (only if modified)

SELLER_COMMENTS (only if modified)

- Response (acknowledgment)

RECORD_STATUS

POSTING_REF

CAPACITY

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

ANC_SVC_REQ

SALE_REF

OFFER_PRICE

SERVICE_DESCRIPTION

SELLER_COMMENTS

ERROR_MESSAGE

002-4.3.8	Purchase of Ancillary Services

002-4.3.8.1	Customer Requests to Purchase Ancillary Services (ancrequest)

Customer Requests to Purchase Ancillary Services (ancrequest) (Input, Template Upload) is used by the customer to request ancillary services that have been posted by a seller of those services. The response simply acknowledges that the Customer's request was received by the OASIS Node. It does not imply that the Seller has received the request. The same requirements exist for the use of STATUS_NOTIFICATION as for transrequest. Submitting values into the reference Data Elements is optional.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection used to input the request.

Supporting "profiles" of ancillary service, which request different capacities (and optionally price) for different time periods within a single request, is at the discretion of the Primary Provider. Continuation records may be used to indicate requests for these service profiles. Each segment of a profile is represented by the Data Elements CAPACITY, START_TIME, and STOP_TIME, which define the intervals in time overwhich a non-zero MW demand is being requested. The initial segment of a profile is defined by the CAPACITY, START_TIME and STOP_TIME Data Elements specified in the first/only record submitted; subsequent segments are specified in continuation records each containing the appropriate CAPACITY, START_TIME and STOP_TIME values defining the segment. Provider's may optionally support price negotiation on segments of a profiled reservation request. In this case, the BID_PRICE Data Element is also included in each continuation record. If the BID_PRICE Data Element is not specified in the continuation records, the BID_PRICE specified in the first/only record submitted will be applied to the entire reservation request.

The START_TIME and STOP_TIME indicate the requested period of service.

When the request is received at the OASIS Node, the TSIP assigns a unique ASSIGNMENT_REF value and queues the request with a time stamp. The STATUS for the request is QUEUED.

Specification of a value YES in the PRECONFIRMED field authorizes the TSIP to automatically change the STATUS field in the ancstatus Template to CONFIRMED when that request is ACCEPTED by the Seller.

Template: ancrequest

- Input

CONTINUATION_FLAG

SELLER_CODE

SELLER_DUNS

CONTROL_AREA

ANC_SERVICE_POINT

CAPACITY

SERVICE_INCREMENT

AS_TYPE

STATUS_NOTIFICATION

START_TIME

STOP_TIME

BID_PRICE

PRECONFIRMED

POSTING_REF (Optionally set by Customer)

SALE_REF (Optionally set by Customer)

REQUEST_REF (Optionally set by Customer)

DEAL_REF (Optionally set by Customer)

CUSTOMER_COMMENTS

- Response (acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF (assigned by TSIP)

SELLER_CODE

SELLER_DUNS

CONTROL_AREA

ANC_SERVICE_POINT

CAPACITY

SERVICE_INCREMENT

AS_TYPE

STATUS_NOTIFICATION

START_TIME

STOP_TIME

BID_PRICE

PRECONFIRMED

POSTING_REF

SALE_REF

REQUEST_REF

DEAL_REF

CUSTOMER_COMMENTS

ERROR_MESSAGE

002-4.3.8.2	Ancillary Services Status (ancstatus)

Ancillary Services Status (ancstatus) is used to provide the status of purchase requests regarding the ancillary services that are available for sale by all Service Providers. Continuation records may be returned in association with a ancillary services reservation to convey information regarding: 1) sale or assignment of ancillary rights on the secondary market (reassignments), or 2) profiled requests. When an ancillary reservation request is the result of a sale or assignment of transmission or ancillary rights on the secondary market, the identity of the original reservation, capacity, and time interval over which rights are assigned to the new reservation are defined by the Data Elements REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. These Data Elements will be returned in continuation records when more than one set of reassignment information is associated with a reservation. If the reservation has an associated profile (support for reservation profiles is at the discretion of the Provider), CAPACITY, START_TIME and STOP_TIME for the segments of the profile will be returned in continuation records. If the Provider supports negotiation of price on each segment of a profiled request, BID_PRICE and OFFER_PRICE will also be returned with CAPACITY, START_TIME and STOP_TIME.

The AFFILIATE_FLAG will be set by the TSIP to indicate whether or not the Customer is an affiliate of the Seller.

The values of STATUS and processes for setting STATUS are the same as for transstatus.

Template: ancstatus

- Query

SELLER_CODE*

SELLER_DUNS*

CUSTOMER_CODE*

CUSTOMER_DUNS*

CONTROL_AREA

ANC_SERVICE_POINT

SERVICE_INCREMENT

AS_TYPE

STATUS

START_TIME

STOP_TIME

START_TIME_QUEUED

STOP_TIME_QUEUED

NEGOTIATED_PRICE_FLAG

ASSIGNMENT_REF

REASSIGNED_REF

SALE_REF

REQUEST_REF

DEAL_REF

TIME_OF_LAST_UPDATE (only if TIME_OF_LAST_UPDATE is posted by record)

- Response

CONTINUATION_FLAG

ASSIGNMENT_REF

SELLER_CODE

SELLER_DUNS

CUSTOMER_CODE

CUSTOMER_DUNS

AFFILIATE_FLAG (Set by TSIP)

CONTROL_AREA

ANC_SERVICE_POINT

CAPACITY

SERVICE_INCREMENT

AS_TYPE

START_TIME

STOP_TIME

CEILING_PRICE

OFFER_PRICE

BID_PRICE

PRICE_UNITS

PRECONFIRMED

POSTING_REF

SALE_REF

REQUEST_REF

DEAL_REF

NEGOTIATED_PRICE_FLAG ("L" if Seller accepted Price is lower than OFFER_PRICE in ancoffering Template; "H" if higher; otherwise blank)

STATUS=

QUEUED, INVALID, RECEIVED, STUDY, REBID, COUNTEROFFER, ACCEPTED, REFUSED, CONFIRMED, WITHDRAWN, SUPERSEDED, DECLINED, ANNULLED, RETRACTED, DISPLACED

STATUS_NOTIFICATION

STATUS_COMMENTS

TIME_QUEUED

RESPONSE_TIME_LIMIT

TIME_OF_LAST_UPDATE

PRIMARY_PROVIDER_COMMENTS

SELLER_COMMENTS

CUSTOMER_COMMENTS

SELLER_NAME

SELLER_PHONE

SELLER_FAX

SELLER_EMAIL

CUSTOMER_NAME

CUSTOMER_PHONE

CUSTOMER_FAX

CUSTOMER_EMAIL

REASSIGNED_REF

REASSIGNED_CAPACITY

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

002-4.3.8.3	Seller Approves Ancillary Service (ancsell)

Seller Approves Ancillary Service (ancsell) is used by the Seller to confirm acceptance after the Seller has approved the purchase of ancillary service.

The following fields may be submitted in continuation records for the ancsell Template to convey ancillary rights from multiple original ancillary service reservations to this new reservation: REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. If the Provider/Seller supports the negotiation of price on individual segments of a profiled reservation request (support for reservation profiles is at the discretion of the Provider), OFFER_PRICE, START_TIME and STOP_TIME Data Elements may be submitted in continuation records to modify the Seller's offer price associated with the profile segment(s) corresponding to START_TIME and STOP_TIME. OFFER_PRICE associated with each segment of a profiled request must match the corresponding BID_PRICE for the reservation request's STATUS to be set to ACCEPTED.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: ancsell

- Input

CONTINUATION_FLAG

ASSIGNMENT_REF (Required)

START_TIME

STOP_TIME

OFFER_PRICE

STATUS =

INVALID, RECEIVED, STUDY, COUNTEROFFER, SUPERSEDED, ACCEPTED, REFUSED, DECLINED, ANNULLED, RETRACTED, DISPLACED

STATUS_COMMENTS

NEGOTIATED_PRICE_FLAG

RESPONSE_TIME_LIMIT

SELLER_COMMENTS

REASSIGNED_REF

REASSIGNED_CAPACITY

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

- Response (acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF

START_TIME

STOP_TIME

OFFER_PRICE

STATUS =

INVALID, RECEIVED, STUDY, COUNTEROFFER, SUPERSEDED, ACCEPTED, REFUSED, DECLINED, ANNULLED, RETRACTED, DISPLACED

STATUS_COMMENTS

NEGOTIATED_PRICE_FLAG

RESPONSE_TIME_LIMIT

SELLER_COMMENTS

REASSIGNED_REF

REASSIGNED_CAPACITY

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

ERROR_MESSAGE

002-4.3.8.4	Customer accepts Ancillary Service (anccust)

Customer accepts Ancillary Service (anccust) is used by the customer to confirm acceptance after the seller has approved the purchase of ancillary service.

The Customer must change the BID_PRICE to be equal to the OFFER_PRICE before the reservation request's STATUS can be set to CONFIRMED. If the Provider/Seller supports the negotiation of price on individual segments of a profiled reservation request (support for reservation profiles is at the discretion of the Provider), BID_PRICE, START_TIME and STOP_TIME Data Elements may be submitted in continuation records to modify the Customer's bid price associated with the profile segment(s) corresponding to START_TIME and STOP_TIME. BID_PRICE associated with each segment of a profiled request must match the corresponding OFFER_PRICE for the reservation request's STATUS to be set to CONFIRMED.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection used to input the request.

Template: anccust

- Input

CONTINUATION_FLAG

ASSIGNMENT_REF (Required)

START_TIME

STOP_TIME

REQUEST_REF

DEAL_REF

BID_PRICE

PRECONFIRMED

STATUS=

REBID, CONFIRMED, WITHDRAWN

STATUS_COMMENTS

STATUS_NOTIFICATION (If left blank, then the original URL from the ancrequest will be used

CUSTOMER_COMMENTS

- Response (Acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF

START_TIME

STOP_TIME

REQUEST_REF

DEAL_REF

BID_PRICE

PRECONFIRMED

STATUS =

REBID, CONFIRMED, WITHDRAWN

STATUS_COMMENTS

STATUS_NOTIFICATION

CUSTOMER_COMMENTS

ERROR_MESSAGE

002-4.3.8.5	Seller to Reassign Service Rights to Another Customer (ancassign)

Seller to Reassign Service Rights to Another Customer (Input) (ancassign) is used by the seller to ask the Transmission Services Information Provider to reassign some or all of the seller's rights to Services to another Customer, for seller confirmed transactions that have occurred off the OASIS Node.

Implementation of this Template is optional until such time that a business case requiring the use of such a facility to selectively reassign ancillary services is clearly demonstrated.

The TSIP shall assign a unique ASSIGNMENT_REF in the response (acknowledgment) and enter the status CONFIRMED as viewed in the ancstatus Template.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Only the following fields may be redefined in a continuation record for the ancassign input Template:  CAPACITY, START_TIME, STOP_TIME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: ancassign

- Input

CONTINUATION_FLAG

CUSTOMER_CODE

CUSTOMER_DUNS

CONTROL_AREA

ANC_SERVICE_POINT

CAPACITY

SERVICE_INCREMENT

AS_TYPE

START_TIME

STOP_TIME

OFFER_PRICE

POSTING_NAME

REASSIGNED_REF

REASSIGNED_CAPACITY (Capacity being sold from each previous assignment)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

SELLER_COMMENTS

- Response (acknowledgment)

RECORD_STATUS

CONTINUATION_FLAG

ASSIGNMENT_REF (assigned by TSIP)

CUSTOMER_CODE

CUSTOMER_DUNS

CONTROL_AREA

ANC_SERVICE_POINT

CAPACITY (Total capacity being reassigned)

SERVICE_INCREMENT

AS_TYPE

START_TIME

STOP_TIME

OFFER_PRICE

POSTING_NAME

REASSIGNED_REF

REASSIGNED_CAPACITY (Capacity being sold from each previous assignment)

REASSIGNED_START_TIME

REASSIGNED_STOP_TIME

SELLER_COMMENTS

ERROR_MESSAGE

002-4.3.9	Seller Posting of Ancillary Services

002-4.3.9.1	Seller Ancillary Services Posting (ancpost)

Seller Ancillary Services Posting (ancpost) is used by the Seller to post information regarding the different services that are available for sale by third party Sellers of ancillary services.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: ancpost

- Input

CONTROL_AREA

SERVICE_DESCRIPTION

CAPACITY

SERVICE_INCREMENT

AS_TYPE

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

SALE_REF

OFFER_PRICE

SELLER_COMMENTS

- Response (acknowledgment)

RECORD_STATUS

POSTING_REF (Assigned by TSIP)

CONTROL_AREA

SERVICE_DESCRIPTION

CAPACITY

SERVICE_INCREMENT

AS_TYPE

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

SALE_REF

OFFER_PRICE

SELLER_COMMENTS

ERROR_MESSAGE

002-4.3.9.2	Seller Modify Ancillary Services Posting (ancupdate)

Seller Modify Ancillary Services Posting (ancupdate) is used by the Seller to modify posted information regarding ancillary services that are available for sale by a third party Seller.

SELLER_CODE and SELLER_DUNS shall be determined from the registered connection used to input the request.

Template: ancupdate

- Input

POSTING_REF (Required)

CAPACITY (only if modified)

SERVICE_DESCRIPTION (only if modified)

START_TIME (only if modified)

STOP_TIME (only if modified)

OFFER_START_TIME (only if modified)

OFFER_STOP_TIME (only if modified)

SALE_REF (only if modified)

OFFER_PRICE (only if modified)

SELLER_COMMENTS (only if modified)

- Response (acknowledgment)

RECORD_STATUS

POSTING_REF

CAPACITY

SERVICE_DESCRIPTION

START_TIME

STOP_TIME

OFFER_START_TIME

OFFER_STOP_TIME

SALE_REF

OFFER_PRICE

SELLER_COMMENTS

ERROR_MESSAGE

002-4.3.10	Informal Messages

002-4.3.10.1	Provider/Customer Want Ads and Informal Message Posting Request (messagepost)

Provider/Customer Want Ads and Informal Message Posting Request (messagepost) is used by Providers and Customers who wish to post a message. The valid entries for CATEGORY shall be defined by providers and shall be listed in the List of CATEGORY Template.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection used to input the request.

When the OASIS node is out of service and transmission requests are received by the TP by phone or fax then the CATEGORY=OASIS_MAINTENANCE_OUTAGE will be used to document the outage.  The VALID_FROM_TIME will be the time the outage started and VALID_TO_TIME will be the time the outage ended. A list of all transactions that occurred during the outage and entered afterwards will be available through a query of the transstatusTemplate using START_TIME_QUEUED=<VALID_FROM_TIME> and STOP_TIME_QUEUED=<VALID_TO_TIME>.

Template: messagepost

- Input

SUBJECT

CATEGORY

VALID_FROM_TIME

VALID_TO_TIME

MESSAGE (must be specified)

- Response (acknowledgment)

RECORD_STATUS

POSTING_REF (assigned by information provider)

SUBJECT

CATEGORY

VALID_FROM_TIME

VALID_TO_TIME

MESSAGE

ERROR_MESSAGE

002-4.3.10.2	Message (message)

Message (message) is used to view a posted Want Ad or Informal Message. The CATEGORY Data Element can be queried.

Template: message

- Query

CUSTOMER_CODE

CUSTOMER_DUNS

POSTING_REF

CATEGORY

VALID_FROM_TIME

VALID_TO_TIME

TIME_POSTED

- Response

CUSTOMER_CODE

CUSTOMER_DUNS

POSTING_REF

SUBJECT

CATEGORY

VALID_FROM_TIME

VALID_TO_TIME

TIME_POSTED

CUSTOMER_NAME

CUSTOMER_PHONE

CUSTOMER_FAX

CUSTOMER_EMAIL

MESSAGE

002-4.3.10.3	Provider/Sellers Message Delete Request (messagedelete)

Provider/Sellers Message Delete Request (messagedelete) is used by Providers and Sellers who wish to delete their message. The POSTING_REF number is used to determine which message.

CUSTOMER_CODE and CUSTOMER_DUNS shall be determined from the registered connection used to input the request.

Template: messagedelete

- Input

POSTING_REF

- Response (Acknowledgment)

RECORD_STATUS

POSTING_REF

ERROR_MESSAGE

002-4.3.10.4	Personnel Transfers (personnel)

The personnel Template is used to indicate when personnel are transferred between the merchant function and the Transmission Provider function as required by FERC Statutes and Regulations (18 CFR 37.4(b)(2)) .

Template: personnel

- Query

TIME_OF_LAST_UPDATE

START_TIME_POSTED

STOP_TIME_POSTED

- Response

POSTING_NAME

EMPLOYEE_NAME

FORMER_POSITION

FORMER_COMPANY

FORMER_DEPARTMENT

NEW_POSITION

NEW_COMPANY

NEW_DEPARTMENT

DATE_TIME_EFFECTIVE

TIME_POSTED

TIME_OF_LAST_UPDATE

002-4.3.10.5	Discretion (discretion)

The discretion Template is used to describe the circumstances when discretion was exercised in applying terms of the tariff, as described in the FERC Statutes and Regulations (18 CFR 37.4(b)(5)(iii)).

Template: discretion

- Query

START_TIME_POSTED

STOP_TIME_POSTED

START_TIME

STOP_TIME

SERVICE_TYPE

SERVICE_NAME

TIME_OF_LAST_UPDATE

- Response

POSTING_NAME

RESPONSIBLE_PARTY_NAME (name of person granting discretion)

SERVICE_TYPE (ancillary or transmission)

SERVICE_NAME (make consistent with offering Templates)

TARIFF_REFERENCE

START_TIME

STOP_TIME

DISCRETION_DESCRIPTION

TIME_POSTED

TIME_OF_LAST_UPDATE

002-4.3.10.6	Standards of Conduct (stdconduct)

The stdconduct Template indicates when information is disclosed in a manner contrary to the standards of conduct, as described in the FERC Statutes and Regulations (18 CFR 37.4(b)(4)(ii)).

Template: stdconduct

- Query

START_TIME_POSTED

STOP_TIME_POSTED

TIME_OF_LAST_UPDATE

- Response

POSTING_NAME

RESPONSIBLE_PARTY_NAME

STANDARDS_OF_CONDUCT_ISSUES

TIME_POSTED

TIME_OF_LAST_UPDATE

002-4.3.11	Audit Log

The OASIS audit log report facility shall be implemented by the definition of the following Templates:

transofferingaudit		 - audit counterpart to transoffering

ancofferingaudit		 - audit counterpart to ancoffering

scheduledetailaudit	 - audit counterpart to scheduledetail

securityaudit		 - audit counterpart to security

systemdataaudit		 - audit counterpart to systemdata

transstatusaudit		 - audit counterpart to transstatus

ancstatusaudit		 - audit counterpart to ancstatus

personnelaudit		 - audit counterpart to personnel

discretionaudit		 - audit counterpart to discretion

dtdconductaudit		 - audit counterpart to stdconduct

Each of these audit Templates is an extension to the OASIS Template definitions of their non-audit counterparts. The requirements for implementation of the audit Templates is defined in the following sections.

002-4.3.11.1	Query Variables

Each of the audit Templates defined shall support exactly the same set of Query Variables as defined for their non-audit Template counterpart. As with the standard Template definitions, audit reports may be downloaded in Comma Separated Value (CSV) format by the specification of the OUTPUT_FORMAT=DATA Query Variable, or may be viewed using a web browser when OUTPUT_FORMAT=HTML is specified.

002-4.3.11.2	Audit Report Response Format

Audit report information shall be returned in response to a valid query request made to any of the audit Templates defined. Query variables may be specified as allowed by each individual Template and shall have the effect of limiting the scope of audit data returned to that set of information selected by that combination of additional Query Variables.

The response to an audit query shall consist of ordered sets of information reflecting both the current information as posted on OASIS and the full history of changes made to that information. These ordered sets of information are organized around the individual postings or "records" returned in response to the applicable non-audit Template. For example, execution of the transstatus (or ancstatus) Template returns a set of individual records identified by unique ASSIGNMENT_REF. The transstatusaudit Template response is then organized by ASSIGNMENT_REF and would show all changes made to those Data Elements associated with each individual ASSIGNMENT_REF record.

Execution of the transoffering (or ancoffering or systemdata) Template returns a set of individual records identified by unique POSTING_REF. The transofferingaudit Template response is then organized by POSTING_REF and would show all changes made to those Data Elements associated with each individual POSTING_REF record.

The specific audit report response format is detailed in the following sections.

002-4.3.11.3	Comma Separated Value (CSV) Format

A CSV formatted audit Template response shall comply with all the general provisions and specifications defined previously for a CSV formatted response. The CSV response records shall be  organized in sets of records containing both the latest information posted on OASIS and all changes made to that information over time.

002-4.3.11.3.1		CSV Response Header Records

The following additional Data Element names shall be included as the first set of Data Elements in the  COLUMN_HEADERS record and the corresponding Data Element values shall be included in each subsequent Data Record (row) returned in the audit response:

RECORD_TYPE

TIME_OF_LAST_UPDATE

MODIFYING_COMPANY_CODE

MODIFYING_NAME

These Data Elements shall precede the standard Data Elements associated with the specific Template being invoked.

The RECORD_TYPE Data Element shall take on one of the following restricted values:

I - denotes a record of information as it appeared on its initial Insertion (posting) on OASIS

U - denotes a record of information as it appeared immediately following an Update to the posted information

D - denotes a record of any Deleted information as it last appeared on OASIS.

The TIME_OF_LAST_UPDATE Data Element shall contain the time that the Template Data Elements were inserted, updated or deleted to the values reported in that record (row) of the response. This Data Element is identical to the standard Template TIME_OF_LAST_UPDATE Data Element, and is included as part of the fixed audit specific Data Element columns to aid users in sorting the audit response records.

The MODIFYING_COMPANY_CODE and MODIFYING_NAME Data Elements shall contain the identity of the entity (by the appropriate 4-6 character customer/provider code) and the person that inserted, updated or deleted the Data Elements to the values reported in that record (row) of the response. In the event the modification of posted information cannot be associated with a specific OASIS user (e.g., as a result of an automated back-end process), the MODIFYING_NAME Data Element may be null.

Immediately following the MODIFYING_NAME column header, each of the standard non-audit counterpart Template's Data Elements shall be listed in the exact sequence defined for that non-audit Template.

Finally, OASIS implementations may include additional Data Elements identified by unique column headers appended after the fixed audit and standard Template Data Elements. These additional Data Elements may be used to convey implementation specific information maintained in the OASIS database in association with the data being audited.

002-4.3.11.3.2		CSV Data Records

In formatting an audit response, OASIS shall collect and order information into sets of Data Records (rows). Each set of records returned shall include a record corresponding to the information as original inserted into the OASIS database denoted by a RECORD_TYPE of "I", and as many additional records with RECORD_TYPE of "U" corresponding to each update made to that information over time. If applicable, a record may also be returned in the set with a RECORD_TYPE of "D" if the corresponding information was effectively deleted from the database. The number of sets of audit report records returned in response to an audit query shall be determined by the number and type of additional Template Query Variables specified by the user.

002-4.3.11.3.3		CSV Continuation Records

Continuation records are used in certain standard Phase 1-A Templates to report repeating Data Elements associated with a single OASIS transaction such as demand profiles or the reassignment of rights on the secondary market. The first (CONTINUATION_FLAG=N) record and all associated continuation (CONTINUATION_FLAG=Y) records shall be treated as a group when generating the response to an audit query. To minimize the volume of information reported in an audit response, implementations may elect to suppress repeating the contents of information contained in continuation records if none of the Data Elements associated with those continuation records were modified. If, however, the Data Element(s) to be reported by an audit record are contained in one or more of the continuation records (e.g., a change was made to a transmission reservation's demand profile), the first (CONTINUATION_FLAG=N) record followed by the entire group of continuation (CONTINUATION_FLAG=Y) records shall be reported.

002-4.3.11.3.4		CSV Response Header Records

Finally, OASIS implementations may include additional Data Elements identified by unique column headers appended after the fixed audit and standard Template Data Elements. These additional Data Elements may be used to convey implementation specific information maintained in the OASIS database in association with the data being audited.

002-4.3.11.4	HTML Output

Specification of the Query Variable OUTPUT_FORMAT=HTML shall minimally result in an audit report formatted identically to the CSV Format (OUTPUT_FORMAT=DATA) with the exception that the response shall be returned using the HTTP header "Content-type: text/plain" specification. This will result in the CSV Data Records being rendered in simple text within the user's web-browser. More sophisticated HTML formatted responses to audit queries may be provided by the TSIPs at their discretion.

002-4.3.11.5	Special Audit Template Considerations

Transoffering

The transoffering Template is used to convey information on transmission services offered for sale as well as the availability of transmission capability (TTC/ATC). The proposed audit reporting scheme may prove inadequate to generate audits of both the commercial aspects of offers posted on OASIS (i.e., price, etc.) and the reliability aspects associated with those offers (i.e., ATC) depending on how these two different types of information are represented internally by each OASIS node.

For those OASIS implementations that handle TTC/ATC information separately from the posting of commercial offers of service, audit reports generated by the transofferingaudit Template may be limited to only reporting changes to the Data Elements associated with the commercial aspects of the offer (e.g., OFFER_PRICE, OFFER_START_TIME, etc.), and may return a null value for the CAPACITY Data Element. These nodes shall use the systemdataaudit Template audit reporting facility to allow for the full auditing of changes made to TTC and ATC postings as required under Federal Regulations.

Scheduledetail

The scheduledetail Template combines information from one or more transmission reservations and transmission security event postings (e.g., TLRs) with information posted on actual scheduled use of the transmission system.Audit information related to changes made to a given transmission reservation shall be auditable using the transstatusaudit Template. Audit information related to the posting of transmission security events that led to a curtailment or interruption of service, or the denial of a request to schedule service shall be auditable using the securityaudit Template. Therefore, the scheduledetailaudit Template shall only be required to report changes to the following Data Elements associated with the scheduledetail Template:

TRANSACTION_ID

START_TIME

STOP_TIME

SCHEDULE_REQUESTED

SCHEDULE_GRANTED

ASSIGNMENT_REF

PROVIDER_ACTION

SCHEDULE_LIMIT

CURTAILMENT_OPTIONS

SECURITY_REF

002-4.4	FILE REQUEST AND FILE DOWNLOAD EXAMPLES

In the examples, the end-of-line (eol) character is represented by the character," ( ". This symbol may appear different on displays or printouts.

002-4.4.1	File Example for Hourly Offering

Example of the request to Primary Provider, aaa, and response for Seller, wxyz, for PATH_NAME "W/AAAA/PATH-ABC//" for April 10, 1996 from 8 a.m. to 3 p.m. (Note that the PATH_NAME consists of a REGION_CODE, PRIMARY_PROVIDER_CODE, PATH_CODE, and an OPTIONAL_CODE, separated with a slash, "/".)

The VERSION for this release is 1.4. The request is in the form of a URL query string and the response is an ASCII delimited file.

- Query

http://(OASIS Node name)/OASIS/aaa/data/transoffering? ver=1.2&templ=transoffering& fmt=data&pprov=AAAA &pprovduns=123456789& path=W/AAA/ABC// &seller=WXYZAA &sellerduns=987654321& POR=aaa& POD=bbb& servincre=hourly& TSCLASS1=firm &TSCLASS2=non-firm&tz=PD&stime=19960410080000PD&sptime= 19960410150000PD

- Response Data

REQUEST-STATUS=200( (Successful)

TIME_STAMP=19960409113526PD (

VERSION=1.4(

TEMPLATE=transoffering(

OUTPUT_FORMAT=DATA (

PRIMARY_PROVIDER_CODE=AAAA(

PRIMARY_PROVIDER_DUNS=123456789(

DATA_ROWS=14(

COLUMN_HEADERS=TIME_OF_LAST_UPDATE,SELLER_CODE,SELLER_DUNS,PATH_NAME,

POINT_OF_RECEIPT,POINT_OF_DELIVERY,INTERFACE_TYPE,OFFER_START_TIME, OFFER_STOP_TIME,

START_TIME,STOP_TIME, CAPACITY, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD,

TS_SUBCLASS, SALE_REF, POSTING_REF, CEILING_PRICE, OFFER_PRICE, PRICE_UNITS,

SERVICE_DESCRIPTION,SELLER_NAME,SELLER_PHONE,SELLER_FAX, SELLEREMAIL,

SELLER_COMMENTS (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

080000PD,19960410090000PD,300, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A, A001,

1.50,1.35,MW,N/A,N/A,N/A,N/A,N/A,10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

080000PD,19960410090000PD,300, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A,A001,1.50,

1.35,MW,N/A,N/A,N/A,N/A,N/A, 10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

090000PD,1996041010000PD,300, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A,

N/A,A001,1.50,1.35,MW,N/A,N/A,N/A,N/A,N/A,10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

090000PD,19960410100000PD,300, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A,A001,1.50,

1.35,MW,N/A,N/A,N/A,N/A,N/A, 10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

100000PD,19960410110000PD,300, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A,

N/A,A001,1.50,1.35,MW,N/A,N/A,N/A,N/A,N/A,10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

100000PD,19960410110000PD,300, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A,A001,1.50,

1.35,MW,N/A,N/A,N/A,N/A,N/A, 10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

110000PD,19960410120000PD,300, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A,

N/A,A001,1.50,1.35,MW,N/A,N/A,N/A,N/A,N/A,10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

110000PD,19960410120000PD,300, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A,A001,1.50,

1.35,MW,N/A,N/A,N/A,N/A,N/A, 10% DISCOUNT (

. . .

. . .

. . .

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

140000PD,19960410150000PD,300, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A,

N/A,A001,1.50,1.35,MW,N/A,N/A,N/A,N/A,N/A,10% DISCOUNT (

19960409030000PD,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,19960402080000PD,19960410080000PD,19960410

140000PD,19960410150000PD,300, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK, N/A, N/A,A001,1.50,

1.35,MW,N/A,N/A,N/A,N/A,N/A, 10% DISCOUNT (

002-4.4.2	File Example for Hourly Schedule Data

This example shows a request for the hourly schedule data from Primary Provider, AAAA, related to the seller, WXYZ, for the period 10 a.m. to 3 p.m. on April 10, 2000.

There are two identical requests examples using two slightly different methods. The first request is using a HTTP URL request string through an HTML GET method. The second request is a similar example using fetch_http from a file using a POST method.

- Query

URL Request (HTTP method=GET)

http://(OASIS Node name)/OASIS/aaaa/data/scheduledetail? ver=1.4& pprov=AAAA& templ=scheduledetail& fmt=data &pprovduns=123456789 &path=W/AAA/ABC//& seller=WXYZ &por=BBB &pod=CCC& tz=PD& stime=20000410100000PD& sptime=20000410150000PD

URL Request (HTTP method=POST)

$ fetch_http http://(OASIS Node name)/OASIS/aaaa/data/OASISdata -f c:/OASIS/wxyz/upload/infile. txt Where in-file.txt contains the following: ver=1.4& pprov=AAAA& templ=scheduledetail& fmt=data &pprovduns=123456789 &path=W/AAA/ABC//& seller=WXYZ &por=BBB &pod=CCC& tz=PD& stime=20000410100000PD& sptime=20000410150000PD

- Response Data

REQUEST_STATUS=200(

ERROR_MESSAGE=No error. (

TIME_STAMP=20000410160523ES(

VERSION=1.4(

TEMPLATE=scheduledetail(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AAAA(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=PD(

DATA_ROWS=3(

COLUMN_HEADERS=CONTINUATION_FLAG, TIME_OF_LAST_UPDATE, SCHEDULE_REF, TRANSACTION_ID, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, GCA_CODE, LCA_CODE, SOURCE, SINK, SCHEDULE_PRIORITY, START_TIME, STOP_TIME, SCHEDULE_REQUESTED, SCHEDULE_GRANTED, ASSIGNMENT_REF, SELLER_CODE, SELLER_DUNS, CUSTOMER_CODE, CUSTOMER_DUNS, AFFILIATE_FLAG, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_WINDOW, TS_SUBCLASS, NERC_CURTAILMENT_PRIORITY, OTHER_CURTAILMENT_PRIORITY, CAPACITY_USED, PROVIDER_ACTION, SCHEDULE_LIMIT, CURTAILMENT_OPTIONS, SECURITY_REF, INITIATING_PARTY, RESPONSIBLE_PARTY, PROCEDURE_NAME, PROCEDURE_LEVEL, FACILITY_LOCATION, FACILITY_NAME, FACILITY_CLASS, FACILITY_LIMIT_TYPE(

N, 20000409030000PD,12345,2233, W/AAA/ABC//, BBB, CCC,,,,,1, 20000410100000PD, 20000410110000PD,300,300,856743, wxyz,987654321, WXYZAA,987654322, Y, HOURLY, NON_FIRM, POINT_TO_POINT, OFF_PEAK, FIXED,,1,1,300,,,,,,,,,,,, (

N, 20000409030000PD,12346,2233, W/AAA/ABC//, BBB, CCC,,,,,1, 20000410130000PD, 20000410140000PD,300,300,856743,wxyz,987654321, WXYZAA,987654322, Y, HOURLY, NON_FIRM, POINT_TO_POINT, OFF_PEAK, FIXED,,1,1,300,,,,,,,,,,,, (

N, 20000409030000PD,12347,2233, W/AAA/ABC//, BBB, CCC,,,,,1, 20000410140000PD, 20000410150000PD,300,300,856743,wxyz,987654321, WXYZAA,987654322, Y, HOURLY, NON_FIRM, POINT_TO_POINT, OFF_PEAK, FIXED,,1,1,300,,,,,,,,,,,, (

002-4.4.3	Customer Posting a Transmission Service Offering

This example shows how a Customer would post for sale the transmission service that was purchased previously. The Seller would create a file and upload the file using the FETCH_HTTP program to send a file to the OASIS Node of the Primary Provider.

- Input:

VERSION=1.4(

TEMPLATE=transpost(

OUTPUT_FORMAT=DATA (

PRIMARY_PROVIDER_CODE=AAAA(

PRIMARY_PROVIDER_DUNS=123456789(

DATA_ROWS=1(

COLUMN_HEADERS=PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, INTERFACE_TYPE, CAPACITY, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_SUBCLASS, START_TIME, STOP_TIME, OFFER_START_TIME, OFFER_STOP_TIME, SALE_REF, OFFER_PRICE, SERVICE_DESCRIPTION, SELLER_COMMENTPF(

WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,150, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A,, 19960402080000PD,19960410080000PD, 19960410080000PD,19960410150000PD, A123,.90,N/A,"As Joe said, ""It is a good buy"""(

FETCH_HTTP Command to send posting $ fetch_http http://(OASIS Node name)/OASIS/abcd/data/transrequest -f c:/OASIS/abcd/upload/post.txt

- Response Data

REQUEST-STATUS=200 ( (Successful)

TIME_STAMP=19960409113526PD (

VERSION=1.4(

TEMPLATE=transpost(

OUTPUT_FORMAT=DATA (

PRIMARY_PROVIDER_CODE=AAAA(

PRIMARY_PROVIDER_DUNS=123456789(

DATA_ROWS=1(

COLUMN_HEADERS=RECORD_STATUS, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, INTERFACE_TYPE, CAPACITY, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_SUBCLASS, START_TIME, STOP_TIME, OFFER_START_TIME, OFFER_STOP_TIME, SALE_REF, OFFER_PRICE, SERVICE_DESCRIPTION, SELLER_COMMENTS, ERROR_MESSAGE(

200,WXYZ,987654321,W/AAA/ABC//,N/A,N/A,E,150, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK, N/A, 19960402080000PD,19960410080000PD, 19960410080000PD,19960410150000PD, A123,.90,N/A, "As Joe said, ""It is a good buy""", No Error(

002-4.4.4	Example of Re-aggregating Purchasing Services using Reassignment

The following examples do not show the complete Template information, but only show those elements of the Template of interest to the example.

a. Customer #1, "BestE" requests the purchase of 150 MW Firm ATC for 8 a.m. to 5 p.m. for $1.00 from a Primary Provider (transrequest).

TEMPLATE=transrequest(

CUSTOMER_CODE=BestE(

CAPACITY=150(

TS_CLASS="FIRM"(

START_TIME="1996050708000000PD"(

STOP_TIME="1996050717000000PD"(

BID_PRICE="$1.00"(

The Information Provider assigns ASSIGNMENT_REF = 5000 on acknowledgment.

b. Customer #1 purchases 120 MW ATC Non-firm for 3 p.m. to 9 p.m. for $.90 (transrequest). The Information Provider assigns the ASSIGNMENT_REF=5001 when the request for purchase is made and is shown in the acknowledgment.

TEMPLATE="transrequest"(

CUSTOMER_CODE="BestE"(

CAPACITY=120(

TS_CLASS="NON-FIRM"(

START_TIME="1996050715000000PD"(

STOP_TIME="1996050721000000PD"(

BID_PRICE="$1.05"(

c. Customer #1 becomes Seller #1 and post the Transmission service of 100 MW ATC Non-firm capacity from 8 a.m. to 9 p.m. for resale at $.90/MW-hour.

TEMPLATE="transpost"(

SELLER_CODE="BestE"(

CAPACITY=100(

TS_CLASS="NON-FIRM"(

START_TIME="1996050708000000PD"(

STOP_TIME="1996050721000000PD"(

SALE_REF="BEST100"(

OFFER_PRICE=.90(

SELLER_COMMENTS="aggregating two previous purchases"(

d. Customer #2 then requests purchase of 100 MW Non-firm from Reseller #1 from 8 a.m. to 6 p.m. for $0.90/MW-hour (transrequest).

TEMPLATE="transrequest"(

CUSTOMER_CODE="Whlsle"(

SELLER_CODE="BestE"(

CAPACITY=100(

TS_CLASS="NON-FIRM"(

START_TIME="1996050708000000PD"(

STOP_TIME="1996050721000000PD"(

SALE_REF="BEST100"(

DEAL_REF="WPC100"(

BID_PRICE=.90(

CUSTOMER_COMMENTS="Only need service until 6 p.m." (

The Information Provider provides the ASSIGNMENT_REF=5002 for this transaction.

e. Seller informs the Information Provider of the reassignment of the previous transmission rights when the seller accepts the customer purchase request (transsell).

TEMPLATE="transsell"(

CUSTOMER_CODE="Whlsle"(

SELLER_CODE="BestE"(

ASSIGNMENT_REF=5002(

STATUS="Accepted"(

REASSIGNED_REF1=5000(

REASSIGNED_CAPACITY1=100(

REASSIGNED_START_TIME1="199605070800PD"(

REASSIGNED_STOP_TIME1="199605071700PD"(

REASSIGNED_REF2=5001(

REASSIGNED_CAPACITY2=100(

REASSIGNED_START_TIME2="199605071700PD"(

REASSIGNED_STOP_TIME2="199605071800PD"(

002-4.4.5	File Examples of the Use of Continuation Records

a. Basic Continuation Records

The first example of the use of Continuation Records is for the transrequest Template submitted by a Seller for purchase of a transmission reservation spanning 16 hours from 06:00 to 22:00 with "ramped" demand at beginning and end of time period. Two additional reservations appear prior to and following the profile to demonstrate the handling of ASSIGNMENT_REF by the OASIS Node.

Only the following fields may be redefined in a continuation record for the transrequest   Template: CAPACITY_GRANTED, START_TIME, STOP_TIME. Specification of any values corresponding to COLUMN_HEADERs other than CAPACITY-GRANTED, START_TIME, and STOP_TIME will be ignored, however commas must be included to properly align the CAPACITY_GRANTED, START_TIME and STOP_TIME fields.

Input:

VERSION=1.4(

TEMPLATE=transrequest(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=7(

COLUMN_HEADERS=CONTINUTATION_FLAG, SELLER_CODE,SELLER_DUNS, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SOURCE, SINK,CAPACITY_REQUESTED, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_WINDOW, TS_SUBCLASS, STATUS_NOTIFICATION,START_TIME,STOP_TIME,BID_PRICE, PRECONFIRMED, ANC_SVC_LNK, POSTING_REF, SALE_REF, REQUEST_REF, DEAL_REF, CUSTOMER_COMMENTS, REQUEST_TYPE,REASSIGNED_REF(

N, AEP,123456789, ABC/XY, CE, MECS,,,35, DAILY, FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423000000ES,20000424000000ES,24.5, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, Standard daily reservation, ORIGINAL, (

N, AEP,123456789, ABC/XY, CE, AMPO,,,5, HOURLY, NON-FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423060000ES,20000423070000ES,2.5, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, First piece of profile spanning 5 records, ORIGINAL, (

Y,,,,,,,,10,,,,,,, ,20000423070000ES,20000423080000ES,,,,,,,, Second piece,, (

Y,,,,,,,,15,,,,,,, ,20000423080000ES,20000423200000ES,,,,,,,, Third piece,, (

Y,,,,,,,,10,,,,,,, ,20000423200000ES,20000423210000ES,,,,,,,, Fourth piece,, (

Y,,,,,,,,5,,,,,,, ,20000423210000ES,20000423220000ES,,,,,,,, Fifth piece,, (

N, AEP,123456789, ABC/XY, CE, MECS, , ,20, HOURLY, NON-FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423040000ES,20000423160000ES,2, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, Standard hourly reservation after profiled reservation, ORIGINAL, (

Response:

REQUEST_STATUS=200(

ERROR_MESSAGE=Successfully updated. (

TIME_STAMP=20000422160523ES(

VERSION=1.4(

TEMPLATE=transrequest(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=7(

COLUMN_HEADERS=RECORD_STATUS, CONTINUTATION_FLAG, ASSIGNMENT_REF, SELLER_CODE,SELLER_DUNS, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SOURCE, SINK,CAPACITY_REQUESTED, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD, TS_WINDOW, TS_SUBCLASS, STATUS_NOTIFICATION,START_TIME,STOP_TIME,BID_PRICE, PRECONFIRMED, ANC_SVC_LNK, POSTING_REF, SALE_REF, REQUEST_REF, DEAL_REF, CUSTOMER_COMMENTS, REQUEST_TYPE,REASSIGNED_REF, ERROR_MESSAGE(

200,N,8234, AEP,123456789, ABC/XY, CE, MECS,,,35, DAILY, FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423000000ES,20000424000000ES,24.5, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, Standard daily reservation, ORIGINAL,, No error(

200,N,8235, AEP,123456789, ABC/XY, CE, AMPO,,,5, HOURLY, NON-FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423060000ES,20000423070000ES,2.5, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, First piece of profile spanning 5 records, ORIGINAL,, No error(

200,Y,8235,,,,,,,,10,,,,,,,,20000423070000ES,20000423080000ES,,,,,,,, Second piece,,, No error(

200,Y,8235,,,,,,,,15,,,,,,,,20000423080000ES,20000423200000ES,,,,,,,, Third piece,,, No error(

200,Y,8235,,,,,,,,10,,,,,,,,20000423200000ES,20000423210000ES,,,,,,,, Fourth piece,,, No error(

200,Y,8235,,,,,,,,5,,,,,,,,20000423210000ES,20000423220000ES,,,,,,,, Fifth piece,,, No error(

200,N,8236, AEP,123456789, ABC/XY, CE, MECS,,,20, HOURLY, NON-FIRM, POINT_TO_POINT, FULL_PERIOD, FIXED,, pub/AEP/incoming,20000423040000ES,20000423160000ES,2, Y, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, P0123 , S123, R765, D123, Standard hourly reservation after profiled reservation, ORIGINAL,, No error(

b. Submission of Reassignment Information - Case 1:

In the prior example, a reservation request was submitted to "Rseler" for 20MW of Hourly Non-firm service from 04:00 to 16:00. Assume that Rseler has previously reserved service for the CE-VP path for Daily Firm in amount of 50 MW on 4/23 under ASSIGNMENT_REF=7019, and Hourly Non-Firm in amount of 10 MW from 08:00 to 20:00 on 4/23 under ASSIGNMENT_REF=7880. Rseler must designate which transmission service rights are to be reassigned to Cust to satisfy the 20MW from 04:00 to 16:00. This reassignment information is conveyed by Rseler using the transsell Template when the reservation request is ACCEPTED. At the SELLER's discretion, rights are assigned from the Non-firm reservation first (ASSIGNMENT_REF=7880) with the balance taken up by the Firm reservation (ASSIGNMENT_REF=7019).

The only fields allowed in "continuation" records for transsell Template are REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. Price may not be negotiated for each "segment" in a capacity profile.

Input:

VERSION=1.4(

TEMPLATE=transsell(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=3(

COLUMN_HEADERS=CONTINUATION_FLAG,ASSIGNMENT_REF, START_TIME, STOP_TIME,OFFER_PRICE,CAPACITY_GRANTED, STATUS, STATUS_COMMENTS, ANC_SVC_LINK, ANC_SVC_REQ, NEGOTIATED_PRICE_FLAG, SELLER_REF, SELLER_COMMENTS, RESPONSE_TIME_LIMIT,REASSIGNED_REF,REASSIGNED_CAPACITY, REASSIGNED_START_TIME , REASSIGNED_STOP_TIME(

N,8236, 20000423040000ES, 20000423160000ES,2.5,20, ACCEPTED, Status comments here, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;,, S123, Seller comments here,,7019,20, 20000423040000ES, 20000423080000ES(

Y,8236,,, ,, , , ,,,, ,,7880,10, 20000423080000ES, 20000423160000ES(

Y,8236,,, ,, , , ,,,, ,,7019,10, 20000423080000ES, 20000423160000ES(

Response:

REQUEST_STATUS=200(

ERROR_MESSAGE=Successfully updated. (

TIME_STAMP=20000422160523ES(

VERSION=1.4(

TEMPLATE=transsell(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=3(

COLUMN_HEADERS=RECORD_STATUS,CONTINUATION_FLAG,ASSIGNMENT_REF, START_TIME, STOP_TIME,OFFER_PRICE,CAPACITY_GRANTED, STATUS, STATUS_COMMENTS, ANC_SVC_LINK, ANC_SVC_REQ, NEGOTIATED_PRICE_FLAG, SELLER_REF, SELLER_COMMENTS, RESPONSE_TIME_LIMIT,REASSIGNED_REF,REASSIGNED_CAPACITY, REASSIGNED_START_TIME , REASSIGNED_STOP_TIME, ERROR_MESSAGE(

N,,8236, 20000423040000ES, 20000423160000ES,2.5,20, ACCEPTED, Status comments here, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;,, S123, Seller comments here,,7019,20, 20000423040000ES, 20000423080000ES, No error(

Y,,8236,,, ,, , , ,,,, ,,7880,10, 20000423080000ES, 20000423160000ES, No error(

Y,,8236,,, ,, , , ,,,, ,,7019,10, 20000423080000ES, 20000423160000ES, No error(

c. Submission of Reassignment Information - Case 2:

Primary provider, AEP, is notified of a sale/assignment of transmission service rights from "Resell" to "cust". The parameters of the new reservation are for 10MW on 4/23 for "off-peak" hours (00:00- 06:00 and 22:00-24:00) on POR/POD CE-VP. Rseler is assigning rights to 10MW from a prior reservation for the CE-VP path for Daily Firm in amount of 50 MW on 4/23 under ASSIGNMENT_REF=7019 to Cust. AEP would submit the following information using the transassign Template to post this (re)sale. The only fields allowed in "continuation" records for the transassign Template are CAPACITY, START_TIME , STOP_TIME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME. Even though there is a one-to-one correspondence between the segments of the new reservations and the reassignment of service from a prior reservation, it is entirely possible that a reservation spanning a single contiguous period would require multiple continuation records to convey reassignment information, and vice versa.

Fields for CUSTOMER_NAME and SELLER_NAME were used to convey user names for subsequent resolution of contact information from user registration.

Input:

VERSION=1.4(

TEMPLATE=transassign(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=2(

COLUMN_HEADERS=CONTINUATION_FLAG, CUSTOMER_CODE, CUSTOMER_DUNS, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SOURCE, SINK, CAPACITY_REQUESTED, CAPACITY_GRANTED, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD,TS_WINDOW, TS_SUBCLASS, START_TIME, STOP_TIME, OFFER_PRICE, ANC_SVC_LNK, POSTING_NAME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME , REASSIGNED_STOP_TIME , SELLER_COMMENTS, SELLER_REF(

N, ACSTMR,987654321, , CE, VP,,,10,10, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK,FIXED,, 20000423000000ES, 20000423060000ES,2, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, Jane Doe ,7019,10, 20000423000000ES, 20000423060000ES, Seller comments go here, S123(

Y,,,,,,,,10,10,,,,,,, 20000423220000ES, 20000424000000ES,,,,7019,10, 20000423220000ES, 20000424000000ES,, (

Response:

REQUEST_STATUS=200(

ERROR_MESSAGE=Successfully updated. (

TIME_STAMP=20000422160523ES(

VERSION=1.4(

TEMPLATE=transassign(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=2(

COLUMN_HEADERS=RECORD_STATUS,CONTINUATION_FLAG,ASSIGNMENT_REF, CUSTOMER_CODE, CUSTOMER_DUNS, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SOURCE, SINK, CAPACITY_REQUESTED, CAPACITY_GRANTED, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD,TS_WINDOW, TS_SUBCLASS, START_TIME, STOP_TIME, OFFER_PRICE, ANC_SVC_LNK, POSTING_NAME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME , REASSIGNED_STOP_TIME , SELLER_COMMENTS, SELLER_REF5, ERROR_MESSAGE(

200,N,8207, ACSTMR,987654321, , CE, VP,,,10,10, HOURLY, NON-FIRM, POINT_TO_POINT, OFF_PEAK,FIXED,, 20000423000000ES, 20000423060000ES,2, SC:(AEP:RQ);RV:(AEP:RQ);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, Jane Doe ,7019,10, 20000423000000ES, 20000423060000ES, Seller comments go here, S1235, No error(

200,Y,8207,,,,,,,,10,10,,,,,,, 20000423220000ES, 20000424000000ES,,,,7019,10, 20000423220000ES, 20000424000000ES,,5, No error(

d. Query of Transmission Reservation Status:

The following typical response to a transstatus query might be delivered for 4/23 based on prior examples. Note that the only fields returned in "continuation" records are, ASSIGNMENT_REF, CAPACITY_REQUESTED, CAPACITY_GRANTED, START_TIME, STOP_TIME, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME, and REASSIGNED_STOP_TIME (price fields are debatable).

Input:

<appropriate query name/value pairs to return reservations for 4/23>

Response:

REQUEST_STATUS=200(

ERROR_MESSAGE=No error. (

TIME_STAMP=20000423160523ES(

VERSION=1.4(

TEMPLATE=transstatus(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=AEP(

PRIMARY_PROVIDER_DUNS=123456789(

RETURN_TZ=ES(

DATA_ROWS=11(

COLUMN_HEADERS=CONTINUATION_FLAG, ASSIGNMENT_REF, SELLER_CODE, SELLER_DUNS, CUSTOMER_CODE, CUSTOMER_DUNS, AFFILIATE_FLAG, PATH_NAME, POINT_OF_RECEIPT, POINT_OF_DELIVERY, SOURCE, SINK, CAPACITY_REQUESTED, CAPACITY_GRANTED, SERVICE_INCREMENT, TS_CLASS, TS_TYPE, TS_PERIOD,TS_WINDOW, TS_SUBCLASS, NERC_CURTAILMENT_PRIORITY, OTHER_CURTAILMENT_PRIORITY, START_TIME , STOP_TIME, CEILING_PRICE, OFFER_PRICE, BID_PRICE,PRICE_UNITS, PRECONFIRMED, ANC_SVC_LINK, ANC_SVC_REQ, POSTING_REF, SALE_REF, REQUEST_REF, DEAL_REF,IMPACTED,REQUEST_TYPE,RELATED_REF, NEGOTIATED_PRICE_FLAG, STATUS,STATUS_NOTIFICATION, STATUS_COMMENTS, TIME_QUEUED, TIME_OF_LAST_UPDATE, PRIMARY_PROVIDER_COMMENTS,SELLER_REF, SELLER_COMMENTS, CUSTOMER_COMMENTS, SELLER_NAME, SELLER_PHONE, SELLER_FAX, SELLER_EMAIL, CUSTOMER_NAME, CUSTOMER_PHONE, CUSTOMER_FAX, CUSTOMER_EMAIL, REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME , REASSIGNED_STOP_TIME(

N,8207, RSELLR,234567890, ACSTMR,987654321, N, , CE, VP, ,,10,10, HOURLY, FIRM, POINT_TO_POINT, OFF_PEAK,,,,, 20000423000000ES, 20000423060000ES,2.25,2,2,$/MW, N, SC:(AEP:AR:121);RV:(AEP:AR:122);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;, ,S1235, , ,0, RESALE,, L, CONFIRMED,, , 20000422121354ES, 20000422123054ES, TP Comments,, Seller comments go here, Customer comments, Joe Smith, (888)-123-4567, (888)-123-1231, jsmith@xyz.com, Jane Doe, (999)-123-4567, (999)-123-8823,,7019,10, 20000423000000ES, 20000423060000ES(

Y,8207,,,,,,,,,,,10,10,,,,,,,,, 20000423220000ES, 20000424000000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,7019,10, 20000423220000ES, 20000424000000ES(

N,8234, AEP,123456789, CUSTMR,345678912, N, , CE, MECS, ,,35,35, DAILY, FIRM, POINT_TO_POINT,FULL_PERIOD,FIXED,,,, 20000423000000ES, 20000423060000ES,42,24.5,24.5,$/MW, N, SC:(AEP:AR:123);RV:(AEP:AR:124);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;, P0123 , S123, R765, D123,0, ORIGINAL,, L, CONFIRMED, pub/AEP/incoming,, 20000422131354ES, 20000422133354ES, Standard daily reservation,, System Operator, Customer comments, Frank Orth, (999)-123-4567, (999)-123-1231, jsmith@xyz.com, Jane Doe, (999)-123-4567, (999)-123-8823,,7019,10, 20000423000000ES, 20000423060000ES(

N,8235, AEP,123456789, CUSTMR,345678912, N, , CE, AMPO, ,,5,5, HOURLY, NON-FIRM, POINT_TO_POINT,FULL_PERIOD,FIXED,,,, 20000423060000ES, 20000423070000ES,2.5,2.5,2.5,$/MW, N, SC:(AEP:AR:125);RV:(AEP:AR:126);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;, P0123 , S123, R765, D123,0, ORIGINAL,,, CONFIRMED, pub/AEP/incoming,, 20000422160523ES, 20000422170523ES, Profile verified,, First piece, Customer comments, System Operator, (888)-123-4567, (888)-123-1231, jsmith@xyz.com, Jane Doe, (999)- 123-4567, (999)-123-8823,,7019,10, 20000423000000ES, 20000423060000ES(

Y,8235,,,,,,,,,,,10,10,,,,,,,,, 20000423070000ES, 20000423080000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,5 Y,8235,,,,,,,,,,,15,15,,,,,,,,, 20000423080000ES, 20000423200000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

Y,8235,,,,,,,,,,,10,10,,,,,,,,, 20000423200000ES, 20000423210000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,5 Y,8235,,,,,,,,,,,5,5,,,,,,,,, 20000423210000ES, 20000423220000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

N,8236, AEP,123456789, CUSTMR,345678912, N, , CE, VP, ,,20,20, HOURLY,NON_FIRM, POINT_TO_POINT,FULL_PERIOD,FIXED,,,, 20000424040000ES, 20000424160000ES,2.5,2.5,2.5,$/MW, N, SC:(AEP:AR:127);RV:(AEP:AR:128);RF:(FT);EI:(FT);SP:(FT);SU:(FT);, SC:M;RV:M;RF:U;EI:U;SP:U;SU:U;, P0123 , S123, R765, D123,0, ORIGINAL,,, CONFIRMED, pub/AEP/incoming,, 20000422160723ES, 20000422171523ES, Bid price refused,, Negotiated OFFER_PRICE accepted,, Joe Smith, (888)-123-4567, (888)-123-1231, jsmith@xyz.com, Jane Doe, (999)-123-4567, (999)-123-8823,,7019,20, 20000423040000ES, 20000423080000ES(

Y,8236,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,7880,10, 20000423080000ES, 20000423160000ES(

Y,8236,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,7019,10, 20000423080000ES, 20000423160000ES(

002-4.4.6	Examples of Negotiation of Price and Partial Service Offer

002-4.4.6.1	Negotiation with Preconfirmation

a. The Customer submits a PRECONFIRMED transmission service request using the transrequest Template. Initially, the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, COUNTEROFFER, ACCEPTED, DECLINED, or REFUSED.

c. The Seller has the option of entering a CAPACITY_GRANTED and setting the STATUS to COUNTEROFFER via the transell Template if the seller can only provide partial service.

d. If the Seller sets STATUS to ACCEPTED (and, as required by Section 4.2.10.1i, the OASIS Node forces the Seller to set OFFER_PRICE equal to BID_PRICE as a condition to setting STATUS to ACCEPTED) and CAPACITY_GRANTED is equal to CAPACITY_REQUESTED, the OASIS Node will immediately set STATUS to CONFIRMED. (Section 4.2.10.1k requires the OASIS Node to set a null CAPACITY_GRANTED equal to CAPACITY_REQUESTED when STATUS is set to ACCEPTED.)

e. The Customer may WITHDRAW request via transcust Template at any time up to point where the Seller sets STATUS to ACCEPTED.

f. Once the STATUS is CONFIRMED, the OFFER_PRICE and CAPACITY_GRANTED officially becomes the terms of the reservation.

002-4.4.6.2	Negotiations without Preconfirmation

a. The Customer submits a transmission reservation request with the BID_PRICE less than the CEILING_PRICE via the transrequest Template. Initially the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting the STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, ACCEPTED, DECLINED, COUNTEROFFER, or REFUSED. If INVALID (due to invalid entries in the request), DECLINED (due to the Seller determining that the proposed price is not acceptable and further negotiations are not desired), or REFUSED (due to the unavailability of the requested service) are set, the transmission reservation request is terminated.

c. The Seller has the option of entering a CAPACITY_GRANTED and setting the STATUS to COUNTEROFFER via the transell Template if the seller can only provide partial service.

d. If the Seller set the STATUS to RECEIVED or STUDY, and determines that the BID_PRICE is too low, the Seller sets the OFFER_PRICE to the price desired, and sets the STATUS to COUNTEROFFER via the transsell Template.

e. The Customer agrees to the OFFER_PRICE, sets the BID_PRICE equal to the OFFER_PRICE, and sets the STATUS to CONFIRMED via the transcust Template.

f. The OFFER_PRICE and CAPACITY_GRANTED with the STATUS of CONFIRMED locks in the terms of the reservation.

002-4.4.6.3	Multiple Step Negotiations

a. The Customer submits a transmission reservation request with the BID_PRICE less than the CEILING_PRICE via the transrequest Template. Initially the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting the STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, ACCEPTED, DECLINED, COUNTEROFFER, or REFUSED. If INVALID, DECLINED, or REFUSED are set, the transmission reservation request is terminated.

c. The seller has the option of entering a CAPACITY_GRANTED and setting the STATUS to COUNTEROFFER via the transell Template if the seller can only provide partial service. If ATC changes before the request reaches the STATUS of CONFIRMED, seller may change the CAPACITY_GRANTED.

d. The Seller determines that the BID_PRICE is too low, sets the OFFER_PRICE to the desired value, and sets the STATUS to COUNTEROFFER via the transsell Template.

e. The Customer responds to the new OFFER_PRICE with an updated BID_PRICE and sets the STATUS to REBID for re-evaluation by the Seller.

f. The Seller determines that the BID_PRICE now is acceptable, and sets the STATUS to ACCEPTED via the transsell Template. The transition to ACCEPTED state requires the OFFER_PRICE to be set to the BID_PRICE: accepting a reservation with an OFFER_PRICE different from BID_PRICE would require the STATUS be set to COUNTEROFFER rather than ACCEPTED (see item c).

g. The Customer agrees to the OFFER_PRICE and sets the STATUS to CONFIRM via the transcust Template.

h. The OFFER_PRICE and CAPACITY_GRANTED with the STATUS as CONFIRMED locks in the terms of the reservation.

002-4.4.6.4	Negotiations Declined by Seller

a. The Customer submits a transmission reservation request with the BID_PRICE less than the CEILING_PRICE via the transrequest Template. Initially the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting the STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, ACCEPTED, DECLINED, COUNTEROFFER, or REFUSED. If INVALID, DECLINED, or REFUSED are set, the transmission reservation request is terminated.

c. The Seller determines that the BID_PRICE is too low, sets OFFER_PRICE to his desired value, and sets STATUS to COUNTEROFFER via the transsell Template.

d. The Customer responds to OFFER_PRICE with updated BID_PRICE and sets the STATUS to REBID via the transcust Template for re-evaluation by Seller.

e. The Seller breaks off all further negotiations by setting the STATUS to DECLINED, indicating that the price is unacceptable and that he does not wish to continue negotiations.

002-4.4.6.5	Negotiations Withdrawn by Customer

a. The Customer submits a transmission reservation request with the BID_PRICE less than the CEILING_PRICE via the transrequest. Initially the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting the STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, ACCEPTED, DECLINED, COUNTEROFFER, or REFUSED. If INVALID, DECLINED, or REFUSED are set, the transmission reservation request is terminated.

c. The Seller has the option of entering a CAPACITY_GRANTED and setting the STATUS to COUNTEROFFER via the transell Template if the seller can only provide partial service.

d. The Seller determines that the BID_PRICE is too low, sets the OFFER_PRICE to his desired value, and sets the STATUS to COUNTEROFFER via the transsell Template.

e. The Customer responds to the OFFER_PRICE with an updated BID_PRICE and sets the STATUS to REBID for re-evaluation by Seller.

f. The Seller determines that the BID_PRICE is still too low, sets the OFFER_PRICE to another value, and sets STATUS to COUNTEROFFER via the transsell Template.

g. The Customer breaks off all further negotiations, either because the OFFER_PRICE or CAPACITY_GRANTED are unacceptable, by setting STATUS to WITHDRAWN (or the Customer/Seller could go through additional iterations of REBID/COUNTEROFFER until negotiations are broken off or the reservation is CONFIRMED).

002-4.4.6.6	Negotiations Superseded by Higher Priority Reservation

a. The Customer submits a transmission reservation request with the BID_PRICE less than the CEILING_PRICE via the transrequest Template. Initially the STATUS is set to QUEUED by the OASIS Node.

b. The Seller has the option of setting the STATUS via the transsell Template to one of the following: INVALID, RECEIVED, STUDY, ACCEPTED, DECLINED, COUNTEROFFER, or REFUSED. If INVALID, DECLINED, or REFUSED are set, the transmission reservation request is terminated.

c. If the Seller determines that another reservation has higher priority and must displace this request, he sets the STATUS to SUPERSEDED and the negotiations are terminated.

d. However, if desired and permitted by the tariff, the Seller may set the STATUS of a request in any of these previous states (including COUNTEROFFER and ACCEPTED) to COUNTEROFFER with an OFFER_PRICE which could avoid the request being superseded, thus allowing the Customer the choice of being SUPERSEDED or accepting the proposed OFFER_PRICE.

002-4.4.7	Audit Template examples

The following examples are included to show the general type of audit report responses that could be expected to be returned by implementations of the audit reporting Templates as documented above.

002-4.4.7.1	Offerings

The following is an example of a hypothetical audit query for daily non-firm offerings to the "DDD" point of delivery for Monday August 17, 1998 (line breaks and indentations added to improve readability):

REQUEST_STATUS=200 (

ERROR_MESSAGE (

TIME_STAMP=19980821091601ES (

VERSION=1.4 (

TEMPLATE=transofferingaudit (

OUTPUT_FORMAT=DATA (

PRIMARY_PROVIDER_CODE=WXYZ (

PRIMARY_PROVIDER_DUNS=78912345 (

RETURN_TZ=ES (

DATA_ROWS=14 (

COLUMN_HEADERS=RECORD_TYPE,TIME_OF_LAST_UPDATE,MODIFYING_COMPANY_CODE,MODIFYIN G_NAME, TIME_OF_LAST_UPDATE,SELLER_CODE,SELLER_DUNS,PATH_NAME,POINT_OF_RECEIPT,POINT_OF_DEL IVERY, INTERFACE_TYPE,OFFER_START_TIME,OFFER_STOP_TIME,START_TIME,STOP_TIME,CAPACITY,SERVIC E_INCREMENT, TS_CLASS,TS_TYPE,TS_PERIOD,TS_WINDOW,TS_SUBCLASS,ANC_SVC_REQ,SALE_REF,POSTING_REF,CEI LING_PRICE, OFFER_PRICE,PRICE_UNITS,SERVICE_DESCRIPTION,NERC_CURTAILMENT_PRIORITY,OTHER_CURTAIL MENT_PRIORITY, SELLER_NAME,SELLER_PHONE,SELLER_FAX,SELLER_EMAIL,SELLER_COMMENTS (

U,19980815131756ES,WXYZ,Jane Doe,19980815131756ES, WXYZ,78912345,X/WXYZ/AAA-DDD//,AAA,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,800, DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48732,102.00,85.00,$/MW-Day,,3,, Jane Doe,123-456-7813,123-456-7801, doej@wxyz.com (

U,19980815124022ES,WXYZ, Jane Doe,19980815124022ES, WXYZ,78912345,X/WXYZ/AAA-DDD//,AAA,DDD,E, 1 9980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,850, DAILY,NON-FIRM,POINT_TO_ POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,, 48732,102.00,85.00,$/MW-Day,,3,, Jane Doe,123-456-7813,123-456-780 1,doej@wxyz.com, (

U,19980814120018ES,WXYZ, Joe Smith,19980814120018ES,WXYZ,78912345,X/WXYZ/AAA-DDD//,AAA,DDD,E,1 9980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,850, DAILY,NON-FIRM,POINT_TO_ POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48732,102.00,90.00,$/MW-Day,,3,,Joe Smith,123-456-7893,123-456-7801 ,smithj@wxyz.com (

I,19980813171204ES,WXYZ, Supervisor,19980813171204ES, WXYZ,78912345,X/WXYZ/AAA-DDD//,AAA,DDD,E, 19980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,850, DAILY,NON-FIRM,POINT_TO _POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48732,102.00,95.00,$/MW-Day,,3,, Supervisor,123-456-7890,123-456-78 01 (

U,19980815124022ES,WXYZ, Jane Doe,19980815124022ES, WXYZ,78912345,X/WXYZ/BBB-DDD//,BBB,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,1200, DAILY,NON-FIRM,POINT_TO_ POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48783,102.00,85.00,$/MW-Day,,3,,Jane Doe,123-456-7813,123-456-7801, doej@wxyz.com (

U,19980814120022ES,WXYZ,Joe Smith,19980814120022ES,WXYZ,78912345,X/WXYZ/BBB-DDD//,BBB,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,1200,DAILY,NON-FIRM,POINT_TO_ POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48783,102.00,90.00,$/MW-Day,,3,,Joe Smith,123-456-7893,123-456-7801 ,smithj@wxyz.com (

I,19980813171210ES,WXYZ,Supervisor,19980813171210ES,WXYZ,78912345,X/WXYZ/BBB-DDD//,BBB,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,1200,DAILY,NON-FIRM,POINT_TO_ POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48783,102.00,95.00,$/MW-Day,,3,,Supervisor,123-456-7890,123-456-780 1, (

U,19980816101000ES,WXYZ,Supervisor,19980816101000ES,WXYZ,78912345,X/WXYZ/CCC-DDD//,CCC,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,85,DAILY,NON-FIRM,POINT_TO_PO INT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48820,102.00,102.00,$/MW-Day,,3,,Supervisor,123-456-7810,123-456-7801, 5U,19980814143807ES,WXYZ,Supervisor,19980814143807ES,WXYZ,78912345,X/WXYZ/CCC-DDD//,CCC,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,90,DAILY,NON-FIRM,POINT_TO_PO INT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48820,102.00,102.00,$/MW-Day,,3,,Supervisor,123-456-7890,123-456-7801, 5U,19980814120023ES,WXYZ,Joe Smith,19980814120023ES,WXYZ,78912345,X/WXYZ/CCC-DDD//,CCC,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,110,DAILY,NON-FIRM,POINT_TO_P OINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48820,102.00,90.00,$/MW-Day,,3,,Joe Smith,123-456-7893,123-456-7801,s mithj@wxyz.com (

I,19980813171214ES,WXYZ,Supervisor,19980813171214ES,WXYZ,78912345,X/WXYZ/CCC-DDD//,CCC,DDD,E,19 980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,110,DAILY,NON-FIRM,POINT_TO_P OINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48820,102.00,95.00,$/MW-Day,,3,,Supervisor,123-456-7890,123-456-7801, (

U,19980815124023ES,WXYZ,Jane Doe,19980815124023ES,WXYZ,78912345,X/WXYZ/WXYZ-DDD//,WXYZ,DDD, E,19980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,340,DAILY,NON-FIRM,POINT_T O_POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48855,102.00,85.00,$/MW-Day,,3,,Jane Doe,123-456-7813,123-456-78 01,doej@wxyz.com (

U,19980814120023ES,WXYZ,Joe Smith,19980814120023ES,WXYZ,78912345,X/WXYZ/WXYZ-DDD//,WXYZ,DDD, E,19980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,340,DAILY,NON-FIRM,POINT_T O_POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48855,102.00,90.00,$/MW-Day,,3,,Joe Smith,123-456-7893,123-456-7 801,smithj@wxyz.com (

I,19980813171222ES,WXYZ,Supervisor,19980813171222ES,WXYZ,78912345,X/WXYZ/WXYZ-DDD//,WXYZ,DDD, E,19980814000000ES,19980817000000ES,19980817000000ES,19980818000000ES,340, DAILY,NON-FIRM,POINT_T O_POINT,FULL_PERIOD,FIXED,,SC:M;RF:M,,48855,102.00,95.00,$/MW-Day,,3,,Supervisor,123-456-7890,123-456-7 801, (

From this audit report, the daily non-firm offerings on the four paths to "DDD" (AAA-DDD, BBB-DDD, CCC-DDD, and WXYZ-DDD) were all originally posted by WXYZ's "Supervisor" at approximately 17:12 on 8/13 at a price of $95.00 /MW-Day discounted from a ceiling price of $102.00.

At approximately 12:00 on 8/14, Joe Smith changed the offer price to $90.00 on all four paths.

At 14:14 on 8/14, "Supervisor" adjusted the capacity available on path X/WXYZ/CCC-DDD// to 90 MW (POSTING_REF = 48820) and set the offer price up to match the tariff ceiling rate (presumably due to the path now being constrained and released from the requirement to have discounted service offered at the same rate as all other unconstrained paths to DDD). Capacity on this path was last updated to a value of 85 MW at 10:10 on 8/16, which is the current information posted on OASIS for this path at the time of the query.

Jane Doe adjusted the price on the three presumably unconstrained paths to DDD at 12:40 on 8/15 to $85.00, which may have been in response to a negotiation for service on one of these paths. No further updates have occurred to the offerings on paths BBB-DDD and WXYZ-DDD since that time.

Finally, the capacity available on path X/WXYZ/AAA-DDD// was updated by Jane Doe from 850 to 800 MW at 13:17 on 8/15, which may have corresponded with final confirmation of a reservation at a negotiated discount by the customer that initiated the price change from $90.00 to $85.00.

002-4.4.7.2	Reservations

The following is an example of a hypothetical audit query for a specific transmission service reservation (line breaks and indentations added to improve readability):

REQUEST_STATUS=200(

ERROR_MESSAGE=(

TIME_STAMP=19980821092048ES(

VERSION=1.4(

TEMPLATE=transstatusaudit(

OUTPUT_FORMAT=DATA(

PRIMARY_PROVIDER_CODE=WXYZ(

PRIMARY_PROVIDER_DUNS=78912345(

RETURN_TZ=ES(

DATA_ROWS=9(

COLUMN_HEADERS=RECORD_TYPE,TIME_OF_UPDATE,MODIFYING_COMPANY_CODE,MODIFYING_NAME, CONTINUATION_FLAG,ASSIGNMENT_REF,SELLER_CODE,SELLER_DUNS,CUSTOMER_CODE, CUSTOMER_DUNS,AFFILIATE_FLAG,PATH_NAME,POINT_OF_RECEIPT,POINT_OF_DELIVERY, SOURCE,SINK,CAPACITY,SERVICE_INCREMENT,TS_CLASS,TS_TYPE,TS_PERIOD,TS_WINDOW, TS_SUBCLASS,NERC_CURTAILMENT_PRIORITY,OTHER_CURTAILMENT_PRIORITY,START_TIME, STOP_TIME,CEILING_PRICE,OFFER_PRICE,BID_PRICE,PRICE_UNITS,PRECONFIRMED,ANC_SVC_LINK,ANC _SVC_REQ,POSTING_REF,SALE_REF,REQUEST_REF,DEAL_REF,NEGOTIATED_PRICE_FLAG, STATUS,STATUS_NOTIFICATION,STATUS_COMMENTS,TIME_QUEUED,RESPONSE_TIME_LIMIT, TIME_OF_LAST_UPDATE,PRIMARY_PROVIDER_COMMENTS,SELLER_COMMENTS, CUSTOMER_COMMENTS,SELLER_NAME,SELLER_PHONE,SELLER_FAX,SELLER_EMAIL, CUSTOMER_NAME,CUSTOMER_PHONE,CUSTOMER_FAX,CUSTOMER_EMAIL,REASSIGNED_REF, REASSIGNED_CAPACITY, REASSIGNED_START_TIME,REASSIGNED_STOP_TIME(

U,19980815131629ES,DEFPM,Alan Trader,N,104392,WXYZ,78912345,DEFPM,912876543,N,X/WXYZ/AAA-DDD//,A AA,DDD,AAA,ZZZ,50,DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,3,,19980817000000ES,199808 18000000ES,102.00,85.00,85.00,$/MW-Day,N,,SC:M;RF:M,,,,,,CONFIRMED,,,19980815121510ES,19980815144100ES, 19980815131629ES,,,,Jane Doe,123-456-7813,123-456-7801,doej@wxyz.com,Alan Trader,312-678-9104,312-678-9100,a .trader@defmarketing.com,,,, (

U,,,,Y,,,,,,,,,,,,75,,,,,,,,,19980818000000ES,19980819000000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

U,,,,Y,,,,,,,,,,,,100,,,,,,,,,19980819000000ES,19980820000000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

U,19980815125042ES,WXYZ,Jane Doe,N,104392,WXYZ,78912345,DEFPM,912876543,N,X/WXYZ/AAA-DDD//,AAA ,DDD,AAA,ZZZ,50,DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,3,,19980817000000ES,19980818 000000ES,102.00,85.00,82.00,$/MW-Day,N,,SC:M;RF:M,,,,,,COUNTEROFFER,,,19980815121510ES,19980815144100 ES,19980815125042ES,,,,Jane Doe,123-456-7813,123-456-7801,doej@wxyz.com,Alan Trader,312-678-9104,312-678-910 0,a.trader@defmarketing.com,,,, (

U,19980815124811ES,DEFPM,Alan Trader,N,104392,WXYZ,78912345,DEFPM,912876543,N,X/WXYZ/AAA-DDD//,A AA,DDD,AAA,ZZZ,50,DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,3,,19980817000000ES,199808 18000000ES,102.00,85.00,82.00,$/MW-Day,N,,SC:M;RF:M,,,,,,REBID,,,19980815121510ES,19980815144100ES,19980 815124811ES,,,,Jane Doe,123-456-7813,123-456-7801,doej@wxyz.com,Alan Trader,312-678-9104,312-678-9100,a.trader @defmarketing.com(

U,19980815124100ES,WXYZ,Jane Doe,N,104392,WXYZ,78912345,DEFPM,912876543,N,X/WXYZ/AAA-DDD//,AAA ,DDD,AAA,ZZZ,50,DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,3,,19980817000000ES,19980818 000000ES,102.00,85.00,80.00,$/MW-Day,N,,SC:M;RF:M,,,,,,COUNTEROFFER,,,19980815121510ES,19980815144100 ES,19980815124100ES,,,,Jane Doe,123-456-7813,123-456-7801,doej@wxyz.com,Alan Trader,312-678-9104,312-678-910 0,a.trader@defmarketing.com(

I,19980815121510ES,DEFPM,Alan Trader,N,104392,WXYZ,78912345,DEFPM,912876543,N,X/WXYZ/AAA-DDD//,A AA,DDD,AAA,ZZZ,50,DAILY,NON-FIRM,POINT_TO_POINT,FULL_PERIOD,FIXED,,3,,19980817000000ES,199808 18000000ES,102.00,90.00,80.00,$/MW-Day,N,,SC:M;RF:M,,,,,,QUEUED,,,19980815121510ES,,19980815121510ES,,,,Company Default,123-456-7800,123-456-7801,,Alan Trader,312-678-9104,312-678-9100,a.trader@defmarketing.com(

I,,,,Y,,,,,,,,,,,,75,,,,,,,,,19980818000000ES,19980819000000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

I,,,,Y,,,,,,,,,,,,100,,,,,,,,,19980819000000ES,19980820000000ES,,,,,,,,,,,,,,,,,,,,,,,,,,,,, (

First, this example shows the handling of continuation records which conveyed a time varying demand of 50 MW on 8/17, 75 MW on 8/18, and 100 MW on 8/19. This demand profile was initially entered with the original reservation request (transrequest Template) at 12:15 on 8/15 by Alan Trader. Since the Data Elements associated with the profile were never modified, the intervening audit response records do not repeat the data from these continuation records.

As part of the original reservation, Alan Trader attempted to negotiate a price for service of $80.00 /MW-Day. Jane Doe responded to this request with a counter offer at the rate of $85.00 /MW-Day at 12:41 on 8/15. Since the status of COUNTEROFFER constitutes acceptance of all terms of the reservation except price (i.e., transmission capability has been evaluated and is available), the RESPONSE_TIME_LIMIT Data Element has been updated to reflect the time by which the customer must confirm service (assuming the establishment of customer confirmation time limits is approved by FERC).

At 12:48, Alan Trader attempted to negotiate further for a rate of $82.00 /MWDay and the reservation status was set to REBID. Jane Doe responded at 12:50 with a second counter offer restating a rate of $85.00, which Alan Trader finally agreed to at 13:16 on 8/15. The current posted information on OASIS shows this final CONFIRMED reservation.

002-4.5	GENERAL POSTINGS

002-4.5.1	INFO.HTM

When a regulatory order requires informational postings on OASIS and there is no OASIS S&CP template to support the postings or it is deemed inappropriate to use a template, or the location of the posting has not been  required to be elsewhere, there shall be a reference in INFO.HTM to the required information, including, but not limited to, references to the following:

  - A common source of interconnection wide curtailment and interruption information, such as the NERC Transmission Loading Relief (TLR) web site.

  - Information related to the Transmission Provider's methodology for computing and application of Capacity Benefit Margin (CBM) and Transmission Reliability Margin (TRM). If the Transmission Provider does not use CBM or TRM in their assessment of Available Transmission Capability (ATC), that information shall also be in INFO.HTM.

  - The location of the list of system studies conducted.

  - Information on requesting the text file of the tariffs and service agreements.

For the purposes of this section, any link to required informational postings that can be accessed from INFO.HTM would be considered to have met the OASIS posting requirements, provided that the linked information meets all other OASIS accessibility requirements.

002-4.5.2	STANDARDS OF CONDUCT

The Transmission Provider shall establish a link entitled “Standards of Conduct,” located on the OASIS home page at the Transmission Provider’s registered URL address.

The following types of information, as found in Standards of Conduct for Transmission Providers, Order 2004, 105 FERC ¶61,248 (2003);order on reh’g, Order 2004-A, 107 FERC ¶61,032; order on reh’g, Order 2004-B, 108 FERC ¶61,118 (2004); order on reh’g, Order 2004-C, 109 FERC ¶61,325; order on reh’g, Order 2004-D, 110 FERC ¶61,320, and 18 CFR §358 should be accessible from the Standards of Conduct link.

Emergency Circumstances Deviations (§358.4(a)(2))

Marketing and Energy Affiliate List (§358.4(b)(1))

Shared Facilities (§358.4(b)(2))

Organizational Charts and Job Descriptions (§358.4(b)(3)(i))

Common Employees (§358.4(b)(3)(iii))

Potential Merger Partners (§358.4(b)(3)(v))

Transfers (§358.4(c))

Information Disclosure (§358.5(b) (3))

Voluntary Consent to Share Non-Affiliated Customer Information (§358.5(b)(4))

Discretionary Actions under Tariff  (§358.5(c)(4))

Discounts (§358.5(d))

Chief Compliance Officer (§358.4(e)(6))

Written Procedures for Implementation (§358.4 (e)(3))

These items shall appear in the order specified above and before any other items which may be required as per specific FERC direction or local business practice.  Posting of the cites noted in the parentheses is optional.  Access to some of the information found under the Standards of Conduct link above may require the user to register with the individual OASIS sites according to WEQ-002-3.1

002-5	PERFORMANCE REQUIREMENTS

A critical aspect of any system is its performance. Performance encompasses many issues, such as security, sizing, response to user requests, availability, backup, and other parameters that are critical for the system to function as desired. The following sections cover the performance requirements for the OASIS Nodes .

002-5.1	SECURITY

Breaches of security include many inadvertent or possibly even planned actions. Therefore, several requirements shall be implemented by the TSIPs to avoid these problems:

a. Provider Update of TS Information: Only Providers, including Secondary Providers, shall be permitted to update their own TS Information.

b. Customer Input Only ASCII Text: TSIPs shall be permitted to require that inputs from Customers shall be filtered to permit only strict ASCII text (strip bit 8 from each byte).

c. Provider Updating Over Public Facilities: If public facilities are involved in the connection between a Provider and the OASIS Node, the Provider shall be able to update his TS Information only through the use of ASCII or through encrypted files.

d. User Registration and Login: All Users shall be required to register and login to a Provider's Account before accessing that Provider's TS Information.

e. User Passwords: All Users shall enter their personal password when they wish access to TS Information beyond the lowest Access Privilege.

f. Service Request Transactions: Whenever Service Request transactions are implemented entirely over OASIS Nodes, both an individual Customer password for the request, and an individual Provider password for the notification of acceptance shall be required.

g. Data Encryption: Sophisticated data encryption techniques and the "secure id" mechanisms being used on the public Internet shall be used to transfer sensitive data across the Internet and directly between OASIS Nodes.

h. Viruses: Since only data is being transmitted between the OASIS Nodes and the Users, viruses are unlikely to be passed between them. Therefore, TSIPs shall be responsible for ensuring that the OASIS Nodes are free from viruses, but need not screen data exchanges with Users for viruses.

i. Performance Log: TSIPs shall keep a log on User usage of OASIS resources.

j. Disconnection: TSIPs shall be allowed to disconnect any User who is degrading the performance of the OASIS Node through the excessive use of resources, beyond what is permitted in their Service Level Agreement.

k. Premature Access: The TSIP log shall also be used to ensure that Users who are affiliated with the Provider's company (or any other User) do not have access to TS information before it is publicly available.

l. Firewalls: TSIPs shall employ security measures such as firewalls to minimize the possibility that unauthorized users shall access or modify TS Information or reach into Provider or User systems. Interfaces through Public Data Networks or the Internet shall be permitted as long as these security requirements are met.

m. Certificates and Public Key Standards (optional): Use of alternative forms of login and authentication using certificates and public key standards is acceptable.

002-5.2	ACCESS PRIVILEGES

Users shall be assigned different Access Privileges based on external agreements between the User and the Provider. These Access Privileges are associated with individual Users rather than just a company, to ensure that only authorized Users within a company have the appropriate access.

The following Access Privileges shall be available as a minimum:

a. Access Privilege Read-Only: The User may only read publicly available TS Information.

b. Access Privilege for Transactions: The Customer is authorized to transact Service Requests.

c. Access Privilege Read/Write: A Secondary Provider shall have write access to his own Provider Account on an OASIS Node.

002-5.3	OASIS RESPONSE TIME REQUIREMENTS

002-5.3.1	TSIPs can only be responsible for the response capabilities of two portions of the Internet-based OASIS network:

- The adequacy of the TSIP's internet interconnection(s) for reasonable high-volume utilization

- The response capabilities of the OASIS Node functions to process interactions with Users

002-5.3.2	Measurement Criteria for Internet Connections

An OASIS node's Internet connection(s) should not exceed 60% sustained utilization. To determine the sustained utilization, TSIPs shall retain usage records and logs related to the Internet service.

002-5.3.3	Measurement Criteria for OASIS Node functions

It is required that OASIS query functions meet or exceed the response times listed below during the normal conduct of business.

| Template or GUI equivalent | Average Response not fewer than: | 90% of Responses not fewer than: |
| --- | --- | --- |
| transstatus | 100 rows/minute | 10 rows/minute |
| transoffering | 500 rows/minute | 100 rows/minute |

It should be recognized that during periods of minimal interactivity there might be heavier loading due to automated processes gathering larger volumes of data or due to OASIS node housekeeping services. The offloading of such discretionary demand should not be discouraged if it serves to make the OASIS more responsive during primary periods of customer activity.

To assess whether these performance capabilities are obtainable, an OASIS application shall collect and log pertinent statistics on an hourly basis about each invocation of the primary types of data queries on the Templates transstatus and transofferring. Statistics logged shall be the number of invocations per type of template, the service processing time to retrieve the information, format of the responses, and effective template data row count.

002-5.4	OASIS PROVIDER ACCOUNT AVAILABILITY

The following are the OASIS Provider Account availability requirements:

a. OASIS Provider Account Availability: The availability of each OASIS Provider account on an OASIS Node shall be at least 98.0% (downtime of about 7 days per year).

Availability is defined as:

% Availability = (1 - Cumulative Provider Account Downtime) * 100

Total Time

A Provider account shall be considered to be down, and downtime shall be accumulated, upon occurrence of any of the following:

1. One or more Users cannot link and log on to the Provider account. The downtime accumulated shall be calculated as:

Σ for affected Users of 1/n * (Login Time), which is the time used by each affected User to try to link and log on to the Provider account, and where "n" is the total number of Users actively registered for that Provider account.

2. One or more Users cannot access TS Information once they have logged on to a Provider account. The downtime accumulated shall be calculated as:

Σ for affected Users of 1/n * (Access Time), which is the time used by each affected User to try to access data, and where "n" is the total number of Users actively registered for that Provider.

3.  A five (5) minute penalty shall be added to the cumulative downtime for every time a User loses their connection to a Provider's account due to an OASIS Node momentary failure or problem.

002-5.5	BACKUP AND RECOVERY

The following backup and recovery requirements shall be met:

a. Normal Backup of TS Information: Backup of TS Information and equipment shall be provided within the OASIS Nodes so that no data or transaction logs are lost or become inaccessible by Users due to any single point of failure. Backed up data shall be no older than 30 seconds. Single points of failure include the loss of one:

- Disk drive or other storage device

- Processor

- Inter-processor communications (e.g. LAN)

- Inter-OASIS communications

- Software application

- Database

- Communication ports for access by Users

- Any other single item which affects the access of TS Information by Users

b. Spurious Failure Recovery Time: After a spurious failure situation, all affected Users shall regain access to all TS Information within 30 minutes. A spurious failure is a temporary loss of services which can be overcome by rebooting a system or restarting a program. Permanent loss of any physical component is considered a catastrophic failure.

c. Long-Term Backup: Permanent loss of critical data due to a catastrophic failure shall be minimized through off-line storage on a daily basis and through off-site data storage on a periodic basis.

d. Catastrophic Failure Recovery: Recovery from a catastrophic failure or loss of an OASIS Node may be provided through the use of alternate OASIS Nodes which meet the same availability and response time requirements. TSIPs may set up prior agreements with other TSIPs as to which Nodes will act as backups to which other Nodes, and what procedure will be used to undertake the recovery. Recovery from a catastrophic failure shall be designed to be achieved within 24 hours.

002-5.6	TIME SYNCHRONIZATION

The following are the time requirements:

a. Time Synchronization: Time shall be synchronized on OASIS Nodes such that all time stamps will be accurate to within "0.5 second of official time. This synchronization may be handled over the network using NTP, or may be synchronized locally using time standard signals (e.g. WWVB, GPS equipment).

b. Network Time Protocol (NTP): OASIS Nodes shall support the Internet tool for time synchronization, Network Time Protocol (NTP), which is described in RFC-1305, version 3, so that Users shall be able to request the display and the downloading of current time on an OASIS Node for purposes of user applications which might be sensitive to OASIS time.

002-5.7	TS INFORMATION TIMING REQUIREMENTS

The TS Information timing requirements are as follows, except they are waived during emergencies.

a. TS Information Availability: The most recent Provider TS information shall be available on the OASIS Node within 5 minutes of its required posting time at least 98% of the time. The remaining 2% of the time the TS Information shall be available within 10 minutes of its scheduled posting time.

b. Notification of Posted or Changed TS Information: Notification of TS Information posted or changed by a Provider shall be made available within 60 seconds to the log. S&CP Version

c. Acknowledgment by the TSIP: Acknowledgment by the TSIP of the receipt of User Purchase requests shall occur within 1 minute. The actual negotiations and agreements on Purchase requests do not have time constraints.

002-5.8	TS INFORMATION ACCURACY

The following requirements relate to the accuracy of the TS information:

a. TS Information Reasonability: TS information posted and updated by the Provider shall be validated for reasonability and consistency through the use of limit checks and other validation methods.

b. TS Information Accuracy: Although precise measures of accuracy are difficult to establish, Providers shall use their best efforts to provide accurate information.

002-5.9	PERFORMANCE AUDITING

The following are the performance auditing requirements:

a. User Help Desk Support: TSIPs shall provide a "Help Desk" that is available at least during normal business hours (local time zone) and normal work days.

b. Monitoring Performance Parameters: TSIPs shall use their best efforts to monitor performance parameters. Any User shall be able to read or download these performance statistics.

002-5.10	MIGRATION REQUIREMENTS

Whenever a new version of the S&CP is to be implemented, a migration plan will be developed for cutting over to the new version.

# Footnotes

According to WEQ-002-4.3.10.4 a template is required for this item.

According to WEQ-002-4.3.10.6 a template is required for this item.

According to WEQ-002-4.3.10.5 a template is required for this item.

According to WEQ-002-4.3.2.1 a template is required for this item.