## Slide 1: Loop Flow and Congestion Management in the Western Interconnection
Eric Baran
Senior Program Manager – Electric System Reliability
NAESB Update
October 15, 2025

## Slide 2: Who is WIRAB?
Statutory Authority: Established in 2005, as an independent body with statutory authority under Section 215(j) of the Federal Power Act to Advise FERC, NERC, and WECC on reliability matters in the Western Interconnection.
Membership: All state and provinces with load served in the Western Interconnection
Funding: Assessments approved by FERC to load serving entities under Section 215 of the Federal Power Act.

## Slide 3: Western RC Transition (2019)
Beginning of 2019
End of 2019
WIRAB Report

## Slide 4: Western Interconnection Context
Large interconnected system
13 states, 2 Canadian Provinces + Baja
“WECC Donut”
  Major load concentration in CA
  Major generation sources:
    PNW Hydro
    RM Coal & Wind
    DSW Nuclear & Solar
  Empty space in the middle
PNW
CA
RM
DSW
Notes: .

## Slide 5: What is Loop Flow?
Definition: Unintended, unscheduled power flows that occur because electricity follows the path of least resistance (or impedance), not the commercial “contract path.”
Result: Actual MW flows spread across multiple parallel lines and cross Balancing Authorities and state boundaries, affecting facilities far from the scheduled transaction.

## Slide 6: The Physics of Loop Flow (Unscheduled Flow)
Core Idea:
  Power follows the easiest electrical path
Kirchhoff's Current Law (KCL)
  At any junction (busbar or node) in the electrical grid, the total current flowing in must equal the total current flowing out.
Impedance and Ohm's Law
  The path electricity takes is determined by the impedance (the total opposition to the flow of alternating current) of all available lines.
The Interconnected Nature of the Grid
  Power generated in one location instantly affects the flow patterns across the entire system.
Notes: The Physics of Loop Flow (Unscheduled Flow)
Loop flow is the phenomenon where electricity physically travels through unintended paths in the electrical grid, ignoring the direct contractual paths scheduled by operators. This behavior is governed by fundamental physical laws:
1. Kirchhoff's Current Law (KCL)
At any junction (busbar or node) in the electrical grid, the total current flowing in must equal the total current flowing out.
Implication: When a transmission line is overloaded or congested, the excess current cannot simply disappear; it must seek alternative routes through the interconnected grid to satisfy this law.
2. Impedance and Ohm's Law
The path electricity takes is determined by the impedance (the total opposition to the flow of alternating current) of all available lines.
The Rule: Electricity naturally disperses itself across all available parallel paths in inverse proportion to their impedance. Lower impedance paths carry more current.
Analogy: Think of water flowing down a river that splits into multiple channels. The widest, deepest (lowest resistance/impedance) channel carries the most water, but some water still flows down all other available channels.
Implication: If a direct transmission line has high impedance or is full, nearby lines with low impedance—even if they belong to a different utility or are in a "loop"—will automatically carry a portion of the flow.
3. The Interconnected Nature of the Grid
The Western Interconnection (WECC) is one vast, synchronous AC system. All interconnected generators and loads operate in unison.
The Result: Power generated in one location instantly affects the flow patterns across the entire system. Operators cannot physically force electricity to stay within specific administrative boundaries or contractual lines; they can only manage the overall system balance and line capacities.
In summary, loop flow is a direct consequence of electricity obeying physics (following the path of least resistance) rather than human-made contract paths or market boundaries.
KCL = “What enters a junction must leave” (plumbing: inflow = outflow at a tee).
KVL = “Head/pressure changes around a closed pipe loop sum to zero”; a pump adds head just like a PST adds angle.
Two parallel pipes (lines): the wide/smooth (low friction/low 𝑋) pipe naturally carries more flow. If you add a small pump/PST in one pipe, you can push more water/MW into it (or pull it off with opposite setting).
That’s why electrons ignore the contract path: the grid must obey conservation at nodes (KCL) and angle consistency in loops (KVL), so it self-distributes flows across all available paths.

## Slide 7: Scheduled vs. Unscheduled (Loop) Flow
Schedule from PNW to CA (i.e. Sell Energy from PNW to CA)
PNW
CA
RM
DSW
Scheduled
Flow
Unscheduled Flow
Unscheduled Flow
Unscheduled Flow
Contract Path

## Slide 8: Scheduled vs. Unscheduled (Loop) Flow
Schedule from PNW to CA but through RM and DSW because transmission was available and/or cheaper
PNW
CA
RM
DSW
Scheduled Flow
Unscheduled
Flow
Scheduled Flow
Scheduled Flow
Contract Path

## Slide 9: Unscheduled Flow Creates Congestion
Congestion on Path from PNW to CA due to Unscheduled Flows
PNW
CA
RM
DSW
Scheduled Flow
Unscheduled
Flow
Scheduled Flow
Scheduled Flow
Congested Path

## Slide 10: Western Interconnection Unscheduled Flow Mitigation Plan (WIUFMP)
UFMP is a FERC Approved congestion management plan for select Qualified Paths in the Western Interconnection
Accomplished by:
  Use of Qualified Controllable Device(s) (QCD)
    Phase Shifting Transformers
  Curtailment of transmission schedules
Applies to all organizations that generate power, serve load, and/or buy, sell, or transport energy in the West
Requires after-the-fact accounting performed by the Plan Administrator (SPP)

## Slide 11: UFMP Qualified Paths
Qualified Path (QP):
  A transmission element, or group of transmission elements, where actual flows have exceeded 97% of the applicable Facility Rating for at least 100 hours in past 36 months
  Five Qualified Paths
PNW
CA
RM
DSW

## Slide 12: Phase Shifting Transformers
Control power flow over parallel lines by adjusting phase angle at one end of line
  For example: Adjusting Phase angles in RM Region can divert power away from Path 66 (COI)
= Approx. location of Qualified Phase Shifting Transformers
DSW
PNW
CA
RM

## Slide 13: Phase Shifters Relieve Unscheduled Flow
Congestion on Path from PNW to CA due to Unscheduled Flows
PNW
CA
RM
DSW
Scheduled Flow
Unscheduled
Flow
Scheduled Flow
Scheduled Flow
Congested Path
= Phase Shifter

## Slide 14: Phase Shifters Relieve Unscheduled Flow
Congestion relieved on Path from PNW to CA due by coordinating the operation of phase shifters
PNW
CA
RM
DSW
Scheduled Flow
Unscheduled
Flow
Scheduled Flow
Scheduled Flow
Congestion Relieved
= Phase Shifter
Phase Shifter Owners coordinate the operation of Phase Shifters to alleviate congestion on Congested Path
Did not have to redispatch generation!

## Slide 15: Schedule Cuts Relieve Unscheduled Flow and Congestion
Congestion relieved on Path from PNW to CA due to cutting schedules which redispatches generation
PNW
CA
RM
DSW
Scheduled Flow
Unscheduled
Flow
Scheduled Flow
Scheduled Flow
Congestion Relieved
Sender Reduces Export Schedule
Decrease Generation
Receiver Reduces Import Schedule
Increase Generation
Costs Generators & Customers Money

## Slide 16: Process and Limitations of the WIUFMP
Process:
Advise the Reliability Coordinator (RC)
On-path actions by the path owner/operator
Coordinated operation of Qualified Controllable Devices (QCDs), i.e. phase-shifting transformers (PSTs)
If needed, curtail contributing schedules (hourly events)
Limitations:
Narrow Scope (only “Qualified Paths”)
High Trigger threshold
Tag-centric Relief
Limited “alternative actions”
Phase shifters (QCDs) dependent
Seams & Market Mismatch
Transparency/modeling
Plan administrator (SPP) allocates costs
Notes: Scope (Path-limited)
Applies to a few Qualified Paths, not all SOLs/IROLs
Triggers & Timing
Relief typically after ≥95% loading; hourly cadence; :25 request deadline
Tag-centric Relief
Curtailment by tag “buckets” (priority/TDF) — blunt vs. impact-based
Limited capture of Dynamic Transfers and native/network load
Device Dependence
Relief hinges on a small fleet of PSTs (outages, wear, reversal effects)
Alternative Actions
Hard to credit redispatch/alternate transactions in-hour; manual verification
Seams & Market Mismatch
Multiple RC/BA/market processes; path-based ATC ≠ physical flows
Misaligned with DA/RT market cadence and interface pricing
Transparency/Modeling
No single, shared impact view; path tags mask true contributors

## Slide 17: Market Seams
Notes: if they heard in real time for markets expand in the West seems to introduce new pressure points path based practices don't always reflect actual power flows syndicated through this discussion of loop flow pricing and scheduling across interfaces can be tricky and coordination kits harder when multiple tariffs balcony balancing authorities and market operators are in play the result is more places where unscheduled flow can matter and more complex city can add more complexity in who acts and then who also pays

## Slide 18: Challenges from Loop Flow at New Market Seams
More unscheduled (loop) flows between markets → congestion, reliability stress, and cost shifts
Legacy UFMP limits insufficient for today’s seams
Path-based practices ≠ physical flows
Adopt a single, West-wide, RC-led congestion process using the Enhanced Curtailment Calculator
Notes: The physics won’t change — loop flow appears where markets split. Today’s tools (WIUFMP; path-based ATC) are too narrow or coarse for multi-market day-ahead/real-time operations, and seams complicate pricing, coordination, and shared programs.
Why an ECC-Centered Approach Addresses This
Impact-based relief (all contributors: e-Tags, DTs, GTL) with pro-rata obligations
Intra-hour recalcs; covers SOLs/IROLs; keeps UFMP/PST but expands scope
RC-led, single view with shared model & audit trail; aligns with market-to-market / market-to-non-market coordination
Clear obligations → fewer disputes; more transfer capability unlocked

## Slide 19: Wrap up
Loop flow is inherent in interconnected AC networks (especially pronounced in the Western Interconnection)
Today the West uses WIUFMP to provide a structured, region-wide response for major Paths
With increased market seams, coordination may be more difficult and new risks will develop, therefore congestion management in the West should be improved.

## Slide 20: Thank You!
Eric Baran
ebaran@westernenergyboard.org

## Slide 21: WIRAB Official Membership
21
Alberta
Arizona
British Columbia
California
Colorado
Betsy Li Alward, Director, Generation, Transmission and Markets Policy, Energy Policy, Alberta Energy
Lea Marquez Peterson, Commissioner, Arizona Corporation Commission*
Chris Gilmore, Executive Director, Electricity Policy Branch, Ministry of Energy, Mines and Low Carbon Innovation
Siva Gunda, Vice Chair, California Energy Commission**
James Lester, Senior Policy Lead on Transmission, Climate and Energy, Colorado Energy Office
Idaho
Cally Younger, Administrator, Idaho Governor’s Office of Energy and Mineral Resources
Mexico
Vacant
Montana
Sonja Nowakowski, Director of the Montana Department of Environmental Qulity
Nebraska
Tim Texel, Executive Director, Nebraska Power Review Board
Nevada
Dwayne McClinton, Director, Nevada Governor's Office of Energy
New Mexico
Vacant
Oregon
Janine Benner, Director, Oregon Department of Energy
South Dakota
Greg Rislov, Commission Advisor, South Dakota Public Utility Commission
Texas
Vacant
Utah
Emy Lesofski, Director, Utah Governor's Office of Energy Development
Washington
Elizabeth Osborne, Senior Energy Policy Analyst, Washington State Energy Office
Wyoming
Chris Petrie, Commissioner, Wyoming Public Service Commission
*WIRAB Chair; **WIRAB Vice-Chair

## Slide 22: UFMP Administrator – Southwest Power Pool
Qualified Controllable Device owners and Transmission Operators of Qualified Paths select Plan Administrator
Southwest Power Pool’s responsibilities:
  Collects cost information from Qualified Controllable Device (QCD) Owners
  Confirms cost information
  Determines QCD cost recovery rate
  Allocates QCD Rate to Applicable Entities (i.e. proportionate percentage to Load, Generation, Imports, Exports)
  Tacks on administrative costs
  Administers invoices
  Develops Administrative Report (2016 Report from WECC)
  Resolves Disputes regarding UFMP

## Slide 23: UFMP, Reliability Coordination and the UFMP Administrator
Transmission Operators (TOPs):
  Monitor Qualified Paths
  Advise RC of potential situations
  Attempt to alleviate the issue on their own
  Requests coordinated operation of QCD
  Requests curtailment of schedules
Reliability Coordinator(s):
  Monitors situations
  Reviews requests for curtailment of schedules for reliability implications
  Coordinates with neighboring RCs
  Either approves or denies the request
UFMP Administrator:
  Collects and allocates costs associated with UFMP
  Administers invoices and collects payment

## Slide 24: Annual COPS Hours and Cost
Chart: Annual COPS Hours and Cost
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024
COPS Hours | 777 | 324 | 387 | 690 | 1380 | 958
 | 0.088699 | 0.036986 | 0.044178 | 0.078767 | 0.15753 | 0.10936
QCD Costs | 1761573.87 | 1119697.43 | 1328421.22 | 1719597.11 | 2715259.57 | 2105301.21