## Slide 1: TSR Tracing Tool

## Slide 2: Business Case
Failed eTags due to capacity issues on the TSR
REDIRECT capacity issues
Researching billing issues
Problems where RESALE transactions may have been transitioned to an inappropriate state

## Slide 3: Standards
002-4.3.6.2 Status of Transmission Customer Purchase Request/Reservation (transstatus)
  This standard associates the RELATED_REF and the REASSIGNED_REF data elements with the transstatus template.
002-4.3.4.3 Transmission Reservation Reduction (reduction)
  This standard associates REASSIGNED_REF with the reduction template. It also mentions the type of reductions are defined in WEQ-003 under REDUCTION_TYPE.
003-0 Contains the valid types of reductions.
  CONDITIONAL_EVENT, CONDITIONAL_HOURS, CONSOLIDATION, RECALL, REDIRECT, RESALE, TRANSFER, RELINQUISH

## Slide 4: Design Concepts
View the history (looking backwards) of a REDIRECT/RESALE TSR all the way back to the ORIGINAL
View the usage (looking forwards) of any TSR

## Slide 5: Potential Issues
The data to accomplish this is already in OASIS
  A combination of templates can link the appropriate TSRs together
The issue is not where to get the data, it is the volume
  Even if you could completely build this tool, it might deliver so much data that it would be impractical anyway
  It still seems reasonable that any query would have to be bounded by date and time anyway
Looking backwards would be complicated by RESALEs, Consolidations, and reassignments/transfers. These types of transactions can have more than one parent.
Looking forwards may be challenging due to the volume of REDIRECTs, RESALEs, and reassignments/transfers.

## Slide 6: Path Forward
Any solution to address this problem is highly dependent on a specialized graphical user interface
  This seems inappropriate to put in NAESB standards
  Might fit better in a vendor software enhancement
There may be value in making some template changes
  Reduction Template
    This template could be enhanced to deliver more granular data
    Can the IMPACTING_REF provide a link to other data elements
      POR/POD, SOURCE/SINK, or even a customer code